## Slide 1
Weapons and Ammunition Management in UN Peace Operations
Lesson 6 Net Explosive Quantity Calculation
Notes: Key Reference Documents for lesson:
UN Manual on Ammunition Management
UN Weapons and Ammunition Management Policy (WAM)
International Ammunition Technical Guidelines (IATG)
All photographs in this lesson are © United Nations unless otherwise stated.

## Slide 2: Objective
Apply NEQ calculations to determine the explosive quantity in an ammunition stack, store or means of transport in preparation for any subsequent Explosive Risk Assessment
Notes: Main idea/objective for slide:
Phase 1. Introduction - Introduce the objectives of the lesson.
(Enabling Objective: 2.2.2 Apply NEQ calculations to determine the explosive quantity in an ammunition stack, store or means of transport in preparation for any subsequent Explosive Risk Assessment)
What the instructor should cover (in addition to slide content)
By the end of this training session the participant will understand and be able to apply NEQ calculations to determine the explosive quantity in an ammunition stack, store or means of transport in preparation for any subsequent Explosive Risk Assessment

## Slide 3: Lesson overview
Understanding and Calculating NEQ
Calculating the NEQ for an ammunition stack, store and for ammunition in transit
NEQ and UN T/PCC Ammunition Managers
Notes: Main idea/objective for slide:
Introduce the Key Learning Points
What the instructor should cover (in addition to slide content)
Emphasise ‘recall’ – this is revisiting/revising content covered in the workbook
Key Learning Points
2.2.2.1 Recall the NEQ calculations
2.2.2.2 Discuss the NEQ calculations
2.2.2.3 Apply the NEQ calculations to a unit of ammunition
2.2.2.4 Apply the NEQ calculations to an ammunition stack
2.2.2.5 Apply the NEQ calculations to an ammunition store
2.2.2.6 Apply the NEQ calculations to ammunition during transport
2.2.2.7 Analyse how this would apply to a UN T/PCC Ammunition Manager

## Slide 4: Which has the most explosive material?
Notes: Phase 1. Introduction (Time allocation - 15 min)
Main idea/objective for slide:
Discuss using images, which of these two items holds the most explosive material (in Kg’s) and which is more powerful/destructive.
What the instructor should cover (in addition to slide content)
Explore with the participants, how you find out the amount of explosive material in ammunition.
Block Demolition M5 = 1.1Kg NEQ 1.1D
Round 7.62mm x 51 = 900 x 2.85 grams = 2.565Kg NEQ 1.4S
Photographs in this slide are © Swedish EOD Centre

## Slide 5: Theory of Explosives
What is an Explosive?
An explosive is a substance that when initiated, exerts a sudden and intense pressure on its surroundings, by the rapid formation of large quantities of gas
Notes: Main idea/objective for slide:
Briefly revise the Theory of Explosives based on the pre-course work book.
participant activity
Before revealing the text on the slide, ask participants
What is an Explosive?
Write the participants comments on a whiteboard

## Slide 6: Theory of Explosives
What are the two types of Explosives?
High Explosives:
    Detonate producing a Shock wave
    Velocity of Detonation (VoD) based on chemical composition
    Low Explosives:
    Deflagrate (high speed burning)
    Speed of burning dependent on surface area, density and external pressure
Notes: Main idea/objective for slide:
Briefly revise the Theory of Explosives based on the pre-course work book.
participant activity
Before revealing the text on the slide, ask participants
What are the two types of Explosives?
What are the differences between these?

## Slide 7: Classify these as High or Low Explosives
Notes: Main idea/objective for slide:
Practice classifying high vs low explosives
What the instructor should cover (in addition to slide content)
Ask the participants to write down whether they classifiy each of these items as a 'high' or 'Low' explosive
Check their understanding by going through each image one at a time.
Photographs in this slide are © Swedish EOD Centre

## Slide 8: Propellants
Definition
“An explosive material which undergoes rapid and predictable combustion (without detonation!) resulting in a large volume of heated gas”
Often used to:
  Propel projectiles, bullets and missile warheads
Notes: Main idea/objective for slide:
Briefly revise the Theory of Explosives based on the pre-course work book.
participant activity
Before revealing the text on the slide, ask participants for definition
What the instructor should cover (in addition to slide content)
Photographs in this slide are © Swedish EOD Centre

## Slide 9: Propellants
Composition
Three basic types of solid gun propellant:
Single base: Nitrocellulose
Double base: Nitrocellulose and Nitroglycerine
Triple based: Nitrocellulose, Nitroglycerine and Nitroguanidine
Notes: Main idea/objective for slide:
Briefly revise the Theory of Explosives based on the pre-course work book.
participant activity
Ask the participants to comment on the differences between the three types of propellants and in what ways are they used
What the instructor should cover (in addition to slide content)

## Slide 10: Pyrotechnics
“Pyrotechnic”:
  Pyr (Fire)
  Techne (An Art)
Burning to produce a special effect:
  Coloured smoke
  Noise
  Emission of bright coloured light
  Generation of heat
  Delay compositions
  Igniter compositions
Notes: Main idea/objective for slide:
Briefly revise the Theory of Explosives based on the pre-course work book.
participant activity
Ask the participants to comment on the various ways that pyrotechnics are used on deployed missions
What the instructor should cover (in addition to slide content)
Photographs in this slide are © Swedish EOD Centre

## Slide 11: Pyrotechnics
Similar to explosive compositions:
  Explosives (supersonic decomposition)
  Propellants (subsonic decomposition)
  Pyrotechnics (visibly observable rates)
Fuel/oxidiser composition:
  Specific ratio required
  Heat produced used to react with other volatile substance to produce the required effect
Notes: Main idea/objective for slide:
Briefly revise the Theory of Explosives based on the pre-course work book.
participant activity
Explore the participants understanding of supersonic and subsonic decomposition
What the instructor should cover (in addition to slide content)

## Slide 12: Theory of Explosives
What is this called?
Detonator
High Explosive
Detonating cord
Power/Switch
Notes: Main idea/objective for slide:
Explore with participants their understanding of Explosive Trains.
participant activity
Before revealing this graphic:
Ask a participant to draw an explosive train on a white board
What the instructor should cover (in addition to slide content)
Highlight the Primary, and secondary explosive materials in this diagram.

## Slide 13: Theory of Explosives
What are the effects of an explosion?
  High explosive
    Shock wave
    Brisance
    Intense heat and gas generation (Blast)
  Low Explosive
    Intense heat and gas generation
What hazards effect explosives?
Heat / Impact / Chemicals / Degradation / Moisture
Notes: Main idea/objective for slide:
Briefly revise the Theory of Explosives based on the pre course work book
participant activity
Before revealing the text on the slide, ask participants for suggestions
What the instructor should cover (in addition to slide content)

## Slide 14: Understanding and Calculating NEQ Understanding and Calculating NEQ
Notes: Phase 2. Development
Stage 1 – Understanding and Calculating NEQ

## Slide 15: Definitions
NEQ – Net Explosive Quantity The total explosive content present in a container, ammunition, building etc
AUW – All Up Weight The AUW is the total weight of the munition, or munitions, including packaging and palletisation
Notes: Main idea/objective for slide:
Introduce the participants to the concept of NEQ and AUW
participant activity
Before revealing the text on the slide, ask participants for definitions
What the instructor should cover (in addition to slide content)
Highlight the differences.
Use a flipchart to draw images to explain the difference.

## Slide 16: Markings on Containers
1
2
3
4
Notes: Main idea/objective for slide:
outline the other markings that indicate weight on ammunition packaging
participant activity
Ask the participants to name and explain the markings on the above image
1 - Net Explosive Quantity
2 - Net Weight of Box
3 - Gross Weight of Box
4 - Volume of Box
Some boxes do not have all the markings
What the instructor should cover (in addition to slide content)
Distinguish between these markings for the participants.

## Slide 17: TNT Equivalence Table for Typical Explosive Compounds
Serial Number | Explosive | Mass Specific Energy Qx (kJ/kg) | TNT Equivalent (Qx/QTNT)
1 | Torpex (42% RDX, 40% TNT, 18% aluminium) | 7,450 | 1.667
2 | Nitroglycerin (liquid) | 6,700 | 1.481
3 | PETN | 5,800 | 1.282
4 | HMX | 5,680 | 1.256
5 | Semtex | 5,650 | 1.250
6 | RDX (Cyclonite) | 5,360 | 1.185
7 | Compound B (60% RDX, 40% TNT) | 5,190 | 1.148
8 | Pentolite 50/50 (50% PETN, 50% TNT) | 5,110 | 1.129
9 | TNT | 4,520 | 1.000
10 | Tetryl | 4,520 | 1.000
11 | Blasting gelatin (91% nitroglycerin, 7.9% nitrocellulose, 0.9% antacid, 0.2% water) | 4,520 | 1.000
12 | 60% Nitroglycerin dynamite | 2,710 | 0.600
13 | Amatol (80% ammonium nitrate, 20% TNT) | 2,650 | 0.586
14 | Mercury Fulminate | 1,790 | 0.395
15 | Lead Azide | 1,540 | 0.340
Notes: Main idea/objective for slide:
Discuss the importance of TNT Equivalence and highlight the range of TNT Equivalence factors for common explosives as per the table.
participant activity
What the instructor should cover (in addition to slide content)
Use the whiteboard and give example calculations for a range of primary and secondary explosives.

## Slide 18: Calculating the NEQ for an ammunition stack
Notes: Phase 2. Development
Stage 2 – Calculating the NEQ for an ammunition stack

## Slide 19: Calculate NEQ for an Ammunition Stack
Stack of 100 Rds 105mm HE (TNT)
Each Round has 2.35kg HE
100 Rounds (2.35kg x 100) = 235kg HE
NEQ for a stack of 100 Rds 105mm HE is 235kg
Notes: Main idea/objective for slide:
Introduce the participants to calculating the NEQ for an ammunition Stack.
participant activity
Ask participants questions as this example is being prepared on the board, such as 'What next..?'
What the instructor should cover (in addition to slide content)
Work out this example on a white board to ensure participants understanding.

## Slide 20: Calculate NEQ for an Ammunition Stack
Stack of 100 Rds 105mm HE (Comp B)
Each Round has 2.35kg HE
100 Rounds (2.35kg x 100 x 1.148) = 269.8kg HE
NEQ for a stack of 100 Rds 105mm HE is 269.8kg
TNT Equivalence factor for Comp B = 1.148
Notes: Main idea/objective for slide:
Introduce the participants to calculating the NEQ for an ammunition Stack.
participant activity
Ask participants questions as this example is being prepared on the board, such as 'What next..?'
What the instructor should cover (in addition to slide content)
Work out this example on a white board to ensure participants understanding.

## Slide 21: Calculating the NEQ for an ammunition store
Notes: Phase 2. Development
Stage 2 – Calculating the NEQ for an ammunition store

## Slide 22: Calculate the NEQ for an Ammunition Store
Determine full list of explosive articles being stored
Calculate the NEQ for each Stack within the Store
Add up the stack NEQs to determine the overall Store NEQ weight.
Notes: Main idea/objective for slide:
Introduce the participants to calculating the NEQ for an ammunition Store
What the instructor should cover (in addition to slide content)
Outline to the participants how important it is to have accurate calculations of how much NEQ is in each explosive storehouse,
Photograph is © AMAT/GICHD

## Slide 23: Calculate NEQ for an Ammunition Store
Items in Store:
100 boxes 76mm HE (NEQ = 1,512kg)
25 Boxes GREN FRAG (NEQ = 30kg)
50 Boxes 60mm Mortar HE (NEQ = 121.6kg)
Total NEQ for Store = 1,512 + 30 + 121.6
= 1,663.6kg
Notes: Main idea/objective for slide:
Introduce the participants to calculating the NEQ for an ammunition Store
participant activity
Ask participants questions as this example is being prepared on the board, such as 'What next..?'
What the instructor should cover (in addition to slide content)
Work out this example on a white board to ensure participants understanding.

## Slide 24: Calculating the NEQ for an ammunition in transit
Notes: Phase 2. Development
Stage 2 – Calculating the NEQ for an ammunition in transit

## Slide 25: Calculate the NEQ for an Ammunition in Transit
Determine full list of explosive articles being transported in each truck or container
Calculate the NEQ for each Stack within the vehicle/container
Add up the stack NEQs to determine the overall NEQ weight.
Notes: Main idea/objective for slide:
Introduce the participants to calculating the NEQ for an ammunition in transit
participant activity
What the instructor should cover (in addition to slide content)
Outline to the participants how important it is to have accurate calculations of how much NEQ is in each truck/vehicle
Images are © AMAT/GICHD

## Slide 26: Calculate NEQ for an Ammunition in Transit
Items in Vehicle A:
25 Boxes 84mm RCL HEAT (NEQ = 169.5kg)
20 Boxes 60mm Mortar HE (NEQ = 48.64kg)
Total NEQ for Store = 169.5 + 48.64
= 218.14kg
Notes: Main idea/objective for slide:
Introduce the participants to calculating the NEQ for an ammunition in transit
participant activity
Ask participants questions as this example is being prepared on the board, such as 'What next..?'
What the instructor should cover (in addition to slide content)
Work out this example on a white board to ensure participants understanding.

## Slide 27: NEQ and UN T/PCC Ammunition Managers
Notes: Phase 2. Development
Stage 3 – participant exercise: NEQ and UN T/PCC Ammunition Managers

## Slide 28: Exercise
See Handout
Container 1
100 rounds 84mm HEAT
300 rounds AT4 SRAAW
Container 2
100 rounds 81mm SMK
200 bombs 60mm SMK
Container 3
50 x Shell 105mm HE
20 x Grenade M72 HE
100 x Bomb Mortar 60mm HE
500 x Round 40mm HE
500 x Round 20mm HE
5000 x Round 5.56mm BALL NATO
5000 x Round 7.62mm BALL
5000 x Round 7.65mm BALL
120 x Grenade Smoke Screening
Notes: Main idea/objective for slide:
participant exercise to calculate the required NEQ for a convoy of vehicles moving by road while deployed on a UN mission.
participant activity
Calculate the NEQs using the information provided in the Lesson Handout (Word doc 'Lesson 06a - NEQ Calculation_practical exercise’) (see lesson spec L06)
What the instructor should cover (in addition to slide content)
Instructors are to move around the class and help participants where required.
Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions.

## Slide 29: Exercise
Identify the NEQ for each nature of ammunition in the convoy
Determine the NEQ for each vehicle load
Provide the total NEQ for the Convoy
Make a list of safety considerations for the transport of this quantity of ammunition to FOLSA
Notes: Main idea/objective for slide:
participant exercise to calculate the required NEQ for a convoy of vehicles moving by road while deployed on a UN mission.
participant activity
Calculate the NEQs using the information provided in the Lesson Handout (Word doc 'Lesson 06a - NEQ Calculation practical exercise')
What the instructor should cover (in addition to slide content)
Instructors are to move around the class and help participants where required.
Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions.
Solution:
Container 1 = 233kg
100 rounds 84mm HEAT. 100 x 1.13kg = 113kg
300 rounds AT4 SRAAW. 300 x 0.4kg = 120kg
Container 2 = 129.6kg
100 rounds 81mm SMK 100 x 0.68kg = 68kg
200 rounds 60mm SMK 200 x 0.303kg = 60.6kg
Container 3 =
Total Convoy NEQ 233kg + 128.6kg = 362.6 kg

## Slide 30: Lesson overview
Understanding and Calculating NEQ
Calculating the NEQ for an ammunition stack, store and for ammunition in transit
NEQ and UN T/PCC Ammunition Managers
Notes: Phase 3. Consolidation (Time allocation - 5 min)
Main idea/objective for slide:
Recap Key Learning Points
Key Learning Points
2.2.2.1 Recall the NEQ calculations
2.2.2.2 Discuss the NEQ calculations
2.2.2.3 Apply the NEQ calculations to a unit of ammunition
2.2.2.4 Apply the NEQ calculations to an ammunition stack
2.2.2.5 Apply the NEQ calculations to an ammunition store
2.2.2.6 Apply the NEQ calculations to ammunition during transport
2.2.2.7 Analyse how this would apply to a UN T/PCC Ammunition Manager

## Slide 31: Questions?
Notes: Main idea/objective for slide:
Give participants opportunity to ask any questions

## Slide 32
Look Ahead: Ammunition Safe Storage
Weapons and Ammunition Management in UN Peace Operations
Notes: Main idea/objective for slide:
Look ahead to the next lesson of the course:
Ammunition Safe Storage