## Slide 1
Weapons and Ammunition Management in UN Peace Operations
Hazard Classification Codes
Notes: Key Reference Documents for this lesson:
UN Manual on Ammunition Management
UN Weapons and Ammunition Management Policy (WAM)
International Ammunition Technical Guidelines (IATG)
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf
All photographs in this lesson are © United Nations unless otherwise stated.

## Slide 2: Objective
Apply Hazard Classification Code mixing Rules for the safe storage, transportation and packaging of ammunition.
Notes: Main idea/objective for slide:
Phase 1. Introduction - Introduce the objectives of the lesson.
(Enabling Objective: 2.2.4 Apply Hazard Classiciation Code mixing Rules for the safe storage, transportation and packaging of ammunition.)
What the instructor should cover (in addition to slide content)
By the end of this training session the participant will apply Hazard Classification Code mixing rules for the safe storage, transportation and packaging of ammunition.

## Slide 3: Lesson overview
Recall UN Hazard Classification Code systems and compatibility groups
Discuss UN Hazard Classification Code mixing rule
Apply the Hazard Classification Code mixing rules to an ammunition container and to ammunition transportation
Analyse how this would apply to a UN T/PCC Ammunition Manager
Notes: Main idea/objective for slide:
Introduce the Key Learning Points
What the instructor should cover (in addition to slide content)
Emphasise ‘recall’ – this is revisiting/revising content covered in the workbook
Key Learning Points
2.2.4.1 Recall UN Hazard Classification Code systems
2.2.4.2 Recall UN Hazard Classification Code compatibility groups
2.2.4.3 Discuss UN Hazard Classification Code mixing rule
2.2.4.4 Apply the Hazard Classification Code mixing Rules to an ammunition container
2.2.4.5 Apply the Hazard Classification Code mixing Rules to an ammunition site
2.2.4.6 Apply the Hazard Classification Code mixing Rules to ammunition transportation
2.2.4.7 Analyse how this would apply to a UN T/PCC Ammunition Manager

## Slide 4
The Likelihood and Impact of an Ammunition Incident
Notes: Phase 1. Introduction (Time allocation - 15 min)

## Slide 5
Notes: Main idea/objective for slide:
Discuss using images, the various components of ammunition, pyrotechnics, and explosives and how they are designed to function.
What the instructor should cover (in addition to slide content)
Ask the participants to describe, for each image, how these munition types function.
Explore with the participants, the likelihood and the impact of a serious event, when no rules apply to mixing of ammunition and explosive natures.
Write these potential impacts on a flipchart.
Images supplied by AMAT/GICHD and SWEDEC, Swedish Armed Forces.

## Slide 6
Understanding Hazard Class Coding
Notes: Phase 2. Development (Time allocation - 70 min)
Stage 1 (Time allocation 25 mins) – Understanding Hazard Class Coding

## Slide 7: Introduction
Hazard Divisions (HD)
  Indicates the type of hazard to be expected in the event of an accident.
  There are nine (9) classes.
    Articulated 1 to 9.
  The number for Explosives is “1”.
  Subdivided depending on the type of hazard:
    1.1
    1.2
    1.3
    1.4
    1.5
    1.6
Notes: Main idea/objective for slide:
Revise Hazard Divisions.
participant activity
Before revealing the text on the slide, ask participants what they can tell you about Hazard Divisions
What the instructor should cover (in addition to slide content)
References/further reading
This UN system covers all sorts of dangerous goods from chemicals to medical waste and are defined in nine (9) top-level classes
The Class Number for Explosives is “1”. This is then subdivided into explosives that present different types of hazard for example “1.1” or “1.2” which will be called a Hazard DIVISION.
Hazard Division indicate the type of hazard to be expected primarily in the event of an accident involving a quantity of ammunition. The divisions are articulated numerically.

## Slide 8: Introduction
Compatibility Groups (CG)
  Designed to minimise the risk of storing items together that will either increase the risk or the effects of an accident.
  Articulated by Letters:
    A, B, C, D, E, F, G, H, J, K, L, N, S
Notes: Main idea/objective for slide:
Revise Compatibility Groups
participant activity
Before revealing the text on the slide, ask participants what they can tell you about Compatibility Groups
What the instructor should cover (in addition to slide content)
References/further reading
Compatibility Groups are designed to minimise the risk of storing items together that will either increase the risk of an accident or, for a given quantity, the magnitude of the effects of such an accident. The Compatibility Groups are articulated alphabetically, for example “C” or “D

## Slide 9: Introduction
Hazard Classification Code (HCC)
  Combination of the “Hazard Division” and the “Compatibility Group” results in an alpha-numeric:
    1.1D or 1.4S
Notes: Main idea/objective for slide:
Discuss the origins and rationale of using Hazard Class Codes.
participant activity
Before revealing the text on the slide, ask participants what they can tell you about HCC
What the instructor should cover (in addition to slide content)
These codes, or a similar national system, are critical to the safe storage and movement of ammunition and explosives.
Note that the application of the Hazard Division and Compatibility Group does not take into account the probability of an incident. It assumes that if it can happen it will, and when it does, it identifies the extent of the hazards.
References/further reading
The combination of the “Hazard Division” and the “Compatibility Group” results in an alpha-numeric “Hazard Classification Code” for each item and type of ammunition and explosives. For example "1.1D" or "1.4S".

## Slide 10: Hazard Classification Code
Hazard Division
Denotes the type of hazard to be expected
Compatibility Group
Denotes what can be stored together to minimise risk
Hazard Classification Code
Denotes what can be stored together to minimise risk
Notes: Main idea/objective for slide:
Discuss the origins and rationale of using Hazard Class Codes.
What the instructor should cover (in addition to slide content)
The system comprises:
Hazard Divisions (HD)
Compatibility Groups (CG)
and, when these are combined together: Hazard Classification Codes (HCC)
References/further reading

## Slide 11: Hazard Divisions
The Hazard Division here is 1.4
It is also shown with Compatibility Group, here it is ‘S’
Note that ammunition and its containers generally have many other types of markings as well.
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
The Hazard Division for a particular explosive or type of ammunition shall be determined by its performance and test results according to Part I of the Manual of Tests and Criteria of the UN Recommendations on the Transport of Dangerous Goods.
Stockpile management organisations should ensure that the conventional ammunition and explosives in their possession is classified accordingly, although
alternative local systems may be utilised.
The Hazard Divisions are most often seen marked on orange diamonds on ammunition packaging. Note that these diamonds usually also include the Compatibility group, thus showing the complete Hazard Classification Code. Note that ammunition packaging will generally have a number of other markings on it, all of which perform some useful function. However in this lesson we are only looking at the Hazard Classification Codes.
There are 6 Hazard Divisions for Class 1 Explosive Goods. These are 1.1, 1.2, 1.3, 1.4, 1.5, and 1.6. We will come onto these next.
Note that there is also an additional category which covers unstable explosives. There is no pictogram or HD for this type of ammunition, as unstable explosives are not allowed to be transported.
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading
Photograph is © AMAT/GICHD

## Slide 12: Hazard Divisions
The Hazard Division here is 1.1
It is also shown with Compatibility Group, here it is ‘D’
Note that ammunition and its containers generally have many other types of markings as well.
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
The photo of the box of PE4 Plastic Explosive cartridges has an orange diamond on it. This shows that this type or store is HD 1.1.
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading

## Slide 13: Hazard Divisions
The Hazard Division here is 1.4
It is also shown with Compatibility Group, here it is ‘S’
Note that ammunition and its containers generally have many other types of markings as well.
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading

## Slide 14: Hazard Divisions
The Hazard Division here is 1.2
It is also shown with Compatibility Group, here it is ‘F’
Note that ammunition and its containers generally have many other types of markings as well.
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading

## Slide 15: Hazard Divisions
The Hazard Division here is 1.2
It is also shown with Compatibility Group, here it is ‘E’
Note that ammunition and its containers generally have many other types of markings as well.
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading

## Slide 16: Class 1 Hazard Division
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading

## Slide 17: Hazard Division 1.1
HD 1.1
  Ammunition that has a mass explosion hazard
  May produce a fragmentation and fire hazard
  e.g. Bulk demolition explosive
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
Hazard Division 1.1 has a mass explosion hazard. Note that ammunition in this HD may also produce a fragmentation and fire hazard as well. The main hazard is that of the blast though. An example of a HD 1.1 store might be bulk demolition explosive.
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf
Images found at https://www.airseacontainers.com/blog/hazard-class-101-know-how-to-categorize-your-hazardous-materials/

## Slide 18: Hazard Division 1.2
HD 1.2
  Ammunition that has a projection hazard but not a mass explosion hazard
  Severe projection hazard
  e.g. Certain types of grenades
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
Hazard Division 1.2 has a projection hazard. This means it may produce fragmentation if it functions in an accident. There is no mass explosion hazard though. An example of a HD 1.2 store might be some kinds of grenade.
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 19: Hazard Division 1.3
HD 1.3
  Ammunition that has a fire hazard
  May produce a minor blast or projection hazard
  e.g. Incendiary ammunition
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
Hazard Division 1.3 has a fire hazard. It will also have a minor blast or projection hazard. It does not have a mass explosion hazard though.
The main hazard however is that of fire. An example of a HD 1.3 store might be some kinds of incendiary ammunition.
Note that NATO further subdivide this Hazard Division into 1.3.1 and 1.3.2, to add further granularity to the description based on the type of fire/flash hazard.
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 20: Hazard Division 1.4
HD 1.4
  No significant hazard in an accident
  e.g. Small Arms Ammunition (SAA)
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
Hazard Division 1.4 presents no significant hazard in an accident. The usual example of a HD 1.4 stores would be many types of conventional small arms ammunition.
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 21: Hazard Division 1.5
HD 1.5
  Very insensitive substances which may produce a mass explosion hazard
  Known as ‘Insensitive Munitions’
  Rarely deployed on UN Missions
  Commercial blasting explosives
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
Hazard Division 1.5 relates to very insensitive substances, but which if they do actually initiate will produce a mass explosion hazard.
This Hazard Division may become more widely used as more technologically developed nations develop what are known as “Insensitive Munitions”, also known as “IM”. This type of ammunition may also be known by its French abbreviation “MURAT” These are items of ammunition which are very, very difficult to initiate accidently. For example, a polymer bonded high explosive which is highly unlikely to initiate because of fire or other unplanned stimulus. However, if the IM explosive does initiate, then there will still be a mass explosion hazard.
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 22: Hazard Division 1.6
HD 1.1
  Very insensitive substances which will not produce a mass explosion hazard
Notes: Main idea/objective for slide:
Introduce and explain the Hazard Divisions, using examples
What the instructor should cover (in addition to slide content)
Hazard Division 1.6 ammunition is also extremely insensitive (as for HD 1.5), however even if it does initiate it will not produce a mass explosion hazard.
participant activity
Ask participants to provide further examples
Using a flipchart, write examples under each HD and place it on the wall.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 23: Fire Divisions
Often used with the Hazard Divisions
Used by Fire Fighting Personal to recognise the fire hazard of the store
Used on storage facilities
Different shapes to be recognised from far away
Notes: Main idea/objective for slide:
Introduce and discuss the various Fire Divisions and where they are used.
What the instructor should cover (in addition to slide content)
There are six fire divisions. These equate to the Hazard Divisions.
Each Fire Division has a symbol that represents it. A fire division number is shown on each symbol. These are shown on the slide.
The symbol should be indicated during storage and transportation. This is to allow fire fighting personnel to recognise the fire hazard when approaching the scene of an incident. Hazard Division symbols may also be used for this purpose.
By way of clarification:
The Fire Division 1 fire symbol and number is also used for Fire Division 5 as the fire-fighting hazards are very similar.
The Fire Division 2 fire symbol and number is also used for Fire Division 6 for the same reason.
participant activity
Ask the participants to provide ammunition examples, explain what Fire Division they are in and what considerations they would need to take in the event of a fire.
Write these on a flipchart
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 24
Compatibility Groups
Notes: Phase 2. Development (Time allocation - 70 min)
Stage 2 (Time allocation 25 mins) – Compatibility Groups

## Slide 25: Compatibility Groups
Identify commonalities between ammunition stores
  More importantly – identify incompatible stores
The CG is added to the HD to form the complete
  HAZARD CLASSIFICATON CODE (HCC)
The practical use of these is when applying the ‘Mixing Rules’
Notes: Main idea/objective for slide:
Introduce the participants to the Compatibility Groups and explain their purpose.
What the instructor should cover (in addition to slide content)
Each specific type of conventional ammunition should be allocated a "Compatibility Group". This helps to store similar stores with each. More importantly however, it helps to identify stores which should not be stored together. For example, we would not want to store white phosphorous shells with bulk explosive. In the event of an accident, the combined effect of significant blast and white phosphorous would be much, much worse than an event involving only one of these types of store individually.
There may be hundreds of thousands of individual ammunition items, of many different types, stored in a single stockpile. The different types of ammunition will vary in purpose, calibre, explosive type and manufacturer, all with varying degrees of volatility. Compatibility Groups help to identify commonalities between stores.
Thus, the Compatibility Groups are considered as important to aide safe stock management. The "Compatibility Group" is added to the "Hazard Division" to form the complete "Hazard Classification Code".
The real practical use of the Compatibility Group is when we look at the “Mixing Rules” shortly.
participant activity
Ask questions to the class to ensure understanding.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 26: Example 1 – Detonators
Compatibility Group B
  Articles containing a primary explosive substance and not containing two or more effective protective features
© SWEDEC, Swedish Armed Forces
Notes: Main idea/objective for slide:
Provide examples of Compatibility Groups in images and discuss with the participants
What the instructor should cover (in addition to slide content)
An example would be detonators, as they contain a primary explosive. Furthermore, they are unlikely to include two or more effective safety features.
participant activity
Ask questions to the class to ensure understanding.
References/further reading

## Slide 27: Example 2 – Mortar Smoke WP
Compatibility Group H
  Article containing both explosive substance and white phosphorus.
Notes: Main idea/objective for slide:
Provide examples of Compatibility Groups in images and discuss with the participants
What the instructor should cover (in addition to slide content)
An example would be white phosphorous smoke mortar bombs which also include a bursting charge and a propelling charge. The notes to this CG also state “or other ammunition containing pyrophoric material”, so items containing red phosphorous and thermite may well come under this CG.
participant activity
Ask questions to the class to ensure understanding.
References/further reading

## Slide 28: Example 3 – Small Arms Ammunition
Compatibility Group S
  Substance or article so packed or designed that any hazardous effects arising from accidental functioning are confined within the package
© SWEDEC, Swedish Armed Forces
Notes: Main idea/objective for slide:
Provide examples of Compatibility Groups in images and discuss with the participants
What the instructor should cover (in addition to slide content)
For example, if an appropriately packaged box of Small Arms Ammunition (SAA) (of the ball type) were involved in an accident, it would be expected that if one of the rounds functioned due to say, heat or unplanned percussion, the bullet upon leaving that round would be contained within the packaging
participant activity
Ask questions to the class to ensure understanding.
References/further reading

## Slide 29: Example 4
Compatibility Group E:
  Article containing a secondary detonating explosive substance without means of initiation, with propelling charge.
Compatibility Group F:
  Article containing a secondary detonating explosive substance with its own means of initiation, with a propelling charge.
Notes: Main idea/objective for slide:
Provide examples of Compatibility Groups in images and discuss with the participants
What the instructor should cover (in addition to slide content)
The difference is whether or not the ammunition has its own means of initiation.
“E” might include a guided missile, assuming that the item cannot be initiated without being attached to a launcher, for example.
“F” might include a rocket propelled grenade.
participant activity
Ask questions to the class to ensure understanding.
References/further reading

## Slide 30: Mixing Rules
This table must be used in conjunction with the notes on the following slide
Notes: Main idea/objective for slide:
Explain what compatibility mixing rules are and how they are applied, using the ‘Mixing Rules’.
What the instructor should cover (in addition to slide content)
Conventional ammunition should be stored in accordance with these mixing rules. This table is in the IATG, specifically at IATG 01:50. Note that this applies to ‘fixed’ ammunition storage sites, for example a base ammunition depot, or similar.
Compatibility Group ‘B’ items are those like detonators. Compatibility Group ‘S’ items are things like SAA Ball ammunition.
Compatibility Group ‘H’ items are incendiary items, for example mortar smoke bombs containing white phosphorous.
participant activity
Ask questions to the class to ensure understanding.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 31: Mixing Rules- Notes
Additionally, the following should always be stored separately
Notes: Main idea/objective for slide:
Explain what compatibility mixing rules Notes are and how they are applied, using the ‘Mixing Rules’.
What the instructor should cover (in addition to slide content)
Conventional ammunition should be stored in accordance with these mixing rules. This table is in the IATG, specifically at IATG 01:50. Note that this applies to ‘fixed’ ammunition storage sites, for example a base ammunition depot, or similar.
Compatibility Group ‘B’ items are those like detonators. Compatibility Group ‘S’ items are things like SAA Ball ammunition.
Compatibility Group ‘H’ items are incendiary items, for example mortar smoke bombs containing white phosphorous.
participant activity
Ask questions to the class to ensure understanding.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 32: Mixing Rules: Temporary Storage
Notes: Main idea/objective for slide:
Explain what compatibility mixing rules are and how they are applied, using the ‘Mixing Rules Table for Field Storage’.
What the instructor should cover (in addition to slide content)
Temporary storage presents its own challenges.
A larger safety area will also often be necessary, to ensure explosive safety for neighbouring civilian populations. There will also be security issues to be addressed as the ground area is necessarily larger than that used for permanent ammunition storage facilities.
This table is different from the ‘standard’ mixing rules.
The principle is the same. It is however important to use the correct table, depending on the situation.
participant activity
Ask questions to the class to ensure understanding.
References/further reading
IATG 04.10 Temporary Storage

## Slide 33: Mixing Rules- Notes
Additionally, the following should always be stored separately
Notes: Main idea/objective for slide:
Explain what compatibility mixing rules Notes are and how they are applied, using the ‘Mixing Rules’.
What the instructor should cover (in addition to slide content)
Conventional ammunition should be stored in accordance with these mixing rules. This table is in the IATG, specifically at IATG 04.10. Note that this applies to ‘temporary’ ammunition storage sites, for example a UN Mission operating base, or similar.
Compatibility Group ‘B’ items are those like detonators. Compatibility Group ‘S’ items are things like SAA Ball ammunition.
Compatibility Group ‘H’ items are incendiary items, for example mortar smoke bombs containing white phosphorous.
participant activity
Ask questions to the class to ensure understanding.
References/further reading
http://data.unsaferguard.org/iatg/en/IATG-01.50-Explosive-hazard-classification-system-IATG-V.3.pdf

## Slide 34: Worked Example
How many Ammunition containers will be required to safely store the following ammunition types?
Ammunition Type | Hazard Class Code | Quantity | NEQ
Rds 7.62mm Ball | 1.4S | 10,000 | 30kg
Rds 84mm RCL HEAT | 1.1E | 25 | 28kg
Bombs 60mm Mortar HE | 1.1F | 250 | 76kg
Bombs 60mm Mortar SMK | 1.3G | 100 | 30kg
Grenade Smoke Screening | 1.3G | 100 | 33kg
TNT Charge (500g) | 1.1D | 50 | 25kg
Notes: Main idea/objective for slide:
Provide a range of examples, highlighting how the mixing rules work.
What the instructor should cover (in addition to slide content)
Complete a worked-out example on applying mixing rules for a storage container.
Work through this example and ask questions to the participants regularly.
participant activity
Ask questions to the class to ensure understanding.
References/further reading

## Slide 35
participant Exercise
Notes: Phase 2. Development (Time allocation - 70 min)
Stage 3 (Time allocation 20 mins) – participant Exercise

## Slide 36: Exercise
UNAC SATO has directed that a consignment of ammunition move from Camp MUKA and be held temporarily at Camp FOLSA, while the Engineer Group build a new Temporary Storage Area
You have been tasked to
Review the additional ammunition stocks
Provide justification as to how you can store them within your own Storage compound while paying close attention to Temporary Storage Mixing Rules
Notes: Main idea/objective for slide:
participant exercise using the CARANA scenario to identify the various Hazard Classification Codes and Fire Divisions for a range of ammunition natures deployed on a UN mission.
What the instructor should cover (in addition to slide content)
Instructors are to move around the class and help participants where required. Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions
participant activity
participants must identify the compatibility groups and use the Mixing Rules Table for Field Storage for both ammunition natures that are currently being stored in their own camp and integrate the additional ammunition stores arriving from Camp MUKA
participants must provide a rationale as to how they decided on the mixing of these ammunition natures and explain how many ammunition containers they will require to hold the complete stock.
References/further reading

## Slide 37: Exercise
Your T/PCC Contingent Stocks
Ammunition Type | Hazard Class Code | Quantity | NEQ
Rds 7.62mm Ball Mixed Belt | 1.4S | 25,000 | 75kg
Rds 5.56mm Ball | 1.4S | 50,000 | 100kg
Rds 9mm Ball | 1.4S | 10,000 | 20kg
Rds 84mm RCL HEAT | 1.1E | 50 | 57kg
Grenade 40x46mm HEAT | 1.2E | 200 | 120kg
Gren 66mm Smoke Screen | 1.3G | 250 | 82kg
Bombs 60mm Mortar HE | 1.1F | 300 | 90kg
Gren HE | 1.1D | 400 | 24kg
TNT Charge (500g) | 1.1D | 200 | 100kg
Detonators | 1.1B | 500 | 0.1kg
Notes: Main idea/objective for slide:
participant exercise using the CARANA scenario to identify the various Hazard Class Codes and Fire Divisions for a range of ammunition natures deployed on a UN mission.
What the instructor should cover (in addition to slide content)
Instructors are to move around the class and help participants where required. Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions
participant activity
participants must identify the compatibility groups and use the Mixing Rules Table for Field Storage for both ammunition natures that are currently being stored in their own camp and integrate the additional ammunition stores arriving from Camp MUKA
participants must provide a rationale as to how they decided on the mixing of these ammunition natures and explain how many ammunition containers they will require to hold the complete stock.
References/further reading

## Slide 38: Exercise
Additional Ammunition Stocks from Camp MUKA
Ammunition Type | Hazard Class Code | Quantity | NEQ
Rds 7.62mm Ball | 1.4S | 10,000 | 30kg
Rds 84mm RCL HEAT | 1.1E | 25 | 28kg
Rds 84mm RCL ILLUM | 1.2G | 50 | 56kg
Bombs 60mm Mortar HE | 1.1F | 250 | 76kg
Bombs 60mm Mortar SMK | 1.3G | 100 | 30kg
Grenade Smoke Screening | 1.3G | 100 | 33kg
TNT Charge (500g) | 1.1D | 50 | 25kg
Notes: Main idea/objective for slide:
participant exercise using the CARANA scenario to identify the various Hazard Class Codes and Fire Divisions for a range of ammunition natures deployed on a UN mission.
What the instructor should cover (in addition to slide content)
Instructors are to move around the class and help participants where required. Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions
The instructor can add more exercises if required by improvising new lists of ammunition.
participant activity
participants must identify the compatibility groups and use the Mixing Rules Table for Field Storage for both ammunition natures that are currently being stored in their own camp and integrate the additional ammunition stores arriving from Camp MUKA
participants must provide a rationale as to how they decided on the mixing of these ammunition natures and explain how many ammunition containers they will require to hold the complete stock.
References/further reading

## Slide 39: Available Storage
ESH 1: can store 200kg of 1.1
ESH 2: can store 375kg of 1.1
ESH 3: can store 150kg of 1.1
ESH 4: can store 75kg of 1.1
ESH 1
ESH 2
ESH 3
ESH 4

## Slide 40: Solution
Ammunition Type | Hazard Class Code | Quantity | NEQ (kg) | S | 1.1E | 1.2E | 1.1D | 1.2G | 1.3G | 1.1F | 1.1B
Rds 7.62mm Ball Mixed Belt | 1.4S | 25,000 | 75 | 75 |  |  |  |  |  |  | 
Rds 5.56mm Ball | 1.4S | 50,000 | 100 | 100 |  |  |  |  |  |  | 
Rds 9mm Ball | 1.4S | 10,000 | 20 | 20 |  |  |  |  |  |  | 
Rds 84mm RCL HEAT | 1.1E | 50 | 57 |  | 57 |  |  |  |  |  | 
Grenade 40x46mm HEAT | 1.2E | 200 | 120 |  |  | 120 |  |  |  |  | 
Gren 66mm Smoke Screen | 1.3G | 250 | 82 |  |  |  |  |  | 82 |  | 
Bombs 60mm Mortar HE | 1.1F | 300 | 90 |  |  |  |  |  |  | 90 | 
Gren HE | 1.1D | 400 | 24 |  |  |  | 24 |  |  |  | 
TNT Charge (500g) | 1.1D | 200 | 100 |  |  |  | 100 |  |  |  | 
Detonators | 1.1B | 500 | 0.5 |  |  |  |  |  |  |  | 0.5
Rds 7.62mm Ball | 1.4S | 10,000 | 30 | 30 |  |  |  |  |  |  | 
Rds 84mm RCL HEAT | 1.1E | 25 | 28 |  | 28 |  |  |  |  |  | 
Rds 84mm RCL ILLUM | 1.2G | 50 | 56 |  |  |  |  | 56 |  |  | 
Bombs 60mm Mortar HE | 1.1F | 250 | 76 |  |  |  |  |  |  | 76 | 
Bombs 60mm Mortar SMK | 1.3G | 100 | 30 |  |  |  |  |  | 30 |  | 
Grenade Smoke Screening | 1.3G | 100 | 33 |  |  |  |  |  | 33 |  | 
TNT Charge (500g) | 1.1D | 50 | 25 |  |  |  | 25 |  |  |  | 
 |  | Total NEQ | 946.5 | 225 | 85 | 120 | 149 | 56 | 145 | 166 | 0.5
 |  | Total per CC |  | n/a |  |  | 354 |  | 201 | 166 | 0.5

## Slide 41: Layout
Scenario 1 | 1.1F 166kg and small arms and dets |  | 200 | 166 |  |  |  |  | Scenario 3 | All G stores 201kg |  | 200 | 201 |  | 
 |  |  |  | 225 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | 0.5 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  | note as per dividing wall |  |  |  |  |  |  |  |  | G stores exceed licence | 
 | 1.1E 1.2E 1.1D 354kg |  | 375 | 354 |  |  |  |  |  | 1.1E 1.2E 1.1D 354kg |  | 375 | 354 |  | 
 | 1.3G 145kg |  | 150 | 145 |  |  |  |  |  | 1.1F 166kg and small arms |  | 150 | 166 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 225 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  | F stores exceed licence | 
 | 1.2G 56kg |  | 75 | 56 |  |  |  |  |  | 1.1B .5kg |  | 75 | 0.5 |  | 
 |  |  | Total NEQ | 946.5 |  |  |  |  |  |  |  | Total NEQ | 946.5 |  | 
Scenario 2 | 1.1F 166kg and small arms |  | 200 | 166 |  |  |  |  | Scenario 4 | 1.1F X 166kg and small arms and dets |  | 200 | 166 |  | 
 |  |  |  | 225 |  |  |  |  |  |  |  |  | 225 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 0.5 |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  | note as per dividing wall | 
 | 1.1E 11.2E 1.1D 354kg |  | 375 | 354 |  |  |  |  |  | 1.1E 1.2E 1.1D X 354kg |  | 375 | 354 |  | 
 | 1.3G 145kg |  | 150 | 145 |  |  |  |  |  | 1.3GX 145kg |  | 150 | 145 |  | 
 | 1.2G 56kg and dets |  | 75 | 56 | note mixing approved by nat competent authority |  |  |  |  | 1.2G 56kg |  | 75 | 56 |  | 
 |  |  |  | 0.5 |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Total NEQ | 946.5 |  |  |  |  |  |  |  | Total NEQ | 946.5 |  | 

## Slide 42: Lesson overview
Recall UN Hazard Classification Code systems and compatibility groups
Discuss UN Hazard Classification Code mixing rule
Apply the Hazard Classification Code mixing rules to an ammunition container and to ammunition transportation
Analyse how this would apply to a UN T/PCC Ammunition Manager
Notes: Phase 3. Consolidation (Time allocation - 10 min)
Main idea/objective for slide:
Recap Key Learning Points
participant activity
Give participants opportunity to ask any questions
What the instructor should cover (in addition to slide content)
Key Learning Points
2.2.4.1 Recall UN Hazard Classification Code systems
2.2.4.2 Recall UN Hazard Classification Code compatibility groups
2.2.4.3 Discuss UN Hazard Classification Code mixing rule
2.2.4.4 Apply the Hazard Classification Code mixing Rules to an ammunition container
2.2.4.5 Apply the Hazard Classification Code mixing Rules to an ammunition site
2.2.4.6 Apply the Hazard Classification Code mixing Rules to ammunition transportation
2.2.4.7 Analyse how this would apply to a UN T/PCC Ammunition Manager

## Slide 43
Weapons and Ammunition Management in UN Peace Operations
Look Ahead: Understanding Ammunition Management
Notes: Main idea/objective for slide:
Look ahead to the next lesson of the course:
  Understanding Ammunition Management