## Slide 1
Weapons and Ammunition Management in UN Peace Operations
Understanding Ammunition Management
Notes: Key Reference Documents for this lesson:
UN Manual on Ammunition Management
UN Weapons and Ammunition Management Policy (WAM)
International Ammunition Technical Guidelines (IATG)
http://data.unsaferguard.org/iatg/en/IATG-03.20-Lotting-batching-IATG-V.3.pdf
http://data.unsaferguard.org/iatg/en/IATG-03.10-Inventory-management-IATG-V.3.pdf
http://data.unsaferguard.org/iatg/en/IATG-06.70-Inspection-explosives-facilities-IATG-V.3.pdf
http://data.unsaferguard.org/iatg/en/IATG-12.10-Multi-national-operations-IATG-V.3.pdf
http://data.unsaferguard.org/iatg/en/IATG-01.60-Ammunition-faults-performance-failures-IATG-V.3.pdf
http://data.unsaferguard.org/iatg/en/IATG-01.70-Bans-constraints-IATG-V.3.pdf
All photographs in this lesson are © United Nations unless otherwise stated.

## Slide 2: Objective
Examine ammunition management on UN operations by T/PCCs
Notes: Main idea/objective for slide:
Phase 1. Introduction - Introduce the objectives of the lesson.
(Enabling Objective: 2.2.5 Examine ammunition management on UN operations by T/PCCs .)
What the instructor should cover (in addition to slide content)
By the end of this training session the participant will examine ammunition management on UN operations by T/PCCs

## Slide 3: Lesson overview
Recall and discuss UN good practices for securing hazardous explosive materials and managing an explosive storage site
Discuss Storage Temperatures and the isolation & segregation of ammunition stocks
Discuss the Stacking and Racking of ammunition and the use of Stack Tally Cards
Discuss Lotting & Batching, the use of Bans & Constraints and determining Faults & Performance failures
Apply checks and inspections to provide confidence that Explosive Storage sites conform to UN and international standards
Examine the use of mitigations based on an explosive risk assessment for a temporary storage area
Notes: Main idea/objective for slide:
Introduce the Key Learning Points
What the instructor should cover (in addition to slide content)
Emphasise ‘recall’ – this is revisiting/revising content covered in the workbook
Key Learning Points
2.2.5.1 Recall UN good practices for securing hazardous explosive materials
2.2.5.2 Recall UN good practices for managing an explosive storage site
2.2.5.3 Recall the requirements for the Calculation of Storage Space
2.2.5.4 Discuss the use of checks and inspections in ammunition management
2.2.5.5 Discuss the UN good practices for securing hazardous explosive materials
2.2.5.6 Discuss the UN good practices for managing an explosive storage site
2.2.5.7 Discuss Storage Temperatures and the isolation & segregation of ammunition stocks
2.2.5.8 Discuss the Stacking and Racking of ammunition and the use of Stack Tally Cards
2.2.5.9 Discuss Lotting & Batching, the use of Bans & Constraints and determining Faults & Performance failures
2.2.5.10 Apply checks and inspections to provide confidence that Explosive Storage sites conform to UN and international standards
2.2.5.11 Examine the use of mitigations based on an explosive risk assessment for a temporary storage area

## Slide 4
Good Practices for Security and Storage of Ammunition
Notes: Phase 1. Introduction (Time allocation - 20 min)

## Slide 5
What do you think are good Ammunition Management practices?
Notes: Phase 1. Introduction (Time allocation - 20 min)
Main idea/objective for slide:
Hold a question and answer session with the participants to discuss the range of good practices for security and associated explosives storage.
Discuss the what and why.
Include bad practice if time is available.
What the instructor should cover (in addition to slide content)
Instructors should note these good points on a flipchart and post them to the wall for future reference.

## Slide 6
Managing Ammunition Stocks
Notes: Phase 2. Development (Time allocation - 150 min)
Stage 1 (Time allocation 50 mins) – Managing Ammunition Stocks

## Slide 7: Lotting and Batching Why is it important?
Lotting and batching is a means by which a discrete and homogenous quantity of ammunition may be identified.
It will usually have been manufactured at the same time, using the same raw materials, using the same process and may therefore be expected to provide a uniform and similar performance.
Lotting and Batching is also important for stockpile accounting and to allow for timely and reliable identification of diversions through loss or theft.
Notes: Main idea/objective for slide:
Provide the rationale and benefit of using lotting and batching markings and explain how they are used to identify ammunition and explosives.
What the instructor should cover (in addition to slide content)
Ask the participants what they believe to be the difference between Lotting and Batching and why it is important to know?
References/further reading
IATG 03.20 – Lotting and Batching. http://data.unsaferguard.org/iatg/en/IATG-03.20-Lotting-batching-IATG-V.3.pdf
Ammunition and explosives may deteriorate more rapidly or become damaged unless they are correctly stored, handled and transported, with the resultant effect that they may fail to function as designed and may become dangerous in storage, handling, transport and use. It is therefore important that the location of specific items of ammunition and explosives can be rapidly identified in order that the appropriate remedial action can be taken to ensure safety during these activities. A system of Lotting and Batching is an important component of this safety mechanism.
Lotting and batching is a means by which a discrete and homogenous quantity of ammunition may be identified. It will usually have been manufactured at the same time, using the same raw materials, using the same process and may therefore be expected to provide a uniform and similar performance. Whether it is appropriate to use Lotting or Batching for an item of ammunition will normally depend upon the complexity of the ammunition (ie the number of different components) and will require technical judgment.
Lotting and Batching is also important for stockpile accounting and to allow for timely and reliable identification of diversions through loss or theft.

## Slide 8: Lotting and Batching Definitions
Batch:
“a discrete quantity of ammunition which is assembled from two or more Lotted components (one of which will be the Primary Governing Component), is as homogeneous as possible and under similar conditions may be expected to give uniform performance”
Lot:
“a predetermined quantity of ammunition or components which is as homogeneous as possible and under similar conditions may be expected to give uniform performance. A Lot is normally manufactured from the same raw materials, using the same production technique and in the same production run”
Notes: Main idea/objective for slide:
Define Batch and Lot
References/further reading
IATG 03.20 – Lotting and Batching

## Slide 9: Allocation of Lot Numbers
Normally issued between the manufacturer and the T/PCC
 | Manufacturers Monogram | Date of Assembly or Manufacture | Unique Identification Number | Suffix | Remarks
Requirement | Up to Three letters | In format MMYY | Up to six numerals | One letter | 
Example | HG | 0817 | 005 | D | 
Range | A to ZZZ |  | 000001 to 999999 | A to X (Excluding B or R) | B or R are uniquely used for propellant Lot numbers
Example Lot Number | HG 0817 005D |  |  |  | 
See Handout
Notes: Main idea/objective for slide:
Explain allocation of Lot numbers, with example
What the instructor should cover (in addition to slide content)
Write the following on the white board and ask the participants explain the parts: AB 0320 36421C
Include table in a hand-out for participants
References/further reading
IATG 03.20 – Lotting and Batching

## Slide 10: Allocation of Lot Numbers
- For Propellants
 | Manufacturers Monogram | Date of Assembly or Manufacture | Unique Identification Number | Suffix | Remarks
Requirement | Up to Three letters | In format MMYY | 1 numeral onwards (to 6) | 1 letter | 
Example | BD | 0817 | 004 | (B) | 
Range | A to ZZZ |  | 1 to 999999 | B, R or nothing only | - B indicates that the propellant was been re- blended at some stage in its life cycle. - R indicates that the propellant has been reworked at some stage in its life cycle. - A suffix is not mandatory.
Example Lot Number | BD 0817 004 |  |  |  | 
See Handout
Notes: Main idea/objective for slide:
Explain allocation of Lot numbers for Propellants, with example
What the instructor should cover (in addition to slide content)
Write the following on the white board and ask the participants explain the parts: FZ 1111 56785 B
Include table in a hand-out for participants
References/further reading
IATG 03.20 – Lotting and Batching

## Slide 11: Allocation of Lot Numbers
- For Small Arms Ammunition
 | Manufacturers Monogram | Date of Assembly or Manufacture | Remarks
Requirement | Up to Three letters | In format DDMMYY | 
Example | FG | 011115 | Laser marking systems for SAA now allow a full Batch number A suffix may be used to identify different Lots (production runs) that commenced production on the same day.
Range | A to ZZZ |  | 
Example Lot Number | FG 011115 |  | 
See Handout
Notes: Main idea/objective for slide:
Explain allocation of Lot numbers for Small Arms Ammunition, with example
What the instructor should cover (in addition to slide content)
Write the following on the white board and ask the participants explain the parts: TFI 290898
Include table in a hand-out for participants
References/further reading
IATG 03.20 – Lotting and Batching

## Slide 12: Find the Lot and Batch numbers
Notes: Main idea/objective for slide:
Using images and working in their groups, have the participants identify the relevant lots and batches of a range of munition natures.
What the instructor should cover (in addition to slide content)
Using each image, ask the participants to identify the Lot numbers and explain the detail in each lot number
References/further reading
IATG 03.20 – Lotting and Batching

## Slide 13: Find the Lot and Batch numbers

## Slide 14: Types of Ammunition Stockpiles
Operational
Training
Disposal
War reserve
Experimental
Production
Not Required in Temporary Storage
Notes: Main idea/objective for slide:
Introduce and explain the several types of ammunition stockpiles, their usefulness and where they may be used.
What the instructor should cover (in addition to slide content)
IATG 03.10 – Inventory Management. http://data.unsaferguard.org/iatg/en/IATG-03.10-Inventory-management-IATG-V.3.pdf
Operational ammunition and explosives:
  The ammunition and explosives necessary to support the routine operations of military, police and other security agencies over an agreed period of time.
Training ammunition and explosives:
  The ammunition and explosives necessary to support the routine training of military, police and other security agencies. This will usually be an agreed percentage of the war reserve holdings. 15% would not be unreasonable, dependent on the training activities and frequency.
Ammunition and explosives awaiting disposal:
  The ammunition and explosives that have been identified as unserviceable, unstable or surplus to requirements.
Not used in Temporary Storage, but explain to participants to provide context:
War reserve ammunition and explosives:
  The ammunition and explosives necessary to support the operations of military, police and other security agencies during external conflict or general war over an agreed period of time. 30 days at intensive expenditure rates is often used as the time period.
Experimental ammunition and explosives:
  This type of ammunition is usually only held by those nations with a research, development and production capability. These holdings will be minimal, but must be included for intellectual accuracy.
Production ammunition:
  This type of ammunition is usually only held by those nations with a production capability. The ammunition and explosives that have been produced and are awaiting sale under the control of the manufacturer. These may be available to the military during general war but would not form part of the war reserve as their availability cannot be guaranteed.

## Slide 15: Unit of Space & Stacks
Unit of Space (UOS):
  the volume of most pallets equate to one cubic metre, with an average weight of 1 tonne
  Dependant on the size and type of ammunition
Used to calculate the total space available in an Explosive Storehouse (ESH) or ammunition container
Stack:
  The total volume of ammunition occupying the UOS space
1 x UOS
Stack
Notes: Main idea/objective for slide:
Provide the participants with the definition of a stack and 'Unit Of Space'
What the instructor should cover (in addition to slide content)
It is generally assumed for planning purposes that the volume of most pallets or unit load containers equate to one cubic metre, with an average weight of 1 tonne.
This approach simplifies ammunition storage planning, as the number of UOS within an explosive storehouse may be easily calculated by a simple volume measurement.
A small amount of space can be deducted to allow for:
  the maximum safe stacking height for the ammunition
  aisles wide enough for the type of mechanical handling equipment being used [not likely to be used in Ammunition Containers]
  a 500mm air gap from the front wall of the ESH to ammunition stacks; and [may be less in Ammunition Containers]
  a 500mm air gap between the exterior walls of the ESH and the ammunition stacks. [may be less in Ammunition Containers]
References/further reading
IATG 03.10 – Inventory Management

## Slide 16: Unit of Space & Stacks
16 x UOS
Notes: Main idea/objective for slide:
Introduce and explain the Unit of Space concept and provide an example floor plan or model that demonstrates this concept.
What the instructor should cover (in addition to slide content)
References/further reading
IATG 03.10 – Inventory Management

## Slide 17: Stack Tally Cards
Ammunition Stack Tally Card |  |  |  |  |  |  | 
IATG Form 03.10 |  |  |  |  |  |  | 
ESH |  | 3 |  | ADAC |  | 34638-27C | 
Ammunition Type |  | Shell 155mm HE L15 |  | Lot/Batch |  | GD 0215 217 | 
Condition Code |  | A2 |  | Remarks |  | For Operational use only | 
Date | Issue/Receipt Voucher Number | Received | Issued | Balance | Signature | Name | Grid Locator Reference
03/02/16 | RV 16/0021 | 1,036 |  | 1,036 | Insert signature | Verity | B4,B5,B6, C5 to C11
07/04/16 | Stock check |  |  | 1,036 | Ditto | Booth | B4,B5,B6, C5 to C11
09/05/16 | IV 16/0154 |  | 220 | 816 | Ditto | Verity | B4,B5,B6, C5 to C9
15/06/16 | RV 16/0102 | 96 |  | 912 | Ditto | Root | B4,B5,B6, C5 to C10
29/06/16 | Stock check |  |  | 912 | Ditto | Booth | B4,B5,B6, C5 to C10
See Hand-Out
Notes: Main idea/objective for slide:
Introduce participants to the use of stack tally cards.
What the instructor should cover (in addition to slide content)
Give a hand out of a Stack tally Card to participants, IATG 03.10 – Inventory Management, Page 12
The use of stack tally cards is an effective measure that supports accurate ammunition accounting, assists in stock taking and deters theft.
Each stack of ammunition should have a tally card(s) attached to it that records the following information for that particular stack.
Stack tally cards should be placed in plastic envelopes or suitable substitutes to prevent deterioration of the forms and to protect them from moisture.
When the form is completed, or the last lot or batch of that particular ammunition has been issued, then the stack tally card should be kept for at least two years by the ammunition depot's stock taking department.
This allows future reconciliation of ammunition accounts should a discrepancy occur in the future during stock taking or audit.
A stack tally card should record the following information:
Grid locator reference to identify where in the building or area it is
The Explosive Storehouse (ESH) number or other site identification number
Full description of ammunition
Ammunition Descriptive Asset Codes (ADAC) number or similar asset code system
Lot and/or batch number, (a separate card should be used for each lot and/or batch number)
Ammunition condition code, eg 'serviceable', 'constrained'
A record of transactions for that stack by quantity, lot/batch number and date
The issue or receipt voucher reference for each transaction.
References/further reading
IATG 03.10 – Inventory Management, Page 12

## Slide 18
What can happen if you do not manage your ammunition correctly?
What are the risks?
Notes: Main idea/objective for slide:
Discuss with the class the requirement to accurately account for ammunition and explosives and highlight its benefits.
What the instructor should cover (in addition to slide content)
Using a whiteboard ask the participants to list the:
possible negative effects of implementing poor or no accounting activities
The benefits of good ammunition management practices
References/further reading
IATG 03.10 – Inventory Management
Ammunition is an expensive commodity which could be regarded as an ‘insurance’ policy for the nation. It is hoped that it will never be needed, but long production lead times and national security commitments mean that it must be procured in advance in order that it is available on demand. This all comes at a cost which means that the inventory management systems should not only be capable of accounting for ammunition in great detail to support explosive safety but should also be designed to ensure that best ‘value for money’ is obtained from the ammunition.
Ammunition and explosives may deteriorate more rapidly or become damaged unless they are correctly stored, handled and transported, with the resultant effect that they may fail to function as designed and may become dangerous in storage, handling, transport and use. An accurate assessment of a munition’s life is of paramount importance in terms of safety, performance and cost.
Effective inventory management is an important component in a national authority's ‘Duty of Care’ to ensure that only ammunition that is serviceable and safe to use is issued to security agencies for both training and operational use. There is also a ‘Duty of Care’ to protect the civilian population in the local areas around explosive storage areas with appropriate quantity distances based on accurate net explosives weight of stocks.
The ability to rapidly detect inadvertent inaccuracy in accounting, loss of, theft from or diversion from the national stockpile is also a key control measure of effective stockpile management. Ineffective stock accounting systems significantly increase the risk of proliferation.

## Slide 19
Inspections, Faults and Restrictions of Ammunition
Notes: Phase 2. Development (Time allocation - 150 min)
Stage 2 (Time allocation 50 mins) – Inspections, Faults and Restrictions of Ammunition

## Slide 20: Normal Types of Inspections
There are two types of inspection carried out on Temporary Ammunition Storage Sites.
Internal. Using T/PCC staff as a routine daily task:
  Check that a continuous, logged, monitoring regime exists to assess the condition of each PES, the ammunition contained within, and the overall Temporary Ammunition Storage Site
  Ensure the Explosive Limits Licences are being observed.
  Inspections are recorded in an Inspection Record Sheet
External. Using staff from WAAB or other UN/TCN authority:
  To ensure continued safe storage, processing and use of explosives in compliance with UN/TCN regulations
  Provide a grading of Satisfactory or Unsatisfactory
Notes: Main idea/objective for slide:
Discuss with the class the requirement to accurately account for ammunition and explosives and highlight its benefits.
What the instructor should cover (in addition to slide content)
Emphasise the importance, seriousness and necessity for inspections.
References/further reading
United Nations Manual of Ammunition Management, 2020 1st Ed
Since ammunition contains high energy material and is designed to be as lethal as possible, it is highly desired that it is safe, reliable and effective during operation, transportation and handling.
Therefore, inspections and evaluations shall be carried out to ensure that ammunition policy/guidelines are adhered to by units.
Evaluation and recommendations shall be done to improve the standard of ammunition management in units
The SATO shall carry out the following types of inspection in the units:
  Annual Routine Inspection as per a circulated program;
  The SATO or another ATO shall accompany the COE team to the Operational Readiness Inspection for each unit;
  An inspection carried out on units upon arrival and repatriation;
  Any other inspection as appeared/requested by the concerned unit;
  The SATO shall have the authority to conduct impromptu inspections at any time.
  The SATO may be unable to attend all inspections for all T/PCCs. Each unit shall be inspected at a minimum of once a year.
An internal inspection shall be carried out by the T/PCC person in charge of ammunition storage (or a nominated and qualified representative), normally from the military/police unit occupying the camp, to ensure that:
  There is a continuous recording/logging and monitoring regime to ascertain the condition of each PES, the stockpile contained within and the overall ammunition storage area;
  There is a PES log book with temperature and humidity records;
  The firefighting equipment is working, and drills are conducted;
  The security alarm is working.
The results of the inspection shall be recorded on an inspection record sheet. A copy of these inspection records shall be sent to the SATO.
IATG 06.70 will be adhered to during inspection for consultation. A standard Inspection Criteria/Evaluation Template is attached to this manual at Annex C
The SATO or his/her appropriate representative is authorized to carry out inspection of ammunition and evaluation of units as per this manual.
  Details regarding the competency and responsibility of SATO are given at Annex D.
After the inspection is carried out, the SATO shall furnish an inspection and evaluation report on the ammunition storage conditions of the concerned unit.
  The reports shall be shared with all members of the WAAB and approved during the next WAAB meeting.
  The chair of the WAAB shall be informed without delay when the minimum standards cannot be met.
  Copies of the approved report shall be disseminated to all concerned for appropriate action
IATG 06.70 – Inspection of explosives facilities
As per slide

## Slide 21: Other types of Inspections for national ammunition storage
Follow-up inspections
Specialist inspections
Small unit inspections
Suspended or withdrawn licences
Deployed Units
Notes: Main idea/objective for slide:
Discuss the several types of internal and external inspections highlighting key areas to focus attention and the hazards to look out for.
What the instructor should cover (in addition to slide content)
Explain how these additional inspection may occur from time to time and the conditions that may cause them to arise.
References/further reading
United Nations Manual of Ammunition Management, 2020 1st Ed
IATG 06.70 – Inspection of explosives facilities

## Slide 22: UN Mission Types of Inspections
The SATO shall carry out the following types of inspection in the units:
  • Annual Routine Inspection as per a circulated program;
  • The SATO or another ATO shall accompany the COE team to the Operational Readiness Inspection for each unit;
  • An inspection carried out on units upon arrival and repatriation;
  • Any other inspection as appeared/requested by the concerned unit;
  • The SATO shall have the authority to conduct impromptu inspections at any time.
  • The SATO may be unable to attend all inspections for all T/PCCs.
  Each unit shall be inspected at a minimum of once a year.
Notes: Main idea/objective for slide:
Discuss with the class the requirement to accurately account for ammunition and explosives and highlight its benefits.
What the instructor should cover (in addition to slide content)
Emphasise the importance, seriousness and necessity for inspections.
References/further reading
United Nations Manual of Ammunition Management, 2020 1st Ed
Since ammunition contains high energy material and is designed to be as lethal as possible, it is highly desired that it is safe, reliable and effective during operation, transportation and handling.
Therefore, inspections and evaluations shall be carried out to ensure that ammunition policy/guidelines are adhered to by units.
Evaluation and recommendations shall be done to improve the standard of ammunition management in units
The SATO shall carry out the following types of inspection in the units:
  Annual Routine Inspection as per a circulated program;
  The SATO or another ATO shall accompany the COE team to the Operational Readiness Inspection for each unit;
  An inspection carried out on units upon arrival and repatriation;
  Any other inspection as appeared/requested by the concerned unit;
  The SATO shall have the authority to conduct impromptu inspections at any time.
  The SATO may be unable to attend all inspections for all T/PCCs. Each unit shall be inspected at a minimum of once a year.
An internal inspection shall be carried out by the T/PCC person in charge of ammunition storage (or a nominated and qualified representative), normally from the military/police unit occupying the camp, to ensure that:
  There is a continuous recording/logging and monitoring regime to ascertain the condition of each PES, the stockpile contained within and the overall ammunition storage area;
  There is a PES log book with temperature and humidity records;
  The firefighting equipment is working, and drills are conducted;
  The security alarm is working.
The results of the inspection shall be recorded on an inspection record sheet. A copy of these inspection records shall be sent to the SATO.
IATG 06.70 will be adhered to during inspection for consultation. A standard Inspection Criteria/Evaluation Template is attached to this manual at Annex C
The SATO or his/her appropriate representative is authorized to carry out inspection of ammunition and evaluation of units as per this manual.
  Details regarding the competency and responsibility of SATO are given at Annex D.
After the inspection is carried out, the SATO shall furnish an inspection and evaluation report on the ammunition storage conditions of the concerned unit.
  The reports shall be shared with all members of the WAAB and approved during the next WAAB meeting.
  The chair of the WAAB shall be informed without delay when the minimum standards cannot be met.
  Copies of the approved report shall be disseminated to all concerned for appropriate action
IATG 06.70 – Inspection of explosives facilities
As per slide

## Slide 23: UN Mission Types of Inspections
Internal inspections
An internal inspection shall be carried out by the T/PCC person in charge of ammunition storage (or a nominated and qualified representative), normally from the military/police unit occupying the camp, to ensure that:
There is a continuous recording/logging and monitoring regime to ascertain the condition of each PES, the stockpile contained within and the overall ammunition storage area;
There is a PES logbook with temperature and humidity records;
The firefighting equipment is working, and drills are conducted;
The security alarm is working.
The results of the inspection shall be recorded on an inspection record sheet. A copy of these inspection records shall be sent to the SATO.
Notes: Main idea/objective for slide:
Discuss with the class the requirement to accurately account for ammunition and explosives and highlight its benefits.
What the instructor should cover (in addition to slide content)
Emphasise the importance, seriousness and necessity for inspections.
References/further reading
United Nations Manual of Ammunition Management, 2020 1st Ed
Since ammunition contains high energy material and is designed to be as lethal as possible, it is highly desired that it is safe, reliable and effective during operation, transportation and handling.
Therefore, inspections and evaluations shall be carried out to ensure that ammunition policy/guidelines are adhered to by units.
Evaluation and recommendations shall be done to improve the standard of ammunition management in units
The SATO shall carry out the following types of inspection in the units:
  Annual Routine Inspection as per a circulated program;
  The SATO or another ATO shall accompany the COE team to the Operational Readiness Inspection for each unit;
  An inspection carried out on units upon arrival and repatriation;
  Any other inspection as appeared/requested by the concerned unit;
  The SATO shall have the authority to conduct impromptu inspections at any time.
  The SATO may be unable to attend all inspections for all T/PCCs. Each unit shall be inspected at a minimum of once a year.
An internal inspection shall be carried out by the T/PCC person in charge of ammunition storage (or a nominated and qualified representative), normally from the military/police unit occupying the camp, to ensure that:
  There is a continuous recording/logging and monitoring regime to ascertain the condition of each PES, the stockpile contained within and the overall ammunition storage area;
  There is a PES log book with temperature and humidity records;
  The firefighting equipment is working, and drills are conducted;
  The security alarm is working.
The results of the inspection shall be recorded on an inspection record sheet. A copy of these inspection records shall be sent to the SATO.
IATG 06.70 will be adhered to during inspection for consultation. A standard Inspection Criteria/Evaluation Template is attached to this manual at Annex C
The SATO or his/her appropriate representative is authorized to carry out inspection of ammunition and evaluation of units as per this manual.
  Details regarding the competency and responsibility of SATO are given at Annex D.
After the inspection is carried out, the SATO shall furnish an inspection and evaluation report on the ammunition storage conditions of the concerned unit.
  The reports shall be shared with all members of the WAAB and approved during the next WAAB meeting.
  The chair of the WAAB shall be informed without delay when the minimum standards cannot be met.
  Copies of the approved report shall be disseminated to all concerned for appropriate action
IATG 06.70 – Inspection of explosives facilities
As per slide

## Slide 24: Inspections – Deployed Units
SATO will conduct inspections as outlined below
Type of licence | Inspection Frequency | Remarks
Standard | Annually | Deployed units are unlikely to hold one of these licences
Non- Standard | Twice Annually | 
Range | Twice Annually | 
 | Annually | For these units holding only small arms ammunition
SATO Inspections as per the UN MAM will be covered in a later lesson
Notes: Main idea/objective for slide:
Discuss the several types of internal and external inspections highlighting key areas to focus attention and the hazards to look out for.
What the instructor should cover (in addition to slide content)
Check the participants understanding of Standard and Non-Standard Licences – Clarify if needed
References/further reading
United Nations Manual of Ammunition Management, 2020 1st Ed
IATG 12.10 – Ammunition on multi-national operations
The efficiency of the unit in relation to its ammunition responsibilities should, on completion of each periodic inspection, be graded in terms of Satisfactory or Unsatisfactory.
The grading shall be based on the standard found at the time of the inspection and give an accurate picture of the efficiency of the unit.
Small infringements may be corrected as the inspection proceeds but a general comment observing this is to be recorded in the report.
Subsequent corrective action may be taken as necessary to correct faults and bring the unit up to an acceptable standard.
Accurate reporting is essential to give the chain of command a clear and unambiguous view of ammunition and explosives safety across their area.
This grading shall be recorded on IATG Form 12.10A (see Annex D) (or national equivalent) by the Inspector.
When assessing the grading of a unit’s efficiency, the Inspector should base his or her judgement on the points listed in IATG 06.70 Inspection of explosives facilities, Annex E.
An unsatisfactory grading should only be given if:
  there is more than one violation of a major point which is considered to compromise explosive safety;
  there are four or more minor points violated and no corrective action has been taken during the inspection; or
  Recommendations to resolve a major point or two minor points specified in a previous inspection report have not been carried out.
The Inspector shall also recommend if more specialist inspections are warranted, (e.g. electrical, lightning protection, infrastructure stability etc).
A recommended report format for deployed unit ammunition inspections is at Annex D for information

## Slide 25: Potential Explosion Site Logbooks
Each PES should maintain a logbook to record the results of the internal inspections
  Temperature and humidity readings
  Firefighting equipment, alarms and drills
  Security and physical protection, such as barricades
This logbook should be regularly inspected by the Contingent Commander to ensure that it is being completed properly
  Every 3 months at least
Each PES should also have a temperature and humidity record sheet
Notes: Main idea/objective for slide:
Discuss the necessity for Logbooks at each Potential Explosion Site and the merits of maintaining these logs to a high standard.
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 06.70 – Inspection of explosives facilities
Immediate firefighting appliances (IFFA), including fire beaters, pre-positioned engines and motor driven pumps, hose reels and hydrants, should be inspected by the head of the establishment at intervals specified by the head of the establishment or in the case of equipment, by the manufacturer’s recommendations. IFFA inspections shall be recorded.
Fire alarm systems shall be maintained in accordance with IATG 02.50 Fire safety and the manufacturer’s recommendations. Electrical fire alarm systems should be tested weekly and the test recorded.. All alarm points should be tested during any three-month period.
Details shall be recorded on the reverse of the inspection record sheet for the PES concerned whenever fire or escape drills are practised. Completion of any actions required by the post drill recommendations is also to be recorded. Drills for the whole storage site are to be recorded on the site inspection record sheet.
Security alarms should be inspected and tested regularly. Where specific guidance is not available, the alarms should be tested for serviceability at weekly intervals such that all alarm activation points are tested within a three-month period.
Where fitted, public address systems should be tested in accordance with IATG 05.40 Safety standards for electrical installations. If no specific guidance is available, a weekly test broadcast should be made.
To complement the logbook, each PES should also have a temperature and humidity record sheet

## Slide 26: PES Logbook - Example
See Handout
Notes: Main idea/objective for slide:
Share an example of a Potential Explosion Site logbook.
What the instructor should cover (in addition to slide content)
Provide the PES Logbook as a Handout and explain each page and how it is completed (Record of Checks and Tests)
References/further reading:
IATG 06.70 – Inspection of explosives facilities - Annex C
The following check list of inspection points and records of checks and tests may be used to maintain records

## Slide 27: PES Logbook - Example
See Handout
Notes: Main idea/objective for slide:
Share an example of a Potential Explosion Site logbook.
What the instructor should cover (in addition to slide content)
Provide the PES Logbook as a Handout and explain each page and how it is completed (Fault Reports)
References/further reading:
IATG 06.70 – Inspection of explosives facilities - Annex C

## Slide 28: PES Logbook - Example
See Handout
Notes: Main idea/objective for slide:
Share an example of a Potential Explosion Site logbook.
What the instructor should cover (in addition to slide content)
Provide the PES Logbook as a Handout and explain each page and how it is completed (Fire Evacuation and Drills)
References/further reading:
IATG 06.70 – Inspection of explosives facilities - Annex C

## Slide 29: Temperature and Humidity Record - Example
See Handout
Notes: Main idea/objective for slide:
Share an example of a Temperature and Humidity Record.
What the instructor should cover (in addition to slide content)
Provide the PES Logbook as a Handout and explain each page and how it is completed (Temperature and Humidity Records)
References/further reading:
IATG 06.70 – Inspection of explosives facilities - Annex D
As per slide

## Slide 30: Inspection Reports
Inspectors comments
Previous Reports (Fire, Security etc)
Explosive Licensing and Safeguarding Maps
Ammunition Accounts
Standard Operating Procedures
Condition of Store
Condition of Ammunition
Closing Remarks
See Handout
IATG 12.10 Annex D
UN MAM Annex C
Notes: Main idea/objective for slide:
Share an example of an Inspection Report
What the instructor should cover (in addition to slide content)
Provide a handout of an example Inspection Report, IATG 12.10 – Ammunition on multi-national operations. Annex D
Provide a handout of example Inspection Report, UNMAM Annex & Annex C appendix 1
Explain similar but different layouts and content.
References/further reading:
United Nations Manual of Ammunition Management, 2020 1st Ed
Since ammunition contains high energy material and is designed to be as lethal as possible, it is highly desired that it is safe, reliable and effective during operation, transportation and handling.
Therefore, inspections and evaluations shall be carried out to ensure that ammunition policy/guidelines are adhered to by units.
Evaluation and recommendations shall be done to improve the standard of ammunition management in units
The SATO shall carry out the following types of inspection in the units:
  Annual Routine Inspection as per a circulated program;
  The SATO or another ATO shall accompany the COE team to the Operational Readiness Inspection for each unit;
  An inspection carried out on units upon arrival and repatriation;
  Any other inspection as appeared/requested by the concerned unit;
  The SATO shall have the authority to conduct impromptu inspections at any time.
  The SATO may be unable to attend all inspections for all T/PCCs. Each unit shall be inspected at a minimum of once a year.
An internal inspection shall be carried out by the T/PCC person in charge of ammunition storage (or a nominated and qualified representative), normally from the military/police unit occupying the camp, to ensure that:
  There is a continuous recording/logging and monitoring regime to ascertain the condition of each PES, the stockpile contained within and the overall ammunition storage area;
  There is a PES log book with temperature and humidity records;
  The firefighting equipment is working, and drills are conducted;
  The security alarm is working.
The results of the inspection shall be recorded on an inspection record sheet. A copy of these inspection records shall be sent to the SATO.
IATG 06.70 will be adhered to during inspection for consultation. A standard Inspection Criteria/Evaluation Template is attached to this manual at Annex C
The SATO or his/her appropriate representative is authorized to carry out inspection of ammunition and evaluation of units as per this manual.
  Details regarding the competency and responsibility of SATO are given at Annex D.
After the inspection is carried out, the SATO shall furnish an inspection and evaluation report on the ammunition storage conditions of the concerned unit.
  The reports shall be shared with all members of the WAAB and approved during the next WAAB meeting.
  The chair of the WAAB shall be informed without delay when the minimum standards cannot be met.
  Copies of the approved report shall be disseminated to all concerned for appropriate action
IATG 12.10 – Ammunition on multi-national operations. Annex D. http://data.unsaferguard.org/iatg/en/IATG-12.10-Multi-national-operations-IATG-V.3.pdf
The efficiency of the unit in relation to its ammunition responsibilities should, on completion of each periodic inspection, be graded in terms of Satisfactory or Unsatisfactory.
The grading shall be based on the standard found at the time of the inspection and give an accurate picture of the efficiency of the unit.
Small infringements may be corrected as the inspection proceeds but a general comment observing this is to be recorded in the report.
Subsequent corrective action may be taken as necessary to correct faults and bring the unit up to an acceptable standard.
Accurate reporting is essential to give the chain of command a clear and unambiguous view of ammunition and explosives safety across their area.
This grading shall be recorded on IATG Form 12.10A (see Annex D) (or national equivalent) by the Inspector.
When assessing the grading of a unit’s efficiency, the Inspector should base his or her judgement on the points listed in IATG 06.70 Inspection of explosives facilities, Annex E.
An unsatisfactory grading should only be given if:
  there is more than one violation of a major point which is considered to compromise explosive safety;
  there are four or more minor points violated and no corrective action has been taken during the inspection; or
  Recommendations to resolve a major point or two minor points specified in a previous inspection report have not been carried out.
The Inspector shall also recommend if more specialist inspections are warranted, (e.g. electrical, lightning protection, infrastructure stability etc).
A recommended report format for deployed unit ammunition inspections is at Annex D for information

## Slide 31: Explosive Storehouse Inspection Checklist:
IATG 06.70 Annex F
Notes: Main idea/objective for slide:
Show participants an example Explosive Storehouse Inspection Checklist and give a brief overview to the participants how to complete this
What the instructor should cover (in addition to slide content)
Provide a handout of a sample ESH Inspection Checklist and walk the participants through the various headings.
Print IATG 06.70 Annex C. & UNMAM Annex C, 1 copy per student
References/further reading:
IATG 06.70 – Inspection of explosives facilities - Annex F. http://data.unsaferguard.org/iatg/en/IATG-06.70-Inspection-explosives-facilities-IATG-V.3.pdf

## Slide 32: Definitions
Standard terminology helps us report problems and enable solutions to be implemented.
Incident:
  “a generic term that includes all accidents, performance failures and faults involving ammunition or where ammunition is present.”
Notes: Main idea/objective for slide:
Describe and explain the following definitions giving examples in each case: ammunition accident; blind; misfire; fault; incident; and performance failure.
What the instructor should cover (in addition to slide content)
Ask the participants to define an incident before showing this slide
References/further reading:
IATG 01.60 – Ammunition faults and performance failures

## Slide 33: Definitions
Ammunition Accident:
  "…any incident involving ammunition or explosives that results in, or has potential to result in, death or injury to a person(s) and/or damage to equipment and/or property, military or civilian.”
Notes: Main idea/objective for slide:
Describe and explain the following definitions giving examples in each case: ammunition accident; blind; misfire; fault; incident; and performance failure.
What the instructor should cover (in addition to slide content)
Ask the participants to define an Ammunition Accident before showing this slide
References/further reading:
IATG 01.60 – Ammunition faults and performance failures. http://data.unsaferguard.org/iatg/en/IATG-01.60-Ammunition-faults-performance-failures-IATG-V.3.pdf

## Slide 34: Definitions
Blind:
  “ammunition, which, though initiated, has failed to arm as intended or which has failed to explode after being armed.”
  Or alternatively:
  “an explosives item that fails to function correctly after initiation.”
Notes: Main idea/objective for slide:
Describe and explain the following definitions giving examples in each case: ammunition accident; blind; misfire; fault; incident; and performance failure.
What the instructor should cover (in addition to slide content)
Ask the participants to define a blind before showing this slide
Primer has been struck, mortar has launched and impacted ground but has not functioned as designed.
References/further reading:
IATG 01.60 – Ammunition faults and performance failures

## Slide 35: Definitions
Fault:
  “any error in the make-up and/or marking and/or deterioration in the physical state of the ammunition, explosives, ammunition packages or ammunition containers.”
Notes: Main idea/objective for slide:
Describe and explain the following definitions giving examples in each case: ammunition accident; blind; misfire; fault; incident; and performance failure.
What the instructor should cover (in addition to slide content)
Ask the participants to define a fault before showing this slide
Rust has appeared on the body of the projectile.
References/further reading:
IATG 01.60 – Ammunition faults and performance failures

## Slide 36: Definitions
Misfire:
“ammunition which, when initiated, fails to fire or launch as intended”
Notes: Main idea/objective for slide:
Describe and explain the following definitions giving examples in each case: ammunition accident; blind; misfire; fault; incident; and performance failure.
What the instructor should cover (in addition to slide content)
Ask the participants to define a misfire before showing this slide
References/further reading:
IATG 01.60 – Ammunition faults and performance failures

## Slide 37: Definitions
Performance Failure:
  the failure of the ammunition or any of its constituent parts, including the explosives, to function as designed.
  Blinds and misfires are included within performance failures
Notes: Main idea/objective for slide:
Describe and explain the following definitions giving examples in each case: ammunition accident; blind; misfire; fault; incident; and performance failure.
What the instructor should cover (in addition to slide content)
Ask the participants to define a performance failure before showing this slide
References/further reading:
IATG 01.60 – Ammunition faults and performance failures

## Slide 38: Reporting and Documenting
All faults or performance failures should be immediately reported by users and appropriately investigated.
If any damage or injury has occurred, no matter how minor, the event shall be reported as an ammunition accident.
Notes: Main idea/objective for slide:
Highlight the need to report and document each of these events accurately and how to complete the reporting procedure.
What the instructor should cover (in addition to slide content)
Ask the participants why it is essential to report and document faults or failures. What might happen if we do not?
References/further reading:
IATG 01.60 – Ammunition faults and performance failures
As a fundamental preventative measure to support safe conventional ammunition stockpile management, any faults or performance failures should be immediately reported by users and appropriately investigated in order that the appropriate action can be taken to prevent reoccurrences. Such actions may include:
  the revision of operating systems and procedures;
  the imposition of a ban on the use, storage, handling, transport or disposal of the ammunition type involved;
  after investigation, the imposition of constraints on the use, storage, handling, transport or disposal of the ammunition type involved;
  rectification of the fault by repair; or
  withdrawal of the ammunition from service use.
This will require that an appropriate investigating authority is nominated, staffed and resourced. Therefore, ammunition stockpile management organisations should nominate an appropriate investigating authority and ensure that it is provided with the technically qualified staff and resources that are necessary to provide an effective and efficient capability in this area.
It should be a mandatory requirement for users or stock-holding units to report any ammunition faults or performance failures to the investigating authority. All incidents of this type should be reported, and users or stock-holding units shall not make the decision that incidents are minor or not worth reporting.
If any damage or injury has occurred, no matter how minor, the event shall be reported as an ammunition accident in line with the requirements of IATG 11.10 Ammunition accidents, reporting and investigation.

## Slide 39: Ammunition Incident reporting Form
See Handout
Notes: Main idea/objective for slide:
Highlight the need to report and document each of these events accurately and how to complete the reporting procedure.
What the instructor should cover (in addition to slide content)
Discuss each heading of the Incident Form with the participants and ensure they understand the need for this information
Provide a handout of this Form to the participants
References/further reading:
IATG 01.60 – Ammunition faults and performance failures, Annex C
The organisation responsible for the stockpile management of conventional ammunition should ensure that a system of reporting and investigating ammunition fault and performance failures is developed, promulgated to all users and is then effectively used.
Users should be instructed to immediately report the following information on an ammunition fault or performance failure to the appropriate investigating authority

## Slide 40: Definitions: Ban and Constraints
Ban
“a moratorium placed on the issue and use of ammunition, usually pending technical investigation.”
Constraint
“the imposition of a limitation or restriction in the use, transportation, carriage, issue, storage or inspection of a munition.”
Notes: Main idea/objective for slide:
Provide the definitions of a Ban and a Constraint in terms of ammunition management.
What the instructor should cover (in addition to slide content)
Ask the participants to explain the difference between a Ban and a Constraint before showing this slide
References/further reading:
IATG 01.70 – Bans and Constraints. http://data.unsaferguard.org/iatg/en/IATG-01.70-Bans-constraints-IATG-V.3.pdf
The aim of a formal system of bans and constraints, instigated by a conventional ammunition stockpile management organisation, should be to ensure:
  the safety of personnel during the use, storage, handling, transportation or disposal of conventional ammunition;
  the optimum use of the conventional ammunition stockpile, which is an expensive national asset; and
  the controlled issue and use of specific or generic conventional ammunition during times of shortages.

## Slide 41: Rationale for a Ban
A ban should be imposed to prevent the issue or use of conventional ammunition under the following circumstances:
When it is suspected of being the cause of an ammunition accident, irrespective of whether death or injury has been caused;
When there have been excessive performance failures;
When a defect, which could compromise safety, has been discovered; or
When the ammunition is to be withdrawn at the end of its serviceable life.
Notes: Main idea/objective for slide:
Discuss the differences between a Ban and a Constraint and outline the actions to be carried out when these terms have been applied to ammunition.
What the instructor should cover (in addition to slide content)
Explain why it is necessary to apply a Ban in these cases.
References/further reading:
IATG 01.70 – Bans and Constraints

## Slide 42: Action on notification of a Ban
Mark the ammunition packaging or container with the following information:
  ‘NOT FOR ISSUE OR USE’
  the ban serial number
  any special instructions received with the ban.
Enter the details of the ban in the user’s ammunition account
If instructed to do so, arrange for the ammunition to be transported to the designated ammunition demilitarisation or destruction organisation.
Notes: Main idea/objective for slide:
Discuss the differences between a Ban and a Constraint and outline the actions to be carried out when these terms have been applied to ammunition.
What the instructor should cover (in addition to slide content)
Write the steps for notifying a Ban on ammuntion onto a white board
References/further reading:
IATG 01.70 – Bans and Constraints

## Slide 43: Rationale for a Constraint
Constraints are the imposition of a limitation or restriction in the use, transportation, carriage, issue, storage or inspection of munitions.
These may include:
  storage temperatures to be adhered to
  special handling requirements;
  a decision that ammunition is for training use only
  a change of shelf-life parameters.
Notes: Main idea/objective for slide:
Discuss the differences between a Ban and a Constraint and outline the actions to be carried out when these terms have been applied to ammunition.
What the instructor should cover (in addition to slide content)
Explain why it is necessary to apply a Constraint in these cases.
References/further reading:
IATG 01.70 – Bans and Constraints
Constraints (which may be at generic type, lot, batch and/or serial number level) are the imposition of a limitation or restriction in the use, transportation, carriage, issue, storage or inspection of munitions.
Constraints should be used as a tool for the ammunition management system.
They normally remain in force for the life of ammunition, while a ban can be a short-term measure.
Details of the constraints shall be printed on the ammunition issue vouchers, and a note shall be made on the ammunition account sheet of any constraints.
Constraints on the use, storage, handling, transportation or disposal of ammunition may include:
  storage temperatures to be adhered to;
  special handling requirements;
  a decision that ammunition is for training use only; and
  a change of shelf life parameters.

## Slide 44: Action on notification of a Constraint
Mark the ammunition packaging or container with the following information:
  the constraint serial number
  details of the constraint.
Enter the details of the constraint in the user’s ammunition account.
Notes: Main idea/objective for slide:
Discuss the differences between a Ban and a Constraint and outline the actions to be carried out when these terms have been applied to ammunition.
What the instructor should cover (in addition to slide content)
Write the steps for notifying a Constraint on ammuntion onto a white board
References/further reading:
IATG 01.70 – Bans and Constraints

## Slide 45
Participant Exercise
Notes: Phase 2. Development (Time allocation - 150 min)
Stage 3 (Time allocation 50 mins) – participant Exercise

## Slide 46: Exercise
Using the ESH Inspection Checklist (both types) as a guide, make comments on the following images:
Include comments on:
  Type and condition of storage containers/buildings
  Firefighting capability and signage
  Hazards identified in the area
  The storage of ammunition within the stores
  Access and physical security of the storage area
  Condition of barricades
  Cleanliness and health & safety management
Be prepared to back brief to the class on your findings
Notes: Main idea/objective for slide:
participant Exercise to identify hazards, recommend mitigations and complete ESH Inspection Matrix
participant Activity
Using a series of images of a Temporary Storage Area and its stockpiles, ask the syndicate groups to conduct visual inspections of the images and complete the ESH Inspection Checklist (as provided as a handout during the lesson at Slide 28) for each Stockpile or storehouse.
participants must identify the hazards and make recommendations to mitigate the risks of these hazards.
What the instructor should cover (in addition to slide content)
Instructors are to move around the class and help participants where required. participants may work in groups .
When complete, work through the answers with the class and ask questions.

## Slide 47: Lesson overview
Recall and discuss UN good practices for securing hazardous explosive materials and managing an explosive storage site
Discuss Storage Temperatures and the isolation & segregation of ammunition stocks
Discuss the Stacking and Racking of ammunition and the use of Stack Tally Cards
Discuss Lotting & Batching, the use of Bans & Constraints and determining Faults & Performance failures
Apply checks and inspections to provide confidence that Explosive Storage sites conform to UN and international standards
Examine the use of mitigations based on an explosive risk assessment for a temporary storage area
Notes: Phase 3. Consolidation (Time allocation - 10 min)
Main idea/objective for slide:
Recap Key Learning Points
participant activity
Give participants opportunity to ask any questions
What the instructor should cover (in addition to slide content)
Key Learning Points
2.2.5.1 Recall UN good practices for securing hazardous explosive materials
2.2.5.2 Recall UN good practices for managing an explosive storage site
2.2.5.3 Recall the requirements for the Calculation of Storage Space
2.2.5.4 Discuss the use of checks and inspections in ammunition management
2.2.5.5 Discuss the UN good practices for securing hazardous explosive materials
2.2.5.6 Discuss the UN good practices for managing an explosive storage site
2.2.5.7 Discuss Storage Temperatures and the isolation & segregation of ammunition stocks
2.2.5.8 Discuss the Stacking and Racking of ammunition and the use of Stack Tally Cards
2.2.5.9 Discuss Lotting & Batching, the use of Bans & Constraints and determining Faults & Performance failures
2.2.5.10 Apply checks and inspections to provide confidence that Explosive Storage sites conform to UN and international standards
2.2.5.11 Examine the use of mitigations based on an explosive risk assessment for a temporary storage area

## Slide 48
Weapons and Ammunition Management in UN Peace Operations
Look Ahead: Explosive Risk Assessment
Notes: Main idea/objective for slide:
Look ahead to the next lesson of the course:
  Explosive Risk Assessment