## Slide 1
Weapons and Ammunition Management in UN Peace Operations
Explosive Risk Assessment
Notes: Key Reference Documents for this lesson:
UN Manual on Ammunition Management
UN Weapons and Ammunition Management Policy (WAM)
International Ammunition Technical Guidelines (IATG)
http://data.unsaferguard.org/iatg/en/IATG-02.10-Introduction-risk-management-IATG-V.3.pdf
All photographs in this lesson are © United Nations unless otherwise stated.

## Slide 2: Objective
Develop an Explosive Risk Assessment
Notes: Main idea/objective for slide:
Phase 1. Introduction - Introduce the objectives of the lesson.
(Enabling Objective: 2.2.6 Develop an Explosive Risk Assessment.)
What the instructor should cover (in addition to slide content)
By the end of this training session the participant will compile an Explosive Risk Assessment.

## Slide 3: Lesson overview
Recall the hazards and mitigations associated with ammunition management
Discuss the UN Explosive Risk Assessments process
Examine how to identify, control and report risks associated with explosives
Compile an Explosive Risk Assessment
Notes: Main idea/objective for slide:
Introduce the Key Learning Points
What the instructor should cover (in addition to slide content)
Emphasise ‘recall’ – this is revisiting/revising content covered in the workbook
Key Learning Points
2.2.6.1 Recall the hazards associated with ammunition management
2.2.6.2 Recall the mitigations associated with ammunition management
2.2.6.3 Recall UN Explosive Risk Assessments process
2.2.6.4 Discuss the UN Explosive Risk Assessments process
2.2.6.5 Examine how to identify risks associated with explosives
2.2.6.6 Examine how to control risks associated with explosives
2.2.6.7 Examine how to report risks with explosives
2.2.6.8 Evaluate the Explosive Risk Assessment
2.2.6.9 Compile an Explosive Risk Assessment using supplied documentation

## Slide 4
Why we need Explosive Safety
Notes: Phase 1. Introduction (Time allocation - 10 min)

## Slide 5: What is an Explosive Event?
“…an unexpected and undesired initiation of an explosive substance or article within an ammunition depot leading to significant or catastrophic consequences.”
Notes: Main idea/objective for slide:
Discuss the concept of explosive safety and emphasise the need to manage any event that can lead to a serious consequence.
What the instructor should cover (in addition to slide content)
References/further reading
IATG 2.10 – Introduction to Risk Management Principles and Processes. http://data.unsaferguard.org/iatg/en/IATG-02.10-Introduction-risk-management-IATG-V.3.pdf

## Slide 6: What is Explosive Safety?
Ageing, unstable and excess conventional ammunition stockpiles pose the dual risks of accidental explosions at munition sites.
There is a need for a robust, effective and integrated risk management system.
Risk assessments will involve a combination of both qualitative and quantitative risk assessment methods.
Notes: Main idea/objective for slide:
Discuss the concept of explosive safety and emphasise the need to manage any event that can lead to a serious consequence.
What the instructor should cover (in addition to slide content)
References/further reading
IATG 2.10 – Introduction to Risk Management Principles and Processes
A critical element of conventional ammunition stockpile management planning and operations should be the implementation of a robust, effective and integrated risk management system, preferably in accordance with the ISO guidance.
This system should examine organisational, management, administrative and operational processes and procedures.
The physical phenomena of blast, fragmentation and thermal radiation resulting from explosions are well understood, as are the mechanisms that cause fatalities, injury and damage as a result of these effects.
As a result of this understanding a range of techniques and models have been developed by which these effects can be estimated; these techniques and models form a key element of the overall risk management process.
The term ‘estimated’ is important because the range of variables involved means that exact damage effects are unlikely to be accurately predicted; appropriate safety margins are therefore engineered into preventative measures.

## Slide 7: Concept of Explosive Safety
Safety is achieved by reducing risk to a tolerable level
There can be no absolute safety; some risk will remain:
  this is the residual risk
Notes: Main idea/objective for slide:
Discuss the concept of explosive safety and emphasise the need to manage any event that can lead to a serious consequence.
What the instructor should cover (in addition to slide content)
References/further reading
IATG 2.10 – Introduction to Risk Management Principles and Processes
In the context of conventional ammunition stockpile management the enabling processes of storage, handling, destruction etc. can never be absolutely safe; they can only be relatively safe.
This is an inevitable fact of life, which does not mean that all efforts to ensure safety are not being made.
It just means that it cannot be proved, with 100% confidence, that absolute safety is being achieved.
The risk management systems recommended in IATG, and used within the IATG software, aim to be as close to that 100% ideal confidence level as is realistically possible, whilst allowing stockpile management organisations to determine what is the tolerable risk that they are prepared to accept in their particular environments.

## Slide 8
What types of serious events can occur?
What activities would lead to these events?
Notes: Main idea/objective for slide:
Explore with the participants what types of serious events may occur with stored ammunition and explosives.
participant Activity
Ask the participants to give examples.
What the instructor should cover (in addition to slide content)
Write examples on a flipchart and post it on the wall.
References/further reading
IATG 2.10 – Introduction to Risk Management Principles and Processes
The target of conventional ammunition stock holding organisations should be the safe, effective and efficient stockpile management of conventional ammunition, explosives, propellants and pyrotechnics.
There are potential hazards in this process:
  inadequate storage conditions for conventional ammunition may result in undesired explosive events during storage;
  ineffective physical inspection and chemical analysis of ammunition as part of a technical surveillance system may result in undesired explosive events during storage due to deteriorated ammunition;
  inappropriate handling and processing of conventional ammunition has the potential to cause death or injury to workers or observers.
Additional to these hazards there are a range of potential causes of an undesirable explosive event:
  accidental fire in a vehicle, magazine or explosive storehouse;
  human error due to accident, fatigue or inappropriate handling;
  environmental (e.g. lightning strike);
  intruder initiated (e.g. sabotage); or
  enemy action (in periods of conflict) (e.g. improvised explosive device, direct or indirect fire).

## Slide 9
The Risk Management Process
Notes: Phase 2. Development (Time allocation - 160 min)
Stage 1 (Time allocation 40 mins) – The Risk Management Process

## Slide 10: Definitions:
Harm:
  “physical injury or damage to the health of people, or damage to property or the environment.”
Hazard:
  “a potential source of harm”.
Notes: Main idea/objective for slide:
Discuss the definition of Harm and Hazard, placing emphasis on the management of ammunition and explosive storage
What the instructor should cover (in addition to slide content)
References/further reading
IATG 1.20 – Introduction to Risk Management Principles and Processes. http://data.unsaferguard.org/iatg/en/IATG-02.10-Introduction-risk-management-IATG-V.3.pdf

## Slide 11: Definitions:
Risk:
“a combination of the probability of occurrence of harm and the severity of that harm.”
Risk = Likelihood x Consequence
Risk Evaluation:
  “the process based on risk analysis to determine whether the tolerable risk has been achieved”.
Notes: Main idea/objective for slide:
Discuss the definition of Risk and Risk Evaluation, placing emphasis on the management of ammunition and explosive storage
What the instructor should cover (in addition to slide content)
References/further reading
IATG 2.10 – Introduction to Risk Management Principles and Processes

## Slide 12: Definitions:
Risk Assessment:
  “The overall process comprising a risk analysis and a risk evaluation”.
Risk Management:
  “The complete risk-based decision-making process”.
Notes: Main idea/objective for slide:
Discuss the definition of Risk Assessment and Risk Management, placing emphasis on the management of ammunition and explosive storage
What the instructor should cover (in addition to slide content)
References/further reading
IATG 2.10 – Introduction to Risk Management Principles and Processes

## Slide 13: Definitions:
Risk Mitigation:
  “The measures taken to reduce the effects should an explosion or deflagration occur”.
Risk Reduction
  “Actions taken to lessen the probability, negative consequences or both, associated with a particular risk.”
Notes: Main idea/objective for slide:
Discuss the definition of Risk Mitigation and Risk Reduction, placing emphasis on the management of ammunition and explosive storage
What the instructor should cover (in addition to slide content)
References/further reading
IATG 2.10 – Introduction to Risk Management Principles and Processes

## Slide 14: Definitions:
Safety:
  “The reduction of risk to a tolerable level”.
Tolerable Risk:
  “The risk that is accepted in a given context based on the current values of society”.
Notes: Main idea/objective for slide:
Discuss the definition of Safety and Tolerable Risk, placing emphasis on the management of ammunition and explosive storage
What the instructor should cover (in addition to slide content)
References/further reading
IATG 2.20 – Introduction to Risk Management Principles and Processes

## Slide 15: Definitions:
ALARP
“As Low As Reasonably Practical”.
Notes: Main idea/objective for slide:
Discuss the definition of Tolerable Risk (ALARP), placing emphasis on the management of ammunition and explosive storage
What the instructor should cover (in addition to slide content)
References/further reading
IATG 2.20 – Introduction to Risk Management Principles and Processes

## Slide 16: Tolerable Risk Levels (ALARP)
‘At Risk’ Group | Tolerable Risk Level (IR) | Remarks
Workers in Explosives Facility (Maximum Tolerable Limit) | 1 x 10-3 | Workers may be exposed to this risk level on an occasional basis. A non-standard explosive limit licence should be issued at this risk level. If the IR is greater than 1 x 10-3 then a special case for licensing shall be submitted to the national technical authority, and political acceptance of the risk, in writing, shall be formally sought.
Workers in Explosives Facility (Warning Level) | 1 x 10-4 | This should be the maximum level of risk that workers are exposed to on a regular basis. A non-standard explosive limit licence should be issued at this risk level.
Workers in Explosives Facility (Acceptable Limit) | 1 x 10-6 | This should be the ideal level of risk for daily exposure. A standard explosive limit licence should be issued at this risk level.
General Public (Maximum Tolerable Limit) | 1 x 10-4 | The general public may be exposed to this risk level on an occasional basis and in exceptional circumstances. A non-standard explosive limit licence should be issued at this risk level. If the IR is greater than 1 x 10-3 then a special case for licensing shall be submitted to the national technical authority, and political acceptance of the risk, in writing, shall be formally sought.
General Public (Warning Level) | 1 x 10-5 | This should be the maximum level of risk that the general public is exposed to on a regular basis. A non-standard explosive limit licence should be issued at this risk level.
General Public (Acceptable Limit) | 1 x 10-6 | This should be the ideal level of risk for daily exposure. A standard explosive limit licence should be issued at this risk level
Notes: Main idea/objective for slide:
Discuss Tolerable risk levels
What the instructor should cover (in addition to slide content)
Provide this table as a Handout
References/further reading]
IATG 2.10 – Introduction to Risk Management Principles and Processes, Page 6
Tolerable risk is determined by the search for absolute safety contrasted against factors such as:
  the inherent explosive safety hazards of storing, handling and processing ammunition
  available resources
  the conventions of the society where the ammunition is being stored
  the financial costs.
It follows that there is therefore a need to continually review the tolerable risk that underpins the concept behind stockpile management operations in a particular environment.
The level of tolerable risk shall be determined by the appropriate national authority, but it should not be less than the tolerable risk accepted, for example, in manufacturing or industrial processes

## Slide 17: Risk Management Process: Matrix
Notes: Main idea/objective for slide:
Introduce the risk management process, to include hazard identification, the likelihood of the event occurring and the consequence of such an event happening.
What the instructor should cover (in addition to slide content)
Write these definitions on a flipchart and post it onto the wall.
Risk management – is the overall process of identifying, analysing, mitigating and communicating risk to ensure the safety of people and property from unwanted explosive events
Risk Assessment - Is a process that is made up of three separate processes: Hazard identification, risk analysis, and risk and ALARP evaluation
Risk Reduction and Mitigation – Is a process that identifies and implements controls and measures to reduce the risk to a tolerable level.
Risk Acceptance – Is the formal acceptance of National Authorities of the residual risk from an explosive area, following the effective implementation of mitigating factors to initial risks involved.
Risk Communication – Is the process of communication the necessary information, processes and procedures to be followed by all personnel to ensure that the risk remains ALARA at all times.
Risk Analysis - A process that is used to understand the nature, sources, and causes of the risks that you have identified and to estimate the level of risk
Risk and ALARP Evaluation - Is a process that is used to compare risk analysis results with risk criteria in order to determine whether or not a specified level of risk is acceptable or tolerable
Hazard Identification and Analysis - Is a process that is used to find, recognize, and describe the risks that could affect the safety of people and property from an explosive event
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
Risk management is sometimes a misunderstood term, within which there are common misconceptions in terms of the relationship between, for example, risk assessment and risk analysis.
The matrix identifies the relationship between the different components of risk management that shall be used

## Slide 18
Generic Area / Activity | Specific Area / Activity | Remarks
Risk Management | Identify and nominate specific individual responsible for risk management policy in explosive facilities. | 
Risk Analysis | Identify ‘Explosives Facilities’. | 
Risk Analysis | Identify ‘At Risk’ Groups. | Workers in Explosive Area (Unqualified) Workers in Explosive Area (Explosives Qualified). General Public Residing in Proximity to Explosive Facility. General Public Transiting in Proximity to Explosive Facility.
Risk Analysis | Decide on the appropriate level of Tolerable Risk in terms of IR and SR. | Risk levels should be comparable with other industrial processes.
Risk Acceptance | Obtain written Approval for Tolerable Risk levels. | This ensures that appropriate risk acceptance authority is aware of the risk, and of their responsibilities to allocate appropriate resources to manage the risk and maintain it within tolerable levels.
Risk Communication | Widely communicate the Tolerable Risk levels being applied to Explosive Facilities. | Communities in close proximity should be made aware of the risks they are exposed to by their political class.
Notes: Main idea/objective for slide:
Explore how the activities within a Risk Management Process are used in a typical explosive storage environment
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
Risk management is sometimes a misunderstood term, within which there are common misconceptions in terms of the relationship between, for example, risk assessment and risk analysis.
The matrix identifies the relationship between the different components of risk management that shall be used

## Slide 19: Hazard Identification and Analysis
All Potential Explosion Sites (PES) are considered hazardous.
The severity of the hazard is based on:
  The quantity of ammunition being stored.
  The hazard classification.
  The physical and chemical stability of the ammunition.
  The physical condition of the PES.
  The proximity and distances to people and Exposed Sites.
Notes: Main idea/objective for slide:
Outline what Hazard Analysis involves and what constitutes a hazard in an explosive area.
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
Hazard identification and analysis is a reasonably simple process for the risk management process that supports conventional ammunition storage.
As hazards are defined as a potential source of harm, then the hazard from, for example, individual explosive storehouses (ESH) will depend on the quantity, hazard classification,22 physical condition and chemical stability of the ammunition contained within that ESH.
If the inter-magazine distances (IMD) are not in accordance with the recommendations contained in IATG 02.20, Quantity and separation distances, then further risk analysis will be required.
Normally each ESH is considered to be an individual Potential Explosion Site (PES).
Yet, if there is a risk of practically instantaneous propagation (PIP) due to inadequate IMD between the ESH, then they may have to be treated as one PES, and the explosive quantity aggregated.

## Slide 20: Risk Estimation: Outcomes
The probability of an unplanned and undesirable explosive event.
The physical effects of such an explosion.
The number of casualties to be expected.
The levels of damage to be expected.
Notes: Main idea/objective for slide:
Discuss the need to estimate the risk and determine the likely outcomes from an unwanted explosive event.
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
In many cases, it will be difficult to establish the probability of an unplanned and undesirable explosive event at a particular explosive storage area.
Yet data is available on the number of such events annually and a stockpile management organization should be aware of previous similar events in their region; this will assist the organization in assessing frequency, and hence probability.
This is known as the ‘historical’ approach and an example model is at Clause 8.2.1.1. A more qualitative approach is at Clause 8.2.1.2.
Alternative methods for establishing frequency, and hence the probability of explosive events, during the risk estimation process include analytical techniques such as attempts to define and quantify all of the potential scenarios in which an explosive event can occur.
Logic or fault tree approaches are often used depending upon the complexity of and number of proposed scenarios leading to an event.
It can be a complex and sophisticated process, and further guidance is available in the informative references at Annex B.

## Slide 21: Estimating the Probability
Generic Description | Probability | Qualitative Definition
Likely | Frequent | Expected to occur once or more times.
 | Almost Certain | 
 | Very Probable | 
 | Probable | 
Occasional | Possible | Unlikely, but possible to occur.
Unlikely | Seldom | It may be assumed that it will not occur.
 | Rare | 
 | Improbable | 
Notes: Main idea/objective for slide:
Highlight how important is it to estimate and quantify the probability of such as an unwanted explosive event occurring.
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
A qualitative means of estimating probability

## Slide 22: Categorising the Risk: Extent of fatalities/Injuries/damage
Description | Qualitative Definition
Catastrophic | Undesirable event leading to multiple fatalities and/or serious injury to individuals and/or significant loss or damage to critical equipment or infrastructure.
Major | Undesirable event leading to some fatalities and/or serious injury to individuals and/or significant loss or damage to critical equipment or infrastructure.
Minor | Undesirable event leading to minor injuries to individuals and minimal impact on equipment or infrastructure.
Notes: Main idea/objective for slide:
Discuss how to categorise the risk, once the hazards and the probabilitys have been determined
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
The physical effects of an undesirable explosive event within an ammunition depot can be estimated by using the appropriate equation contained within IATG 01.80 Formulae for ammunition management (Clause 6.2).
This can be used to determine the blast over-pressure and impulse at the distance from a potential explosion site to an exposed site from a known explosive mass.
Threshold blast over-pressures for effects on humans have been established by experimentation, (34,5kPa for onset of hearing damage, 207kPa for lung damage and 690kPa for fatality),27 and therefore if the population density is known within the appropriate ranges an estimate of the total number of fatalities and casualties can then be derived.
Alternatively, the ESTC Outdoor Model may be used. (Both in Clause 11.2 to IATG 01.80 Formulae for ammunition management).
Similarly, the effects of blast on buildings within and outside the perimeter of the ammunition depot can be estimated. (Clause 10 of IATG 01.80 Formulae for ammunition management).

## Slide 23: Achieving Tolerable Risk
Identify the likely stakeholders
Identify each hazard;
Estimate and evaluate the risk to each identified user or group
Judge if that risk is tolerable
If the risk is not tolerable then reduce or mitigate the risk until it becomes tolerable.
Notes: Main idea/objective for slide:
Introduce the Flow Diagram for determine what is the "Tolerable Risk', or the amount of risk that will be accepted by a National Authority.
What the instructor should cover (in addition to slide content)
Provide a handout of this flow chart to participants
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
Tolerable risk is achieved by the iterative process of risk assessment (risk analysis and risk evaluation) and risk reduction
Effective risk assessment has a range of benefits that include:
  it helps in ranking the importance of individual risk contributions to the overall risk;
  it helps to identify risks that are easily reduced or eliminated;
  it helps to clarify what is known and what is not known about the potential risk;
  it can provide an objective basis for decisions on controlling risks, especially those applying to the local civilian communities near ammunition storage areas;
  it can provide important quantitative information as input to decisions for allocating resources to conventional ammunition stockpile management;
  it makes it possible to rank risk reduction or remediation alternatives in terms of risk to workers, the environment, and the public; and
  it can provide a process for consensus-building and a forum for the participation of stakeholders in the development of the risk assessment process and the identification of tolerable risk. This process will hopefully lead to greater acceptance of that risk.

## Slide 24
What types of Risk Mitigation controls can we use?
Notes: Main idea/objective for slide:
Explore and discuss the numerous type of risk mitigation and control measures that can be used to reduce the risk in an explosive storage area.
What the instructor should cover (in addition to slide content)
Ask questions of the participants and write their answers on a white board.
Look to group their responses were possible.
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
In order to reduce the estimated risk from an unplanned or undesirable explosive event at an ammunition storage area, one or a combination of the following actions should be taken:
  closure of the ammunition depot and the transfer of stocks to an ammunition depot with spare capacity, mitigation;
  a reduction of ammunition stock levels within the explosive storage area until appropriate predicted blast over-pressure levels are reached at the exposed site, mitigation
  the probable impact of the estimated risk to the local community is formally accepted at the appropriate political level, acceptance.
  an increase in the separation distance between the potential explosion site and the exposed site until tolerable blast over-pressure levels are reached at the exposed site, mitigation
  improvements in the physical infrastructure of ammunition storage to achieve tolerable estimated blast over-pressure levels at the exposed site, mitigation
  instigation of effective ammunition surveillance and proof systems to identify ammunition and propellant that has deteriorated

## Slide 25
Explosive Risk Assessments
Notes: Phase 2. Development (Time allocation - 160 min)
Stage 2 (Time allocation 40 mins) – Explosive Risk Assessments

## Slide 26: Qualitative V’s Quantitative Risk Assessments
Qualitative:
  Descriptive process
  Written word
Quantitative:
  Quantifies the outcomes and assess the probability
  Provides a numerical approach to making decision
  Creates more realistic scenarios and outcomes
Notes: Main idea/objective for slide:
Discuss the difference between qualitative and quantitative explosive risk assessment.
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
Qualitative risk assessments are descriptive, rather than using measurable or calculable data, and they are by far the most widely used approach to risk analysis in many circumstances.
Probability data is not required and only estimated potential loss is used.
A qualitative risk assessment can be a helpful first step, when a State decides to implement risk assessment procedures, but they should not be used as a replacement for the scientifically accepted and proven techniques which are available to allow for a more quantitative risk assessment.
They may be used though for specific processes that support ammunition management where little quantitative data is available, such as technical procedures for ammunition processing tasks
Quantitative Risk Assessment (QRA) is a powerful tool for the investigation and reduction of risk.
It should be used to estimate the approximate probability of an accidental explosion during ammunition storage and then estimate the fatalities, injuries, damage and other losses from such an explosion (referred to as the consequences).
This enables professional judgement to be applied as to whether or not the risk meets the ALARP principal.
QRA provides an advantage over more subjective methods in that a more complete set of available information is used to quantify ‘risk’ as a parameter.
This allows for consistency and repeatability from decision to decision, (for example when comparing the hazard presented by each explosive storehouse within an ammunition depot).

## Slide 27: Example: Qualitative Risk Assessment
See Handout
Notes: Main idea/objective for slide:
Provide an example of a qualitative explosive risk assessment to the participants and walk them through each section to explain how it is produced.
What the instructor should cover (in addition to slide content)
Provide a handout of this table to the participants, and work through examples.
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes, Page 13

## Slide 28: Example: Quantitative Risk Assessment
Notes: Main idea/objective for slide:
Provide an example of a quantitative explosive risk assessment to the participants and walk them through each section to explain how it is produced.
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes, Annex D

## Slide 29: Example: Quantitative Risk Assessment
See Handout
Notes: Main idea/objective for slide:
Provide an example of a quantitative explosive risk assessment to the participants and walk them through each section to explain how it is produced.
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes, Annex D
Handout QRA to participants

## Slide 30: Simple Risk Assessment Form Example
Notes: Main idea/objective for slide:
Provide an example of a simple quantitative explosive risk assessment to the participants and walk them through each section to explain how it is produced.
Explain the use to a risk assessment matrix
What the instructor should cover (in addition to slide content)
Show a 3x3 matrix and a 5x5 matrix.

## Slide 31: Explosive Consequence Analysis
“…a structured process, utilizing explosives science and explosives engineering, to provide scientific evidence of the potential risk to individuals and property from blast effects and fragmentation in the event of an undesirable explosive event .”
A risk assessment process using IATG based software to support the analysis, and:
  consider a realistic explosion threat scenario
  estimate the explosion effects on nearby personnel and structures
  highlight particularly vulnerable risk areas that may require special protection requirements.
Notes: Main idea/objective for slide:
Discuss Explosive Consequence Analysis
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
The ECA can be a core component of the risk analysis process during the development of a Quantitative Risk Assessment.
The initial component of an ECA should be compiled using the appropriate scientific formula(e) from IATG 01.80 Formulae for ammunition management.
The objectives of an ECA should be to:
  consider a realistic explosion threat scenario;
  estimate the explosion effects on nearby personnel and structures; and
  highlight particularly vulnerable risk areas that may require special protection requirements.
An example of a simple ECA methodology that could be used is at Annex E.
A fuller ECA should also consider the following additional external hazards and contributions to initiation frequency:
  lightning strikes. Where lightning protection in accordance with IATG 05.40 Safety standards for electrical installations is not provided
  flooding. Where the explosives facility is within a known flood plain
  aircraft crash. Where the explosives facility is close to commercial air routes or if in an area of high use by light aircraft
  nearby hazardous installations. Where the explosive facility is close to, or co-located with, for example, petroleum depots or ammunition disposal sites
  malicious destruction. The threat from sabotage or terrorist attack
  consequential initiation. Where the potential explosion sites (PES) are within inappropriate separation distances and an explosion in one causes the initiation of explosives in nearby PES.
The IATG software includes an ‘automated’ ECA which just requires the input of basic readily available data.

## Slide 32: Explosive Consequence Analysis
Blast Damage Estimation https://unsaferguard.org/un-saferguard/blast-damage-estimation
Fragment Velocity Estimation https://unsaferguard.org/un-saferguard/gurney
Explosion Danger Area Calculator https://unsaferguard.org/un-saferguard/explosion-danger-area
Notes: Main idea/objective for slide:
Discuss Explosive Consequence Analysis
What the instructor should cover (in addition to slide content)
Where possible, the instructor can explore these links during the lesson (dependant on internet connectivity)
Otherwise, direct the participant to these links as an online source of support to determine blast radius and explosive danger area distances.
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
The IATG Implementation Support Tool provides an Explosion Consequence Analysis tool that calculates the blast overpressure element for the analysis. Other tools, such as the Gurney equations for Fragment Velocity and Explosion Danger Area Calculator might also be used to support the analysis..

## Slide 33: Example: Explosive Consequence Analysis
See Handout
Notes: Main idea/objective for slide:
Discuss Explosive Consequence Analysis
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes. http://data.unsaferguard.org/iatg/en/IATG-02.10-Introduction-risk-management-IATG-V.3.pdf
Page 30
Handout ECA to participants

## Slide 34: Explosive Safety Cases
Ensure that:
  The explosive risk carried is as low as possible
  Does not jeopardize operational capability
  That health, safety and social environment requirements, and duty of care responsibilities are properly considered
Required for Temporary Storage Areas in T/PCC Field Missions.
Notes: Main idea/objective for slide:
Discuss Explosive Safety Cases
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
For the construction of temporary ammunition storage sites (see IATG 04.10) when full compliance with Outside Quantity Distances and Inside Quantity Distances is not possible, an Explosive Safety Case (ESC) shall be compiled.
This is done to ensure that the explosive risk carried is as low as possible, does not jeopardize operational capability and that health and safety requirements, and duty of care responsibilities, are properly considered.
There will be instances, particularly in post conflict environments, where a multitude of stakeholders are involved in ammunition stockpile management advisory or operational functions for humanitarian purposes.
It is highly desirable that in such circumstances all stakeholders should use a common format for explosive safety cases, which integrates requirements from across the IATG. Such a format is at Annex G.
Explosive Safety Cases shall only be accomplished by individuals whom are appropriately qualified and experienced in ammunition safety management

## Slide 35: Explosive Safety Case
Introduction
Explosion Consequence Analysis (ECA)
Summary of Non-Compliances
Summary of Hazard Mitigation Measures
Residual Risks
Probability of Event
Acceptance of Risk
Signatures
Annexes:
Safety Map (indicating areas of risk).
Site Plan.
Draft Explosive Limits Licence
Draft Acceptance of Risk Letter.
Notes: Main idea/objective for slide:
Discuss Explosive Safety Cases
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes
Include an explanation of the explosive storage area and summarize why full IATG compliance is not possible. This should include location, infrastructure type, total numbers of persons at the site or in the immediate area of the site.
Include the ECA in accordance with Annex E to IATG 02.10.
List all non-compliance issues referenced against the appropriate IATG and Clause. For example: The maximum Outside Quantity Distance (OQD) that may be achieved is only 220m. This is 120m less than the recommended OQD as at IATG 04.10, Clause 8.5.2, Table 11.
List all hazard mitigation measures applied in order to reduce risk. These should be referenced against each non-compliance area.
List the residual risk for each non-compliance issue. For example: The required storage levels of 35,000kg of HD1.1 means that in the event of an undesired explosive the reflected blast over-pressure at 220m will be 41.8kPa. This is in excess of the 34.5kPa level at which permanent hearing damage is to be expected (249m). There are routinely 40 persons working within the 220m to 249m zone who would be inversely affected by suffering permanent hearing damage.
The ESC compiler should try to determine the probability (likelihood) of an event at the site. This may be based on past historical data within the country and the security environment at the time the ESC is complied. Alternatively, estimate can be made on past global explosive events at ammunition storage areas, (data in IATG 02.10, Clause 8.2.1.1).
The ESC and the residual risk identified shall be formally acknowledged by the risk owner. Include here the full details of the risk owner. The wording of the ‘risk acceptance letter’ is extremely important and a draft should be provided by the compiler of the ESC as an Annex to the ESC. Due to the large number of possible scenarios and variables, it is not possible to provide an example draft of such a letter.

## Slide 36: Example: Explosive Safety Case
See Handout
Notes: Main idea/objective for slide:
Discuss Explosive Safety Cases
What the instructor should cover (in addition to slide content)
References/further reading:
IATG 2.10 – Introduction to Risk Management Principles and Processes http://data.unsaferguard.org/iatg/en/IATG-02.10-Introduction-risk-management-IATG-V.3.pdf
Annex G
Handout ESC to participants

## Slide 37
Participant Exercise
Notes: Phase 2. Development (Time allocation - 160 min)
Stage 3 (Time allocation 80 mins) – participant Exercise

## Slide 38: Exercise
See Handout
Notes: Main idea/objective for slide:
participant exercise to identify the various hazards to an ammunition Temporary Storage area.
What the instructor should cover (in addition to slide content)
Using the CARANA scenario, participants are required to identify the various hazards to an ammunition Field Storage area.
Each participant should receive a copy of the handout (word doc ‘WAMUNPOC L10 Risk Assessment Exercise’)
Instructors are to move around the class and help participants where required. Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions.
Participant Activity
The participants must produce a qualitative explosive risk assessment which includes all mitigating controls and demonstrates the awareness of residual risk to ALARP levels.
References/further reading:

## Slide 39: Exercise
See Handout
Notes: Main idea/objective for slide:
participant exercise to identify the various hazards to an ammunition Temporary Storage area.
What the instructor should cover (in addition to slide content)
Using the CARANA scenario, participants are required to identify the various hazards to an ammunition Field Storage area.
Each participant should receive a copy of the handout (word doc ‘WAMUNPOC L10 Risk Assessment Exercise’)
Instructors are to move around the class and help participants where required. Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions.
participant Activity
The participants must produce a qualitative explosive risk assessment which includes all mitigating controls and demonstrates the awareness of residual risk to ALARP levels.
References/further reading:

## Slide 40: Exercise
HD1.1
HD1.3
HD1.2
HD1.4
HD1.4
HD1.3
See Handout
Notes: Main idea/objective for slide:
participant exercise to identify the various hazards to an ammunition Temporary Storage area.
What the instructor should cover (in addition to slide content)
Using the CARANA scenario, participants are required to identify the various hazards to an ammunition Field Storage area.
Each participant should receive a copy of the handout (word doc ‘WAMUNPOC L10 Risk Assessment Exercise’)
Instructors are to move around the class and help participants where required. Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions.
participant Activity
The participants must produce a qualitative explosive risk assessment which includes all mitigating controls and demonstrates the awareness of residual risk to ALARP levels.
References/further reading:

## Slide 41: Exercise
Ammunition Type​ | Hazard Class Code​ | Quantity​ | NEQ​
Rds 7.62mm Ball Mixed Belt​ | 1.4S​ | 25,000​ | 75kg​
Rds 7.62mm Ball ​ | 1.4S​ | 10,000​ | 30kg​
Rds 5.56mm Ball ​ | 1.4S​ | 50,000​ | 100kg​
Rds 9mm Ball ​ | 1.4S​ | 10,000​ | 20kg​
Rds 84mm RCL HEAT​ | 1.1E​ | 75 | 85kg​
Rds 84mm RCL ILLUM​ | 1.2G​ | 50​ | 56kg​
CTGS 40x46mm HEAT​ | 1.2E​ | 200​ | 120kg​
Gren 66mm Smoke Screen​ | 1.3G​ | 250​ | 82kg​
Bombs 60mm Mortar HE​ | 1.1F​ | 550 | 166kg​
Bombs 60mm Mortar SMK​ | 1.3G​ | 200​ | 60kg​
Gren HE​ | 1.1D​ | 400​ | 24kg​
TNT Charge (500g)​ | 1.1D​ | 200​ | 100kg​
Detonators​ | 1.1B​ | 500​ | 0.1kg​
See Handout
Notes: Main idea/objective for slide:
participant exercise to identify the various hazards to an ammunition Temporary Storage area.
What the instructor should cover (in addition to slide content)
Using the CARANA scenario, participants are required to identify the various hazards to an ammunition Field Storage area.
Each participant should receive a copy of the handout (word doc ‘WAMUNPOC L10 Risk Assessment Exercise’)
Instructors are to move around the class and help participants where required. Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions.
participant Activity
The participants must produce a qualitative explosive risk assessment which includes all mitigating controls and demonstrates the awareness of residual risk to ALARP levels.
References/further reading:

## Slide 42: Lesson overview
Recall the hazards and mitigations associated with ammunition management
Discuss the UN Explosive Risk Assessments process
Examine how to identify, control and report risks associated with explosives
Compile an Explosive Risk Assessment
Notes: Phase 3. Consolidation (Time allocation - 10 min)
Main idea/objective for slide:
Recap Key Learning Points
participant activity
Give participants opportunity to ask any questions
What the instructor should cover (in addition to slide content)
Key Learning Points
2.2.6.1 Recall the hazards associated with ammunition management
2.2.6.2 Recall the mitigations associated with ammunition management
2.2.6.3 Recall UN Explosive Risk Assessments process
2.2.6.4 Discuss the UN Explosive Risk Assessments process
2.2.6.5 Examine how to identify risks associated with explosives
2.2.6.6 Examine how to control risks associated with explosives
2.2.6.7 Examine how to report risks with explosives
2.2.6.8 Evaluate the Explosive Risk Assessment
2.2.6.9 Compile an Explosive Risk Assessment using supplied documentation

## Slide 43
Weapons and Ammunition Management in UN Peace Operations
Look Ahead: Transporting Ammunition on UN Operations
Notes: Main idea/objective for slide:
Look ahead to the next lesson of the course:
  Transporting Ammunition on UN Operations