## Slide 1
Weapons and Ammunition Management in UN Peace Operations
Transporting ammunition on UN operations
Notes: Key Reference Documents for this lesson:
UN Manual on Ammunition Management
UN Weapons and Ammunition Management Policy (WAM)
International Ammunition Technical Guidelines (IATG)
All photographs in this lesson are © United Nations unless otherwise stated.

## Slide 2: Objective
Apply good practices for the transport of ammunition in the context of UN peacekeeping operations.
Notes: Main idea/objective for slide:
Phase 1. Introduction - Introduce the objectives of the lesson.
(Enabling Objective: 2.2.7 Apply good practices for the transport of ammunition in the context of UN peacekeeping operations.)
What the instructor should cover (in addition to slide content)
By the end of this training session the participant will apply good practices for the transport of ammunition in the context of UN peacekeeping operations.

## Slide 3: Lesson overview
Define good practices for ammunition transportation
Discuss the application of HCC in respect to ammunition transportation
Discuss additional application of safety considerations for the transportation of ammunition
Apply good practices and safety considerations to the transportation of ammunition on a UN operation
Notes: Main idea/objective for slide:
Introduce the Key Learning Points
Key Learning Points
2.2.7.1 Define good practices for ammunition transportation
2.2.7.2 Discuss the application of HCC in respect to ammunition transportation
2.2.7.3 Discuss additional application of safety considerations for the transportation of ammunition
2.2.7.4 Apply good practices and safety considerations to the transportation of ammunition on a UN operation

## Slide 4
Safe Transport of Ammunition – Guidance Documents
Notes: Phase 1. Introduction (Time allocation - 5 min)
Image provided by Hoplite Consulting Ltd.

## Slide 5: What does the UN Policy say?
Section D, Para 50 of UN Policy on WAM
“Transportation of weapons and ammunition shall be guided according to *MOSAIC 05.20 (para 13) and the **IATG 8.10 respectively. Mission SOPs must cover the transportation of weapons and ammunition onboard UN aircraft in line with UN Aviation Operators Manuals and lATA Dangerous Goods Regulations.”
* https://www.un.org/disarmament/convarms/mosaic/
**https://unsaferguard.org/un-saferguard/guide-lines
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
Annex A of MOSAIC 05.10 outlines a model security plan for the stockpile management for SALW.
Image provided by Hoplite Consulting Ltd.

## Slide 6: Guidance
The United Nations Recommendations on the Transport of Dangerous Goods (referred to as ‘UN Recommendations’ and sometimes as the ‘Orange Book’)
Road - UN Model Regulations & The European Agreement Concerning the International Carriage of Dangerous Goods by Road (ADR)
Rail - Convention for International Carriage by Rail (COTIF)
Air - Convention on International Civil Aviation, Annex 18. The Safe Transport of Dangerous Goods by Air & ICAO Technical Instructions for the Safe Movement of Dangerous Goods by Air
Sea - International Convention for the Safety of Life at Sea (SOLAS) & International Maritime Dangerous Goods Code (IMDG)
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
Many guidance documents. Some are enshrined in law.
What the instructor should cover (in addition to slide content)

## Slide 7: IATG 08.10
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
Image provided by Hoplite Consulting Ltd.

## Slide 8: Pre-loading Checks
The vehicle is roadworthy. Only one trailer shall be towed by each vehicle.
Relevant documentation is on-board the vehicle e.g.
  Dangerous goods details
  Drivers' credentials
  Means of identification for all members of the crew
  Competent authority approval
The relevant markings are adhered to the vehicle depending on the goods being carried and the type of vehicle
Safety equipment for fire-fighting, breakdown and emergencies shall be present.
Vehicle telemetry or tracking devices should be used where possible and appropriate.
Notes: Main idea/objective for slide:
Describe the pre-loading safety precautions for vehicles.
What the instructor should cover (in addition to slide content)
Question participants to check recall from slide 8 and 9 of this lecture.
Print out IATG 08.10 Annex D.
participant activity
participants to open IATG 08.10 Annex D.
Ask the participants to pick out any challenges that they would have in a mission to meet the requirements. Suggested answer: Driver credentials do not meet the regulations in terms of minimum age for a heavy vehicle. Solution: Change driver or postpone the transit until a driver is found who meets the criteria.

## Slide 9: Loading and Unloading of Ammunition and Explosives (AE) - Considerations
Only load AE at a secure recognised ammunition site – ensure not only safety but also security of AE
Where possible only load during daylight
The vehicle engine shall be turned off during loading / unloading unless the engine needs to be used to operate loading equipment.
Ensure adherence to CG mixing rules for transport
Notes: Main idea/objective for slide:
Understand basic considerations for loading and unloading of AE.
What the instructor should cover (in addition to slide content)
What other considerations should be considered but may not be written explicitly? Suggested answer: The loading and unloading shall only take place on solid ground designed to withstand the weight of the fully loaded vehicle. Subsidence in the case of heavy rainfall should be considered.

## Slide 10: IATG 08.10 Transport of Ammunition
Movement of AE by road (Safety Precautions during convoy)
50m between vehicles (can be adjusted in built up areas situation dependent)
A guard must remain with the vehicles at all times
Vehicles carrying AE will have a means of communicating with HQ but vehicles carrying electric detonators will not use radios except in the case of an emergency
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
Ask participants:
What type of communications might be used in a UN mission. Answer: UHF (Tetra), VHF (Motorola), HF, Satellite comms, mobile phones.
What are the concerns related to this? Answer: Electric initiators if transported need to be packaged correctly.
participant activity
participants are directed to find section 08.10 of the IATG and to follow the course material using the IATG and MOSAIC.

## Slide 11: IATG 08.10 (Ammunition & Explosives)
Vehicle requirements (Checks by driver)
Vehicles shall be serviceable, have a spare wheel and a wheel changing kit
All vehicles shall comply with ADR 9.2
The vehicles shall be suitable for the load and for the road on which it will travel
Trailers may be used if they are equipped with their own braking system and an automatic activation should the trailer become detached from the vehicle
A grounding strap to prevent buildup of static electricity
Fuel shall only be carried in the fuel tank
A serviceable CO² fire extinguisher will be carried in the cab
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
Spend 5 minutes familiarising the participants with ADR 9.2 by clicking on the link in the slide.
participant activity
Ask the class if any participant has experience with the ADRs

## Slide 12: IATG 08.10 (Ammunition & Explosives)
Equipment requirements (Checks by driver)
PPE in order to carry out general actions
High visibility vest
Contraband container under control of convoy commander containing cigarettes, matches, lighters etc.
Eye rinse
A suitably sized wheel chock
Two torches with a light that can be seen at 150m
Two self-standing red warning triangles & two red warning flags
A shovel and pickaxe
Explosive symbol if deemed appropriate – security dependent
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
Discuss with the class the feasibility of finding all of this equipment in a UN mission. Pre-planning is required to ensure full compliance.
participant activity
Discuss each of the equipment items and ask the participants why each item may be required.

## Slide 13: IATG 08.10 (Ammunition & Explosives)
Driver requirements
A co-driver is required
Appropriate training in the handling and transport of AE
Be in good health
Meet the national minimum legal age and driving licence requirements for the class of vehicle
Be appropriately briefed on the hazards associated with the AE and the security situation and actions to be taken in the event of problems (actions-on…)
No passengers are allowed
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
How the UN licences drivers. Answer: According to national licencing from the T/PCC and subject to the contingent owned equipment inspections.
participant activity
Ask the participants to describe their experiences with inappropriately trained or uncurrent drivers in a mission environment. What are the dangers associated with this other than the breach in regulations?

## Slide 14: MOSAIC 05.20 Small Arms Light Weapons (SALW)
Notes: Main idea/objective for slide:
Introduce the relevant module of MOSAIC dealing with the transport of SALW.
What the instructor should cover (in addition to slide content)
Section 13 deals with transport. Ask the participants to open the relevant section using the link provided. Follow the class using the MOSAIC document.

## Slide 15: MOSAIC 05.20 (SALW) General Security
A risk assessment with the following considerations shall be carried out:
  Quantity of weapons
  Types of weapons
  Duration that the weapons will be in transport
  Number of times weapons will be loaded/unloaded and reloaded onto various transportation
  The expectation of security incidents (based on threat analysis)
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
The instructor may ask the participants to identify other aspects of the risk assessment that they would include
participant activity
Write the considerations that they would add to the list on a flip chart and discuss each one with the class

## Slide 16: MOSAIC 05.20 (SALW) General Security
Sanctioned or known criminal organisations and businesses shall not be used to transport weapons and ammunition
Weapons and ammunition shall be transported separately
Civilian transport contractors shall operate with procedures for authorisation, security, monitoring and inspection of each individual transport and the contractors themselves
Containers and boxes shall have locks that adhere to Clause 9.9.4
The opening of weapons containers shall be placed door-to-door to prevent opening in transit.
Shipments shall be checked upon receipt and if possible, during transit to ensure integrity of locks etc.
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
Ask participants:
How would an ammunition team in the mission determine whether a business or transport agent was on the UN sanctions list? Answer: They would ask through their chain of command where it would be escalated to UNHQ.
What does clause 9.9.4 state? Answer: Locks and padlocks used on the doors and gates of weapons storage buildings should be compliant with EN 12320, Building hardware – Padlocks and padlock fittings – Requirements and test methods.

## Slide 17: MOSAIC 05.20 - Road Transport
Small and light weapons by road may be conducted by marked or unmarked military vehicles or by civilian contractors
Civilian transport contractors should be equipped with protection systems (alarm, trackers)
These should be secured by military or security forces
Routes should be planned and treated as classified and varied when taken regularly
Consider dismantling and removing essential components of weapons and transporting them in separate vehicles.
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
Explain why routes should be varied and weapons may be transported in unmarked vehicles. Answer: To prevent setting a routine and making an ambush more difficult. To prevent the convoy from being identified as high-value.
participant activity
What are the risks associated with dismantling the weapons and transporting them in different vehicles? Answer: Different components end up in the wrong weapons when reassembled or small components get mislaid.

## Slide 18: MOSAIC 05.20 - Sea and Rail Transport
Sea Transport
The weapons consignor should liaise with the master of the vessel to agree the most suitable location for weapons containers in the vessel
Containers of non-sensitive items should be used to block any remaining assessable doors to weapons containers
Weapons should be shipped on vessels that offer a direct voyage to the destination port to reduce the possibility of the weapons being offloaded en-route
Rail Transport
Barriers on rail cars should be used to prevent access to side opening containers
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
participant activity
Ask the participants if they have any experience of the transportation of weapons and ammunition by sea or rail.

## Slide 19: MOSAIC 05.20 - Air Transport
Military aircraft or civilian contractors may be used
Civilian transport contractors shall obtain the necessary over-flight authorisation from the countries over which the weapons are to be transported
Detailed flight and route plans should be charted and overseen by the appropriate national authority of the exporting state
Weapons should be transported on aircraft that offer a direct route. Refuelling stops are permitted
Sanctioned transport agents or airlines shall not be used.
Notes: Main idea/objective for slide:
Highlight the essential manuals and guidance documents that support the safe transport of ammunition and explosives on UN operations.
What the instructor should cover (in addition to slide content)
The importance of obtaining authorisation to overfly territories with ammunition and weapons, even if the aircraft will not land in that country.
participant activity
Ask the participants if they remember how to check if a transport agent or airline is on the sanction list. Answer: They would ask through their chain of command where it would be escalated to UNHQ.

## Slide 20
Ensuring safety in ammunition transport
Notes: Phase 2. Development (Time allocation - 35 min)
Stage 1 (Time allocation 10 mins) – Ensuring safety in ammunition transport
Image provided by Hoplite Consulting Ltd.

## Slide 21: Group discussion based on class experiences
What are the potential hazards of transporting ammunition and weapons through a host country as part of a repatriation operation?
Does anyone have experience of such an operation?
If so, describe the process and discuss any components of the operation that were not aligned with the UN Manual on AM.
If not, what do you think would be the top 5 hazards and the likelihood of each hazard, when transporting ammunition by road through a field mission?
How would you mitigate these hazards according to the UNMAM and the IATG / MOSAIC?
Notes: Main idea/objective for slide:
Group discussion on the various risks (hazards and likelihoods) associated with the transport of ammunition and explosives in a UN mission area.
participant activity
In groups, have the participants discuss the various risks (hazards and likelihoods) associated with the transport of ammunition and explosives in a UN mission area.
What the instructor should cover (in addition to slide content)
(Time allocation 10 mins)
Tailor the discussion according to participant’s experiences.
The instructor should question the groups and their findings in order to develop the depth of understanding of the explosive risks.
Instructors to write these hazards and risks onto the flipchart and post onto the wall.

## Slide 22
Explosive Risk Assessments and Security Plan
Notes: Phase 2. Development (Time allocation - 35 min)
Stage 2 (Time allocation 10 mins) – Hazard Class Codes and transporting ammunition
Revise the UN hazard class code system, including compatibility groups and its mixing rules.
Instructors ask questions to the class to reinforce this learning.
Discuss with the participants the various activities and checks that should be undertaken by the transport driver and the ammunition technician on the vehicle prior to loading.
Highlight the safety precautions that should be put in place for each vehicle which is to carry ammunition.
Discuss the safety precautions to be considered during the convoy, along the route and during the loading and unloading of ammunition onto/from the vehicle.
Provide the participants with a worked-out example of a basic risk assessment that manages this explosive risk.

## Slide 23: Mixing Rules for Transport by Road
Notes: Main idea/objective for slide:
Revise the UN hazard class code system, including compatibility groups and its mixing rules.
What the instructor should cover (in addition to slide content)
Question participants to check recall
Refer to lesson 8 if the participants recall is not sufficient
participant activity
participants to open IATG 08.10

## Slide 24: Mixing Rules for Transport by Road
Notes: Main idea/objective for slide:
Revise the UN hazard class code system, including compatibility groups and its mixing rules.
What the instructor should cover (in addition to slide content)
Question participants to check recall
Refer to lesson 8 if the participants recall is not sufficient
participant activity
participants to open IATG 08.10

## Slide 25: Transport Safety Case / Risk Assessment
In the previous lecture you studied Explosive Safety Cases.
For transportation of dangerous goods no specific explosive safety case exists.
The Explosive Safety Case that we learned is used as the Risk Assessment document.
​
Notes: Main idea/objective for slide:
Introduce the concept of an explosive safety case for transport of AE
What the instructor should cover (in addition to slide content)
Question participants to check recall the details of the previous lecture.
Refer to lesson 10 if the participants recall is not sufficient

## Slide 26: Explosive Safety Case / Risk Assessment
Introduction​
Explosion Consequence Analysis (ECA)​
Summary of Non-Compliances​
Summary of Hazard Mitigation Measures​
Residual Risks​
Probability of Event​
Acceptance of Risk​
Signatures​
​
Annexes:​
Route Map (indicating areas of risk).​
Loading and unloading site Plan.​ ​
Draft Acceptance of Risk Letter.​
Notes: Main idea/objective for slide:
Revise the key headings of the explosive safety case.
What the instructor should cover (in addition to slide content)
Use the participants recent learning of ESC to discuss which sections are more and less relevant to the transport of AE.
We have changed the Annexes to make them more relevant to the transport of ammunition.

## Slide 27: Security Plan – ADR Annex A Chapter 1.10
Name, location and telephone number of the security officer.
Detailed responsibilities of the security personnel
Records of the goods being carried
Generic security threats and risks.
                Include any stops required en route.
                Include details on the intermediate temporary storage of dangerous goods during the transfer of the goods.
Notes: Main idea/objective for slide:
To describe the outline of a security plan as per ADR Annex A Chapter 1.1.
What the instructor should cover (in addition to slide content)
Use the participants experiences in peace operations to highlight the key inputs under each heading.
List these on a whiteboard / flip chart.

## Slide 28
Statement of measures to be taken to reduce security risks:
                Training
              Security policies e.g., Response to an increased threat, new employee verification.
              Operating practices e.g., Route selection, access to the dangerous goods at intermediary temporary storage site, proximity to vulnerable infrastructure.
              Effective and up to date procedures for reporting and dealing with security threats, breaches of security or security incidents.
              Equipment and resources that are to be used to reduce security risks.
Security Plan – ADR Annex A Chapter 1.10
Notes: Main idea/objective for slide:
To describe the outline of a security plan as per ADR Annex A Chapter 1.1.
What the instructor should cover (in addition to slide content)
Use the participants experiences in peace operations to highlight the key inputs under each heading.
List these on a whiteboard / flip chart.

## Slide 29: Security Plan – ADR Annex A Chapter 1.10
              The Security plan should have
              Effective and up to date procedures for reporting and dealing with security threats, breaches of security or security incidents.
Procedures for the evaluation and testing of security plans and procedures for periodic review and update of the plan.
Measures to ensure the physical security of transport information contained in the security plan
Measures to ensure that the distribution of information relating to the transport operation contained in the security plan is limited to the those who need to have it.
Notes: Main idea/objective for slide:
To describe the outline of a security plan as per ADR Annex A Chapter 1.1.
What the instructor should cover (in addition to slide content)
Use the participants experiences in peace operations to highlight the key inputs under each heading.
List these on a whiteboard / flip chart.

## Slide 30
Participant Exercise
Notes: Phase 2. Development (Time allocation - 35 min)
Stage 3 (Time allocation 15 mins) – participant Exercise

## Slide 31: CARANA – Weapon and Ammunition Transport
Sector 3 HQ, MUKA Camp is to be closed and handed over to CARANA national forces
Ammunition is to be transported to GALASI for ship transport to the TCC. The ammunition schedule is contained in a follow-on slide
As the mission ammunition technician, the SATO has tasked you with carrying out the risk assessment and security plan for the movement of the ammunition temporarily stored at MUKA
The unit disposition at MUKA is detailed in the following map
Notes: Main idea/objective for slide:
Introduce CARANA scenario for participant exercise
What the instructor should cover (in addition to slide content)
The threat assessment is High for CARANA.

## Slide 32: CARANA
Notes: Main idea/objective for slide:
Using the CARANA scenario, provide the participants with a basic situation update. Refer to the CARANA scenario included with the lessons. The threat level is assessed as HIGH.
What the instructor should cover (in addition to slide content)
The disposition of friendly forces across the mission.

## Slide 33: CARANA – Transport
Notes: Main idea/objective for slide:
Introduce the location of MUKA and the units based there.
participant activity
Are the participants familiar with the unit symbols? Answer: MUKA contains the battalion HQ, a field engineering company, a signals platoon, a mechanised infantry company and an infantry company.

## Slide 34: Weapons & Ammunition Schedule
Weapons
6 X 120mm mortars
6 X Carl Gustaf recoilless rifles
150 X M16 carbine rifles
Ammunition
Rds RCL HE 441D X 24 boxes (6 per box)
Rds RCL HEAT 551 X 10 boxes (6 per box)
Rds Mortar 120mm HE 88 X 150 boxes (2 per box)
PE No4 8oz Ctgs X 20 boxes (20 per box)
Detonators L2A2 X 2 boxes (50 per box)
Notes: Main idea/objective for slide:
Introduce AE schedule for the transportation requirement

## Slide 35: Factors to consider IATG 08.10
Notes: Main idea/objective for slide:
IATG 08.10 states that ammunition in transport does not generally require the application of explosive safety QD while in movement.
participant activity
Ask the participants what they think that the main issue with trying to maintain the QD in transit is. Answer: Its impracticable due to space and cost
What the instructor should cover (in addition to slide content)
Read the rest of the paragraph in the slide paying particular attention to the requirement to have appropriate QD when undergoing handling etc.

## Slide 36: Mixing rules for Road Transport
Notes: Main idea/objective for slide:
Introduce CARANA scenario for participant exercise
participant activity
Ask the participants to refer to lesson 8 and to compare the mixing rules for storage vs transport
What the instructor should cover (in addition to slide content)
Identify the differences between the mixing rules for storage and transport. E.g. E and F are NOT compatible with B in transit.

## Slide 38: Mixing rules for Storage (for comparison)
Notes: Main idea/objective for slide:
Refresh mixing rules for storage
participant activity
Ask the participants to refer to lesson 8 and to compare the mixing rules for storage vs transport
What the instructor should cover (in addition to slide content)
Identify the differences between the mixing rules for storage and transport. E.g. E and F are NOT compatible with B in transit.

## Slide 39: Risk assessment
A risk assessment with the following considerations shall be carried out:
  Quantity of weapons and ammunition
  Types of weapons and ammunition
  Duration that the weapons and ammunition will be in transport
  Number of times weapons and ammunition will be loaded/unloaded and reloaded onto various transportation
  The expectation of security incidents (based on threat analysis)
  Road transport mixing considerations
  Transport type, appropriate equipment, route planned
  Personnel briefed.
Notes: Main idea/objective for slide:
Introduce CARANA scenario for participant exercise
participant activity
In groups, the participants are to undertake a Risk Assessment for the transport of this ammunition and weapons from one UN camp to another, based on the UN CARANA scenario.
Open discussion
What the instructor should cover (in addition to slide content)
Use the ESC and the Security Plan templates that have been covered in this lecture.
Instructors are to work closely with the groups to help them identify hazards, develop mitigating factors and ultimately produce a suitable explosive risk assessment for this operation.
When the groups have completed their groupwork, work through the answers with the class and ask questions.

## Slide 40: Use this format
Hazard | Mitigation

## Slide 41: Lesson overview
Define good practices for ammunition transportation
Discuss the application of HCC in respect to ammunition transportation
Discuss additional application of safety considerations for the transportation of ammunition
Apply good practices and safety considerations to the transportation of ammunition on a UN operation
Notes: Phase 3. Consolidation (Time allocation - 10 min)
Main idea/objective for slide:
Recap Key Learning Points
participant activity
Give participants opportunity to ask any questions
Key Learning Points
2.2.7.1 Define good practices for ammunition transportation
2.2.7.2 Discuss the application of HCC in respect to ammunition transportation
2.2.7.3 Discuss additional application of safety considerations for the transportation of ammunition
2.2.7.4 Apply good practices and safety considerations to the transportation of ammunition on a UN operation

## Slide 42
Weapons and Ammunition Management in UN Peace Operations
Look Ahead: Ammunition Inspection
Notes: Main idea/objective for slide:
Look ahead to the next lesson of the course:
  Ammunition Inspection