## Slide 1
Weapons and Ammunition Management in UN Peace Operations
Ammunition Inspection
Notes: Key Reference Documents for this lesson:
UN Manual on Ammunition Management
UN Weapons and Ammunition Management Policy (WAM)
International Ammunition Technical Guidelines (IATG)
http://data.unsaferguard.org/iatg/en/IATG-07.20-Inspection-ammunition-IATG-V.3.pdf
All photographs in this lesson are © United Nations unless otherwise stated.

## Slide 2: Objective
Apply inspections to the safe and secure management of ammunition.
Notes: Main idea/objective for slide:
Phase 1. Introduction - Introduce the objectives of the lesson.
(Enabling Objective: 2.2.8 Apply inspections to the safe and secure management of ammunition.)
What the instructor should cover (in addition to slide content)
By the end of this training session the participant will apply inspections to the safe and secure management of ammunition.

## Slide 3: Lesson overview
Discuss the Purpose of Surveillance and Proof
Discuss the Degradation of Explosives and Propellants
Discuss the determination of ammunition surplus and stock management of an explosive storage site
Discuss the ESH Inspection Matrix and early warnings of expired ammunition during inspections
Apply ammunition surveillance procedures to an explosive storage site
Examine ammunition inspection during UN peacekeeping operations
Notes: Main idea/objective for slide:
Introduce the Key Learning Points
What the instructor should cover (in addition to slide content)
Key Learning Points
2.2.8.1 Discuss the Purpose of Surveillance and Proof
2.2.8.2 Discuss the Degradation of Explosives and Propellants
2.2.8.3 Discuss the determination of Ammunition Surplus
2.2.8.4 Discuss stock management of an explosive storage site
2.2.8.5 Discuss the ESH Inspection Matrix
2.2.8.6 Discuss the early warnings of expired ammunition during inspections
2.2.8.7 Apply ammunition surveillance procedures to an explosive storage site
2.2.8.8 Examine ammunition inspection during UN peacekeeping operations

## Slide 4
The Importance of Ammunition Surveillance
Notes: Phase 1. Introduction (Time allocation - 20 min)

## Slide 5
What are the risks when there are poor or no ammunition surveillance and inspection plans?
Notes: Main idea/objective for slide:
Ask participants to identify risks when there are poor or no ammunition surveillance and inspection plans
What the instructor should cover (in addition to slide content)
Explore with participants the likelihood and the impact of a serious event when inadequate ammunition surveillance, stock management or poor inspection plans are in place.
Write ideas on a flipchart

## Slide 6: Why do we need Ammunition Surveillance?
Ammunition contains high energy material and is designed to be as lethal as possible during its use.
Ammunition has a shelf life which depends on:
  Its design.
  The chemistry of the propellants/explosives.
  Its ease of deterioration/ decomposition.
Ammunition deteriorates with age to dangerous levels
T/PCC Leadership must know the Shelf Life of ammunition within their camps
Notes: Main idea/objective for slide:
Discuss the importance of ammunition surveillance to ensure maximum safety in ammunition and explosive storage
What the instructor should cover (in addition to slide content)
UN Manual of Ammunition Management
Ammunition contains high energy material and is designed to be as lethal as possible during its use.
It is also designed to be as safe as any other equipment during its transportation, handling and operation.
Ammunition has an assigned shelf life which depends on its design, the chemistry of the propellants/explosives used and is prone to deterioration/ decomposition even under normal storage conditions.
The quality of ammunition deteriorates with age due to environmental factors, including changes in safety, reliability and effectiveness.
Accordingly, ammunition has an assigned shelf life, defined as the life of its subsystem with the lowest shelf life under normal conditions of storage.
However, the operational exposure of ammunition varies, hence functional life may be different.
It is imperative for mission leadership to understand the shelf life of ammunition in their camps to allow for an overall assessment of risk and replenishment requirements.

## Slide 7: Ammunition Surveillance in UN Missions
Who:
Regular ammunition surveillance is the responsibility of T/PCCs.
At least one ATO or a technical expert with each contingent.
SATO shall monitor the surveillance of T/PCCs and confirm such during periodic inspections.
Notes: Main idea/objective for slide:
Discuss the importance of ammunition surveillance to ensure maximum safety in ammunition and explosive storage
What the instructor should cover (in addition to slide content)
UN Manual of Ammunition Management
In field missions, regular ammunition surveillance is the responsibility of T/PCCs. It requires the deployment of at least one ATO or a technical expert with each contingent as part of the prescribed troop strength.
Technical support, if needed, shall be provided by the SATO.
The SATO shall monitor the surveillance of T/PCCs and confirm such during periodic inspections, or as required.

## Slide 8: Prior to Deployment
T/PCCs will:
  Provide a list of ammunition planned for deployment
  Include all dates of manufacture and shelf-life certificates
  Provide a “Safe to Deploy” certificate (Manual of Ammunition , Annex C)
Emergency deployment/redeployment:
  Ammunition may be moved or deployed quickly on a case-by-case basis
  SATO to monitor replenishment plan closely.
Notes: Main idea/objective for slide:
Discuss ammunition management responsibilities of T/PCCs prior to deployment
References/further reading
UN Manual of Ammunition Management
Prior to deployment, T/PCCs must provide a list of ammunition planned for deployment along with the date of manufacture and remaining shelf life.
The PDV Team shall confirm the remaining shelf life and condition of ammunition in accordance with these guidelines.
T/PCCs are to provide ‘safe to deploy’ certificates as per Form IATG 04.20, Annex C during PDV.
In case of redeployment from one mission to another, and emergency deployment where T/PCCs might have ammunition which does not meet the above criteria, exceptions may be provided to deploy it on a case-by-case basis.
In these cases, T/PCCs may be allowed to deploy with existing ammunition on the condition that they replace it as soon as possible.
The replenishment plan for such ammunition will be monitored by the SATO during the COE operational readiness inspections.

## Slide 9: Shelf-Life of Ammunition
Provided by the manufacturer.
Is the expiration date that will be adhered to by all T/PCCs.
T/PCCs are to provide adequate storage conditions to avoid the reduction in shelf life due to degradation.
SATO can deem the ammunition unserviceable, if:
  T/PCCs do not have the Shelf-Life Certificate.
  The ammunition has signs of physical deterioration.
Notes: Main idea/objective for slide:
Emphasise the importance of the shelf life of ammunition and explosives and the need to monitor the age of all stored explosives.
What the instructor should cover (in addition to slide content)
Ask the participants how they can find out about the shelf life of their service ammunition – who can they ask?
References/further reading
UN Manual of Ammunition Management
The shelf life of ammunition is provided by the manufacturer.
T/PCCs shall provide the date of manufacture to ascertain the balance of ammunition shelf life.
This should be provided during the PDV and on deployment.
The shelf life of the ammunition stored under ideal conditions (specified by the manufacturer) shall be considered the shelf life as stated by its manufacturer.
The T/PCCs are to make every effort to provide the ammunition containers with adequate temperature and humidity control to avoid reduction in shelf life due to climatic conditions.
When such measures are not provided, the T/PCC must conduct regular tests of their ammunition and provide shelf life certificates.
When the T/PCC fails to provide shelf life certificates before the ammunition’s expiration, the mission SATO can declare the ammunition unserviceable.
The SATO may declare any ammunition unserviceable based on the physical deterioration signs.

## Slide 10: Upper-Age Limit of Ammunition
T/PCCs are to deploy with ammunition with a shelf-life greater than the expected length of deployment
Ammunition with the shortest shelf life will be consumed as training ammunition and be replenished with new operational ammunition……..
How do you ensure that?
Notes: Main idea/objective for slide:
Emphasise the importance of the shelf life of ammunition and explosives and the need to monitor the age of all stored explosives.
References/further reading
UN Manual of Ammunition Management
T/PCCs are supposed to deploy to the mission with ammunition with an expected life in excess of the anticipated length of deployment as per COE Manual A/72/288, Chapter 3, Annex A, paragraph 31.
It is necessary to fix the upper age limit of ammunition being deployed in the mission area assuming that the ammunition was stored under ideal conditions by the T/PCCs or the conditions otherwise specified by the T/PCC to avoid the untimely disposal of shelf life expired ammunition.
Under ideal conditions, ammunition with the shortest shelf life will be consumed as training ammunition for standard training and be replenished with new operational ammunition.

## Slide 11: Upper-Age Limit of Ammunition
Ammunition will NOT be accepted if:
  It has crossed ½ of its original shelf life as stated by manufacturer
T/PCCs must produce a Shelf-Life Certificate (prior to deployment) for all ammunition stating:
  The production year and estimated shelf life of the ammunition being deployed.
  That it is “Safe to Deploy”.
  It is subject to a Surveillance and In-Service Proof program.
Notes: Main idea/objective for slide:
Emphasise the importance of the shelf life of ammunition and explosives and the need to monitor the age of all stored explosives.
What the instructor should cover (in addition to slide content)
Put strong emphasis on the rule that ammunition that has less than half of its shelf life left must not be sent to a UN mission.
The "Safe To Deploy' Form, must be included for all ammunition natures.
References/further reading
UN Manual of Ammunition Management
No ammunition will be accepted for deployment which has crossed ½ of its original shelf life as stated by manufacturer.
T/PCCs shall produce a manufacturer’s certificate stating the production year and estimated shelf life of the ammunition being deployed in the mission area.
T/PCCs shall certify that all ammunition deployed in support of national contingents is “safe to deploy” and is subject to a surveillance and proof program fully in compliance with the requirements of IATG 07.20 Surveillance and Proof as per IATG 04.20.
The Form at IATG 04.20 Temporary Storage, Annex C which shall be completed and distributed as indicated on the form.

## Slide 12: ‘Safe to Deploy’ Certificate
Notes: Main idea/objective for slide:
Discuss the early warnings of expired ammunition during inspections
What the instructor should cover (in addition to slide content)
Give this Certificate as a Hand-out to participants
References/further reading
IATG 04.20 Temporary Storage
Annex C

## Slide 13: Ammunition Surveillance in UN Missions
To confirm or assess:
The environmental conditions to which ammunition systems have been exposed to.
Any physical degradation of the condition of the ammunition.
Any degradation of ammunition and component performance:
  Recording and monitoring reliability and defect reports.
  Carrying out functional proof (performance) firing.
  Gathering performance data during training use.
Changes in the physical and chemical characteristics of energetic materials and non-energetic materials judged to affect the life of the ammunition.
Notes: Main idea/objective for slide:
Discuss the importance of ammunition surveillance to ensure maximum safety in ammunition and explosive storage
What the instructor should cover (in addition to slide content)
UN Manual of Ammunition Management
T/PCCs shall regularly conduct surveillance to confirm or assess:
  The environmental conditions to which ammunition systems have been exposed during their storage and deployment to date. This information can be used to confirm either ammunition stock records or data from environmental data logs;
  Any physical degradation of the condition of the ammunition;
  Any degradation of ammunition and component performance, which is possible through:
  Recording and monitoring reliability and defect reports concerning in-service usage of the ammunition system;
  Carrying out functional proof (performance) firing if facilities are available; and/or,
  Gathering performance data during training use, if ranges are available.
  Changes in the physical and chemical characteristics of energetic materials and non-energetic materials judged to affect the life of the ammunition, when a laboratory is available, or a field test is possible
The design of the ammunition surveillance program should be determined by the complexity of the ammunition and the likely failure mechanisms. Analysis of these factors should then determine the types and frequency of inspections and tests that are required to make assessments of future in-service /shelf life.

## Slide 14: Stockpile Management Practices: Expired Ammunition
SATO may declare ammunition unserviceable:
Based on the physical condition of the ammunition on inspection
The expiration dates provided by T/PCCs
Reduced Shelf life based on storage conditions
T/PCC fail to provide a Shelf-Life Certificate
Notes: Main idea/objective for slide:
Discuss the importance of stockpile management practices to ensure maximum safety in ammunition and explosive storage
What the instructor should cover (in addition to slide content)
UN Manual of Ammunition Management
As described in Chapter 3, the Mission SATO or appropriate representatives will confirm the expiration of ammunition shelf life during the inspection and can declare it unserviceable based on its physical condition, the expiration dates, reduced shelf life based on storage conditions or when T/PCCs fail to provide the certificate of extended or balance of shelf life.
T/PCCs are responsible to plan and process for the replenishment of ammunition nearing expiration well in advance.
Upon receiving the warning of ammunition proceeding towards expiration, T/PCCs may request a shelf life extension certificate from their national technical authority following the process described in IATG 07.20 or may request the replenishment of said ammunition.
This process of shelf life extension or replenishment must be completed before the expiration of the ammunition and its subsequent disposal.

## Slide 15: Stockpile Management Practices Early Warning of Expiration
SATO will notify T/PCCs of expiring ammunition when:
  On routine inspection
  When at least 18 months left prior to expiration
  Otherwise reported
If no Replenishment Plan or Extension Certificate provided to SATO the issue will be escalated to the respective Permanent Mission in New York, through UNHQ.
Notes: Main idea/objective for slide:
Discuss the importance of stockpile management practices to ensure maximum safety in ammunition and explosive storage
What the instructor should cover (in addition to slide content)
UN Manual of Ammunition Management
As per mission-specific guidelines (based on this manual) the shelf life of ammunition will be determined by the mission SATO.
Accordingly, when at least 18 months are left before expiration of any type of ammunition, as identified during inspection or otherwise reported, T/PCCs will be notified about the state of the expiring ammunition through their contingent commanders or the contingent ATOs/technical experts.
If no action is taken by the T/PCC for the replenishment of such ammunition, or provision of extension of shelf life certificate within six months, the mission will request UNHQ to raise this issue with the respective Permanent Mission in New York.
Upon confirmation of expiring ammunition, T/PCCs will obtain clearance from the mission SATO/COE Unit for processing its replenishment.
In this case, the SATO/COE Unit will check the records for its initial deployment and confirm that the ammunition was deployed in the mission with considerable shelf life remaining as specified in these guidelines and has lost its shelf life being deployed in the mission area.
Thereafter, the Force/Police HQ will recommend the ammunition for replenishment.
If the T/PCCs are unable to provide the shelf life extension certificate for the ammunition which has expired (as specified by the manufacturer, this manual or as otherwise instructed by appropriate authority, the SATO or his/her appropriate representative will declare the ammunition unserviceable according to COE procedures regardless of its physical condition.
Weapons without serviceable ammunition will also be declared unserviceable until the replenishment is completed.

## Slide 16: EXERCISE If this ammo came with a certificate of a 20 year shelf life when should you inform your Commander. Was manufactured May 2002. Camp opened in 2001…
Notes: DEC 2020

## Slide 17
Degradation of Ammunition and Explosives
Notes: Phase 2. Development (Time allocation - 150 min)
Stage 1 (Time allocation 50 mins) – Degradation of ammunition and explosives

## Slide 18: Ageing and Degradation of Ammunition & Explosives
For most ammunition, one or two of the degradation mechanisms will limit its available life.
Some of the more common failure mechanisms include:
  Physical
  Chemical
  Climatic
Notes: Main idea/objective for slide:
Discuss the effects of ageing and degradation of ammunition and explosives and the risks posed to the entire Field Storage Area.
What the instructor should cover (in addition to slide content)
Ask the participant questions to clarify they understand the difference between Physical, Chemical and Climatic failure
References/further reading

## Slide 19: Degradation of Ammunition: Physical Mechanism
Energetic materials:
  De-bonding between the material and inert surfaces.
  Stabilizer depletion within the energetic material.
  Migration of compounds within the energetic material.
  Cracking of brittle materials; compatibility problems.
Electronics:
  Component ageing; and/or component shock damage.
Structure:
  O-ring failure.
  Mechanical damage (impact, corrosion); and/or vibration.
Notes: Main idea/objective for slide:
Discuss the effects of ageing and degradation of ammunition and explosives and the risks posed to the entire Field Storage Area.
What the instructor should cover (in addition to slide content)
Discuss the early warnings of expired ammunition during inspections
References/further reading

## Slide 20: Degradation of Ammunition: Chemical Mechanism
Explosives are chemical compositions that breakdown, migrate or change over time.
This breakdown is accelerated with:
  Increased temperature
  Low temperatures
  Large variations in temperature - cycling from hot to cold
  High or low humidity
  Vibration
  Shock
  Pressure
The conditions under which the ammunition is stored is critical
Notes: Main idea/objective for slide:
Discuss the impact of chemical stability on explosives and propellants when subjected to poor climatic conditions or when they have aged beyond serviceable life.
What the instructor should cover (in addition to slide content)
Before showing this slide, ask the participants what types of activity can accelerate the degradation of ammunition
References/further reading
UN Manual of Ammunition Management
In addition to the physical damage caused by shock and vibration, ammunition also degrades chemically.
The energetic items that cause the explosive effect are invariably of organic chemical composition and, in common with all other chemical compositions’ breakdown, migrate or change over time.
This change is normally accelerated with increased temperature.
Degradation is be hastened by: large variations in temperature (i.e., cycling from hot to cold); low temperatures; high or low humidity; vibration; shock; and/or pressure.
The conditions under which ammunition is stored, maintained and transported during its normal in-service life will eventually have an impact on the ammunition and a critical failure mode will be reached, which will be the service-life limiting factor

## Slide 21: Degradation of Ammunition: Climatic Mechanism
Explosives are designed for stated climatic conditions.
Excess Climatic conditions can deteriorate and degrade ammunition to unsafe and dangerous states.
Typical climatic conditions include:
  Weather conditions
  Hot/cold temperatures
  Direct solar radiation,
  Daily temperature changes (diurnal cycling)
  High humidity
Notes: Main idea/objective for slide:
Discuss the impact of chemical stability on explosives and propellants when subjected to poor climatic conditions or when they have aged beyond serviceable life.
What the instructor should cover (in addition to slide content)
Before showing this slide, ask the participants what climatic conditions can accelerate the degradation of ammunition
References/further reading
UN Manual of Ammunition Management
The effects of weather, hot/cold temperatures, direct solar radiation, daily temperature changes (diurnal cycling) and high humidity may rapidly degrade the performance and safety of explosives.
Ammunition is designed for use under stated climatic conditions, and its service life will be significantly reduced if it is stored under climatic conditions for which it was not designed.
In cases of severe climatic change, ammunition may rapidly become unserviceable and dangerous to use.

## Slide 22: Examples of Ammunition
Notes: Main idea/objective for slide:
Using relevant imagery, provide the participants with examples of ammunition and explosives which have been degraded to unsafe conditions whether through age or other environmental factors.
What the instructor should cover (in addition to slide content)
Using the images provided, go through each image and ask the participants to comment on:
What signs of degradation can they see?
What do they believe caused this degradation?
What is the most likely outcome if this is not rectified

## Slide 23: Examples of Ammunition
Notes: Main idea/objective for slide:
Using relevant imagery, provide the participants with examples of ammunition and explosives which have been degraded to unsafe conditions whether through age or other environmental factors.
What the instructor should cover (in addition to slide content)
Using the images provided, go through each image and ask the participants to comment on:
What signs of degradation can they see?
What do they believe caused this degradation?
What is the most likely outcome if this is not rectified

## Slide 24: Examples of Ammunition
Notes: Main idea/objective for slide:
Using relevant imagery, provide the participants with examples of ammunition and explosives which have been degraded to unsafe conditions whether through age or other environmental factors.
What the instructor should cover (in addition to slide content)
Using the images provided, go through each image and ask the participants to comment on:
What signs of degradation can they see?
What do they believe caused this degradation?
What is the most likely outcome if this is not rectified

## Slide 25: Examples of Ammunition
Notes: Main idea/objective for slide:
Using relevant imagery, provide the participants with examples of ammunition and explosives which have been degraded to unsafe conditions whether through age or other environmental factors.
What the instructor should cover (in addition to slide content)
Using the images provided, go through each image and ask the participants to comment on:
What signs of degradation can they see?
What do they believe caused this degradation?
What is the most likely outcome if this is not rectified

## Slide 26: Examples of Ammunition
Notes: Main idea/objective for slide:
Using relevant imagery, provide the participants with examples of ammunition and explosives which have been degraded to unsafe conditions whether through age or other environmental factors.
What the instructor should cover (in addition to slide content)
Using the images provided, go through each image and ask the participants to comment on:
What signs of degradation can they see?
What do they believe caused this degradation?
What is the most likely outcome if this is not rectified

## Slide 27: Examples of Ammunition
Notes: Main idea/objective for slide:
Using relevant imagery, provide the participants with examples of ammunition and explosives which have been degraded to unsafe conditions whether through age or other environmental factors.
What the instructor should cover (in addition to slide content)
Using the images provided, go through each image and ask the participants to comment on:
What signs of degradation can they see?
What do they believe caused this degradation?
What is the most likely outcome if this is not rectified

## Slide 28: Examples of Ammunition
Notes: Main idea/objective for slide:
Using relevant imagery, provide the participants with examples of ammunition and explosives which have been degraded to unsafe conditions whether through age or other environmental factors.
What the instructor should cover (in addition to slide content)
Using the images provided, go through each image and ask the participants to comment on:
What signs of degradation can they see?
What do they believe caused this degradation?
What is the most likely outcome if this is not rectified

## Slide 29: Examples of Ammunition
Notes: Main idea/objective for slide:
Using relevant imagery, provide the participants with examples of ammunition and explosives which have been degraded to unsafe conditions whether through age or other environmental factors.
What the instructor should cover (in addition to slide content)
Using the images provided, go through each image and ask the participants to comment on:
What signs of degradation can they see?
What do they believe caused this degradation?
What is the most likely outcome if this is not rectified

## Slide 30: Examples of Expired Ammunition
Notes: Main idea/objective for slide:
Using relevant imagery, provide the participants with examples of ammunition and explosives which have been degraded to unsafe conditions whether through age or other environmental factors.
What the instructor should cover (in addition to slide content)
Using the images provided, go through each image and ask the participants to comment on:
What signs of degradation can they see?
What do they believe caused this degradation?
What is the most likely outcome if this is not rectified

## Slide 31: Degradation of Ammunition: Climatic Mechanism
During prolonged storage:
  Rate of propellant chemical deterioration is at least doubled for every 10°C rise in temperature above 30°C.
Propellant is designed with a shelf life of 15 to 40 years at temperate climates.
In high heat environments, the stabilizer depletes more rapidly, leading to:
  Spontaneous ignition of the propellant in storage
Notes: Main idea/objective for slide:
Discuss the impact of chemical stability on explosives and propellants when subjected to poor climatic conditions or when they have aged beyond serviceable life.
What the instructor should cover (in addition to slide content)
Discuss why propellant is more prone to this type of degradation.
Put heavy emphasis on the potential for auto-ignition – ensure the participants understand the consequences and possible likelihood of such an event
References/further reading
UN Manual of Ammunition Management
During prolonged periods of storage, the rate of propellant chemical deterioration is approximately doubled for every 10°C rise in temperature above 30°C.
Most propellants, dependent on design, have a shelf life of at least 15 to 40 years when stored at a constant 30°C, and will last much longer in temperate climates.
In high heat environments the stabilizer is depleted far quicker and the probability of spontaneous combustion due to autocatalytic ignition becomes much higher.
If a T/PCC is unable to provide constant storage conditions below 30°C or provide specific in-service proof and surveillance details, the mission SATO can reduce the accepted shelf life according to IATG 7.10 Para 7.3.
Necessary early replenishment of ammunition is a national responsibility.

## Slide 32: Propellant degradation due to High Temperatures
Temperature (°C) | Projected Shelf Life (Years) |  |  |  | 
20 | 15.0 | 20.0 | 30.0 | 40.0 | Initial In-Service Shelf Life.
30 | 15.0 | 20.0 | 30.0 | 40.0 | Significant degradation starts after 30ºC
40 | 7.5 | 10.0 | 15.0 | 20.0 | 
50 | 3.75 | 5.0 | 7.5 | 10.0 | 
60 | 1.83 | 2.5 | 3.75 | 5.0 | 
70 | 0.92 | 1.25 | 1.83 | 2.5 | This propellant is now approaching a dangerous condition and should be destroyed as soon as possible.
80 | 0.46 | 0.62 | 0.92 | 1.25 | 
90 | 0.23 | 0.31 | 0.46 | 0.62 | 
Notes: Main idea/objective for slide:
Discuss the impact of chemical stability on explosives and propellants when subjected to poor climatic conditions or when they have aged beyond serviceable life.
What the instructor should cover (in addition to slide content)
Provide this table as a Hand-out to participants
References/further reading
IATG 04.20 – Temporary Storage
Clause 8.1 indicated that ammunition could theoretically reach external surface temperatures of 1010C in the Middle East, although internal temperatures would be substantially less.
Propellant degradation and stabiliser depletion is not linear, and the decay rate reduces during the night when the ammunition cools.
Yet it is clear that field and temporary storage conditions for propellant in these types of temperature extremes would not be a particularly sensible idea.
If operationally necessary the propellant should be separated from the parent ammunition wherever possible during Temporary Field Storage in such climatic conditions.
IATG 07.20:2015[E] Surveillance and proof contains further technical information on the degradation of explosives and should be consulted prior to undertaking field or temporary storage of ammunition.

## Slide 33
Surveillance and Inspection Plans
Notes: Phase 2. Development (Time allocation - 150 min)
Stage 2 (Time allocation 50 mins) – Surveillance and inspection plans

## Slide 34: Purpose of Surveillance
To ensure the safety and stability of ammunition in storage.
To ensure the safety, reliability and performance of ammunition during use.
To predict and therefore prevent ammunition failures that are inherent in their design or the result of aging.
To monitor the environmental conditions under which the ammunition has been stored.
To ensure that the first point of detection of catastrophic failures is not the user.
Notes: Main idea/objective for slide:
Introduce the participants to the purpose of surveillance and in-service proof of their ammunition and explosive stocks and how this is achieved.
What the instructor should cover (in addition to slide content)
Ask the participants to give reasons why we must put in place a surveillance plan and what should it involve?
Write these answers on the white board
References/further reading
UN Manual of Ammunition Management
The safety and stability of ammunition in storage can only be established by a comprehensive ‘Ammunition Surveillance’ system that uses a methodology of both physical inspection by trained personnel and chemical analysis.
The surveillance is carried out systematically by evaluating the characteristics and properties the ammunition type possesses and measuring how the ammunition performs throughout its entire life cycle to allow assessment of the safety, reliability and operational effectiveness of the ammunition.
Surveillance and in-service proof can be used to extend the shelf life of ammunition if appropriate.

## Slide 35: Purpose of Surveillance
To predict failure and degraded performance in support of effective ammunition procurement cycles;
To predict future performance, service life and limitations;
To extend the in-service life of ammunition beyond that which it would normally have without such a system; and
To identify and monitor critical characteristics of the ammunition that change with age and exposure to the environment.
Notes: Main idea/objective for slide:
Introduce the participants to the purpose of surveillance and in-service proof of their ammunition and explosive stocks and how this is achieved.
What the instructor should cover (in addition to slide content)
Ask the participants to give reasons why we must put in place a surveillance plan and what should it involve?
Write these answers on the white board
References/further reading
UN Manual of Ammunition Management
The safety and stability of ammunition in storage can only be established by a comprehensive ‘Ammunition Surveillance’ system that uses a methodology of both physical inspection by trained personnel and chemical analysis.
The surveillance is carried out systematically by evaluating the characteristics and properties the ammunition type possesses and measuring how the ammunition performs throughout its entire life cycle to allow assessment of the safety, reliability and operational effectiveness of the ammunition.
Surveillance and in-service proof can be used to extend the shelf life of ammunition if appropriate.

## Slide 36: Requirements for Effective Surveillance activities
Surveillance and in-service proof requires an integrated range of capabilities and mechanisms to ensure overall system efficiency and effectiveness:
An effective ammunition management plan.
A trained and experienced technical staff.
A capable explosives laboratory.
An effective sampling mechanism.
An efficient ammunition accounting system.
Notes: Main idea/objective for slide:
Emphasise the requirements for effective surveillance and in-service proof activities, including the responsibilities of all key personnel involved
What the instructor should cover (in addition to slide content)
Ask the participants to give reasons why we must put in place a surveillance plan and what should it involve?
Write these answers on the white board
References/further reading
UN Manual of Ammunition Management
The safety and stability of ammunition in storage can only be established by a comprehensive ‘Ammunition Surveillance’ system that uses a methodology of both physical inspection by trained personnel and chemical analysis.
The surveillance is carried out systematically by evaluating the characteristics and properties the ammunition type possesses and measuring how the ammunition performs throughout its entire life cycle to allow assessment of the safety, reliability and operational effectiveness of the ammunition.
Surveillance and in-service proof can be used to extend the shelf life of ammunition if appropriate.

## Slide 37: Requirements for Effective Surveillance activities
Ammunition sampled in home countries:
  No laboratory conditions in missions.
  Shelf life certificates to be provided to T/PCCs.
Based on results:
  Extension to service life may be permitted.
  Ammunition sentenced for destruction.
No ammunition will be accepted for deployment which
has crossed its ½ of the original shelf life
Notes: Main idea/objective for slide:
Emphasise the requirements for effective surveillance and in-service proof activities, including the responsibilities of all key personnel involved
What the instructor should cover (in addition to slide content)
Ask the participants to give reasons why we must put in place a surveillance plan and what should it involve?
Write these answers on the white board
References/further reading
UN Manual of Ammunition Management
An effective system of surveillance and in-service proof requires an integrated range of capabilities and mechanisms to ensure overall system efficiency and effectiveness.
These are:
  An effective ammunition management plan;
  A trained and experienced technical staff;
  A capable explosives laboratory;
  An effective sampling mechanism; and
  An efficient ammunition accounting system.
An explosives laboratory and the ability to conduct sample tests are not available in-mission, the T/PCCs shall conduct these tests, preferably on ammunition from the same batch and stored in similar conditions, in their home countries and provide certificates of balance of shelf life for the deployed ammunition.
Based on the results of the surveillance and in-service proof, decisions may be taken on the extension of the in- service life of an ammunition, or the need for its destruction. T
o simplify and reduce these difficult procedures as much as possible, no ammunition will be accepted for deployment which has crossed its ½ of the original shelf life as described under 3.5.2.
This can only be waivered by the Head of Mission, based on the WAAB recommendation.

## Slide 38: Responsibility for Surveillance and in-service proof
The contingent ATO will:
Develop and carry out an in-service proof and surveillance plan for each ammunition type
Ensure ammunition has NOT crossed ½ of its original shelf life.
Ensure that ammunition is allocated the appropriate condition code.
Rapidly identification stocks that are unsafe to either use or store.
Ensure that the disposal of expired stocks takes place within an expedient time.
Notes: Main idea/objective for slide:
Emphasise the requirements for effective surveillance and in-service proof activities, including the responsibilities of all key personnel involved
What the instructor should cover (in addition to slide content)
Before showing this slide, ask the participants what the duties of a Contingent ATO are?
Write these on a white board
References/further reading
UN Manual of Ammunition Management
The contingent ammunition technical officer or a technical expert should be responsible for:
The development and promulgation of an in-service proof and surveillance plan for each ammunition type in the national inventory;
Ensuring that the plan is carried out;
Coordination with their respective national authorities on the requirement of tests, provision of certificates and delivery of ammunition that has NOT crossed ½ of its original shelf life.
Ensuring that ammunition is allocated the appropriate condition code;
Rapid identification of stocks that are unsafe to either use or store; and,
Ensuring that the disposal of expired stocks takes place within an expedient time period following in-service proof and surveillance.

## Slide 39: Surveillance and Inspection: Condition Codes
All ammunition and explosives should be classified or reclassified as to their condition, following any inspection process
Notes: Main idea/objective for slide:
Highlight the requirements for using Condition Codes across ammunition and providing information that is understandable at all levels through common reporting formats
What the instructor should cover (in addition to slide content)
participants are to be made aware of the condition codes that are used to provide consistent understanding at all levels as to the condition of ammunition under inspection.
Provide the table as a handout
References/further reading
IATG 07.20 Inspection of Ammunition, Page 10
The following groupings and codes can be used as a means of classifying the condition of ammunition stocks

## Slide 40: Surveillance and Inspection: Defect Codes
Defect Type | Effect Code | Ammunition Status
Critical | 1 | Defects affecting safety in storage, handling, transportation or use.
Major | 2 | Defects that affect the performance of the ammunition and that require remedial action to be taken.
Minor | 3 | Defects that do not affect the safety or performance of the ammunition but are of such a nature that the ammunition should not be issued prior to remedial action having been taken.
Insignificant | 4 | Any defect that does not fall into any of these categories, but which could conceivably deteriorate into one of them if no remedial action is taken.
Technical | N/A | Any defect that requires further technical investigation.
Notes: Main idea/objective for slide:
Highlight the requirements for using Defect Codes across ammunition and providing information that is understandable at all levels through common reporting formats
What the instructor should cover (in addition to slide content)
participants are to be made aware of the Defect codes that are used to provide consistent understanding at all levels as to the condition of ammunition under inspection.
Provide the table as a handout
References/further reading
IATG 07.20 Inspection of Ammunition, Page 10
When ammunition is subject to inspection and surveillance, which should be good stockpile management practice, it is inevitable that defects will be found.
These defects shall determine within which ‘Condition Type’ the ammunition item is placed, the Effect Code allocated to it, and how it is categorised according to the table

## Slide 41: Surveillance and Inspection: Common Inspection Points
Lot / Batch Numbers: Lot and/or batch numbers are to be checked against the lot and/or batch numbers on the ammunition packaging
Rust: Rust levels represent a useful indicator of the overall condition of ammunition
Rust Level (RL) |  | % of Rust on Surface Area | Serviceability Assessment | Recommended Action
Code | Summary |  |  | 
RL = 1 | Little visible rust levels | <5 | Serviceable | None
RL = 2 | Medium rust levels | >5 | Serviceable | Expend at Training
RL = 3 | Heavy rust levels | >10 | Limited Serviceability | Repair Request In-Service Proof
RL = 4 | Very heavy rust levels | >40 | Unserviceable | Destroy
Notes: Main idea/objective for slide:
Emphasise the requirements for observing common inspection points across ammunition and providing information that is understandable at all levels through common reporting formats
What the instructor should cover (in addition to slide content)
participants are to be made aware of the common Inspection Points for ammunition that are used to provide consistent understanding at all levels as to the condition of ammunition under inspection.
Provide the table as a handout
References/further reading
IATG 07.20 Inspection of Ammunition, Page 12

## Slide 42: Physical Inspection of Ammunition
Visual Inspection:
  The physical (visual) inspection of ammunition is an important component in ensuring the overall safety of the ammunition stockpile
Ammunition Packaging
  The packaging should be marked with the correct details of the ammunition
  The metal fitments should be free from oxidation (rust)
  The package should be intact with minimal external damage
  The seals are intact
Ammunition Specific Inspection Points – Annex C
See Handout
Notes: Main idea/objective for slide:
Discuss with the participants how to physically inspect ammunition and what are the most common inspection points to observe and record
What the instructor should cover (in addition to slide content)
Outline the various parts and components of ammunition that should be inspected and the observations recorded.
Print appropriate inspection points list from IATG 07.20
References/further reading
IATG 07.20 Inspection of Ammunition, Annex C "Guidance on physical inspection of ammunition"

## Slide 43: Ammunition Specific Inspection Points
Notes: Main idea/objective for slide:
Discuss with the participants how to use the Specific Inspection Point table to acquire guidance as to what to inspect on each ammunition type.
What the instructor should cover (in addition to slide content)
Provide hand-out to participant and work through the table, explaining how to use it
References/further reading
IATG 07.20 Inspection of Ammunition, Annex C "Guidance on physical inspection of ammunition"

## Slide 44: Ammunition Specific Inspection Points
Notes: Main idea/objective for slide:
Discuss with the participants how to use the Specific Inspection Point table to acquire guidance as to what to inspect on each ammunition type.
What the instructor should cover (in addition to slide content)
Provide hand-out to participant and work through the table, explaining how to use it
References/further reading
IATG 07.20 Inspection of Ammunition, Annex C "Guidance on physical inspection of ammunition"

## Slide 45
SATO
Notes: Phase 2. Development (Time allocation - 150 min)
Stage 2 (Time allocation 50 mins) – Surveillance and inspection plans

## Slide 46: SATO - Competencies
SATO Must be qualified through a national Ammunition Technical Officer’s Course according to IATG 01.90, Annex L.
Cont…
He/she should:
  Have the knowledge and understanding of DPO Ammunition Management Guidelines for Peacekeeping Operations, as well as IATG and IATG-recommended ammunition management standards and guidelines
  Have solid knowledge of Risk Management and practical knowledge of risk mitigation measures concerning ammunition management and storage
Notes: Main idea/objective for slide:
Describe the Competencies of SATO deployed in the field mission.
What the instructor should cover (in addition to slide content)
Participants are to be made aware of the competencies of SATO that are considered while selecting/nominating SATO in any field mission by UNHQ.
References/further reading
Annex D of UNMAM, Page 43

## Slide 47: SATO - Competencies
Be able to identify IQD and OQD applied from PES to PES and to an ES
Be able to plan an Ammunition Area (e.g., number of PES required, barricade requirements, appropriate IQD and OQD
Be able to organize an ammunition field depot based on economical storage principles and procedures
Have the knowledge and understanding of lightning protection systems and fire prevention requirements
Cont…
Notes: Main idea/objective for slide:
Describe the Competencies of SATO deployed in the field mission.
What the instructor should cover (in addition to slide content)
Participants are to be made aware of the competencies of SATO that are considered while selecting/nominating SATO in any field mission by UNHQ.
References/further reading
Annex D of UNMAM, Page 43

## Slide 48: SATO - Competencies
Be able to visually identify the explosive safety standards shortcomings during a survey of ammunition storage and maintenance operations
Be knowledgeable of the accident reporting procedures
Have the knowledge and understanding of lightning protection systems and fire prevention requirements
Be able to develop an SOP
Cont…
Notes: Main idea/objective for slide:
Describe the Competencies of SATO deployed in the field mission.
What the instructor should cover (in addition to slide content)
Participants are to be made aware of the competencies of SATO that are considered while selecting/nominating SATO in any field mission by UNHQ.
References/further reading
Annex D of UNMAM, Page 43

## Slide 49: SATO - Competencies
Be able to determine the risks and consequences of deviations from the regulations and communicate with the operational commander the mitigating efforts necessary to reduce or eliminate hazards
Be able to prepare draft explosives licences
Carry out periodic, operational and arrival/repatriation inspections of ammunition and explosives of T/PCC units along with the Contingent-Owned Equipment (COE) Unit team or separately
Notes: Main idea/objective for slide:
Describe the Competencies of SATO deployed in the field mission.
What the instructor should cover (in addition to slide content)
Participants are to be made aware of the competencies of SATO that are considered while selecting/nominating SATO in any field mission by UNHQ.
References/further reading
Annex D of UNMAM, Page 43

## Slide 50: Responsibilities of SATO
  Act as the senior ammunition specialist and safety officer and be responsible for advising the Force Commander on all ammunition and explosives safety matters
  Provide direction and advice on all technical matters related to ammunition/explosives
  Conduct special inspections of unserviceable, expired and segregated ammunition and explosives and recommend their disposal (in the mission area) to the concerned force EOD units/UNMAS
  Provide technical assistance and advice in connection with the safety, storage and maintenance standards of ammunition and explosives
Cont…
Notes: Main idea/objective for slide:
Describe the Responsibilities of SATO deployed in the field mission.
What the instructor should cover (in addition to slide content)
Participants are to be made aware of the responsibilities of SATO that are required to be performed by SATO in the field missions.
References/further reading
Annex D of UNMAM, Page 43

## Slide 51: Responsibilities of SATO
  Conduct Dangerous Goods (DG)-Ammunition / Explosives inspections
  Coordinate risk assessments
  Prepare/update all necessary Ammunition and Explosives Regulations and technical SOPs
  Develop and operate of the ammunition storage licensing system
Cont…
Notes: Main idea/objective for slide:
Describe the Responsibilities of SATO deployed in the field mission.
What the instructor should cover (in addition to slide content)
Participants are to be made aware of the responsibilities of SATO that are required to be performed by SATO in the field missions.
References/further reading
Annex D of UNMAM, Page 43

## Slide 52: Responsibilities of SATO
  Attend the COE and MOU Management Review Board (CMMRB)/and any meeting the matter related to ammunition and explosives
  Assist the COE Team during Operational Readiness Inspections (ORI) with expert opinion on ammunition and, to a limited extent, armaments
  Advise the PDV Team
  Act as WAAB Manager
Notes: Main idea/objective for slide:
Describe the Responsibilities of SATO deployed in the field mission.
What the instructor should cover (in addition to slide content)
Participants are to be made aware of the responsibilities of SATO that are required to be performed by SATO in the field missions.
References/further reading
Annex D of UNMAM, Page 43

## Slide 53: SATO Inspection
Annual Routine Inspection
  UN MAM Para 1.15
  UN MAM Annex C

## Slide 54: SATO - Inspection and Evaluation
Purpose of Inspection:
  To ensure that ammunition policy/guidelines are adhered to by T/PCC units
  To improve the standard of ammunition management in T/PCC units
Notes: Main idea/objective for slide:
Discuss with the participants about the purpose of inspection.
What the instructor should cover (in addition to slide content)
Highlight the importance of inspection as ammunition contains high energy material and is designed to be as lethal as possible, it is highly desired that it is safe, reliable and effective during operation, transportation and handling.
References/further reading
UNMAM-2020
IATG 07.20 Inspection of Ammunition, Annex C "Guidance on physical inspection of ammunition"

## Slide 55: Inspection and Evaluation
Inspection Criteria/Evaluation System (Annex C of UNMAM) : Ammunition Inspection Template has got 10 parts:
  Part-A: Verification
  Part-B: Storage Situation
  Part-C: Ammunition Stacks
  Part-D: Expiration and Disposal
  Part-E: Safety, Security and Fire Protection
  Part-F: Miscellaneous
  Part-G: Inspecting Officer’s Comments
  Part-H: Commanding Officer’s Opinion
  Part-J: Sector/Brigade Commander’s Opinion
  Part-K: Force Commander’s Remarks
Notes: Main idea/objective for slide:
Discuss with the participants about the frequency of inspection and how to physically inspect ammunition and what are the most common inspection points to observe and record
What the instructor should cover (in addition to slide content)
Outline the various parts and components of ammunition that should be inspected and the observations recorded.
Print template from UNMAM
References/further reading
UNMAM-2020
IATG 07.20 Inspection of Ammunition, Annex C "Guidance on physical inspection of ammunition"

## Slide 56: Inspection and Evaluation
Concurrence of Inspection & Evaluation Report:
SATO shall furnish an inspection and evaluation report on the ammunition storage conditions of the concerned T/PCC unit.
The reports shall be shared with all members of the WAAB and approved during the next WAAB meeting.
The chair of the WAAB shall be informed without delay when the minimum standards cannot be met
Notes: Main idea/objective for slide:
Discuss with the participants about the concurrence of Inspection and Evaluation Report by WAAB.
What the instructor should cover (in addition to slide content)
Highlight the importance of concurrence by WAAB as well as non-compliance.
References/further reading
UNMAM-2020

## Slide 57: Inspection and Evaluation
    SUMMARY:
    Purpose of inspection
Type of inspections
Inspection criteria/evaluation system
Concurrence of evaluation reporting
Notes: Main idea/objective for slide:
Discuss with the participants about summary.
What the instructor should cover (in addition to slide content)
Summarized the topic
References/further reading
UNMAM-2020
IATG 07.20 Inspection of Ammunition, Annex C "Guidance on physical inspection of ammunition"

## Slide 58
Participant Exercise
Notes: Phase 2. Development (Time allocation - 150 min)
Stage 3 (Time allocation 50 mins) – participant Exercise

## Slide 59: Exercise
During a recent ammunition inspection of a new ammunition consignment to Camp FOLSA, UNAC SATO highlighted the following images and has requested a suitable surveillance and inspection plan be put in place immediately
In each case provided, SATO has asked for comment:
What are the visible deteriorations observed in each munition?
What are the likely causes for this deterioration?
The likelihood of an explosive event if no mitigation measures are included
What mitigation measures can be employed each case?
What inspection activities will you undertake to manage this ammunition in its current state?
Is this ammunition SERVICEABLE and SAFE TO DEPLOY?
Notes: Main idea/objective for slide:
participant exercise to suggest appropriate surveillance actions for different images, providing rationale for each action
What the instructor should cover (in addition to slide content)
In groups, participants will be provided a range of images showing ammunition and explosives. Instructors are to move around the class and help participants where required. Teamwork is permitted where preferred.
When complete, work through the answers with the class and ask questions
participant Activity
participants must review the images provided, suggest the surveillance actions they will take in each case, providing rationale for doing so.
Each group, will provide a back brief on one image. participants must review all images in the manner above.
The Instructor will select the image to be briefed by the group.

## Slide 60: Lesson overview
Discuss the Purpose of Surveillance and Proof
Discuss the Degradation of Explosives and Propellants
Discuss the determination of Ammunition Surplus and stock management of an explosive storage site
Discuss the ESH Inspection Matrix and early warnings of expired ammunition during inspections
Apply ammunition surveillance procedures to an explosive storage site
Examine ammunition inspection during UN peacekeeping operations
Notes: Phase 3. Consolidation (Time allocation - 10 min)
Main idea/objective for slide:
Recap Key Learning Points
participant activity
Give participants opportunity to ask any questions
What the instructor should cover (in addition to slide content)
Key Learning Points
2.2.8.1 Discuss the Purpose of Surveillance and Proof
2.2.8.2 Discuss the Degradation of Explosives and Propellants
2.2.8.3 Discuss the determination of Ammunition Surplus
2.2.8.4 Discuss stock management of an explosive storage site
2.2.8.5 Discuss the ESH Inspection Matrix
2.2.8.6 Discuss the early warnings of expired ammunition during inspections
2.2.8.7 Apply ammunition surveillance procedures to an explosive storage site
2.2.8.8 Examine ammunition inspection during UN peacekeeping operations

## Slide 61
Look Ahead: Range Management
Weapons and Ammunition Management in UN Peace Operations
Notes: Main idea/objective for slide:
Look ahead to the next lesson of the course:
  Range Management