## Slide 1
Weapons and Ammunition Management in UN Peace Operations
Range Management
Notes: Key Reference Documents for this lesson:
UN Manual on Ammunition Management
UN Weapons and Ammunition Management Policy (WAM)
International Ammunition Technical Guidelines (IATG)
All photographs in this lesson are © United Nations unless otherwise stated.

## Slide 2: Objective
Examine range management procedures.
Notes: Main idea/objective for slide:
Phase 1. Introduction - Introduce the objectives of the lesson.
(Enabling Objective: 2.2.9 Examine range management procedures.)
What the instructor should cover (in addition to slide content)
By the end of this training session the participant will examine range management procedures.

## Slide 3: Lesson overview
Discuss necessity, responsibility and planning for the disposal of unserviceable ammunition
Discuss the provision of Ranges, Range Siting Boards and Safety Boards
Discuss issuing a "Certificate of Disposal" for unserviceable ammunition
Examine Ammunition Destruction - Burning Tanks, Open Burning & Open Detonation
Examine the safe use, construction and closure of Ranges
Notes: Main idea/objective for slide:
Introduce the Key Learning Points
What the instructor should cover (in addition to slide content)
Key Learning Points
2.2.9.1 Discuss necessity, responsibility and planning for the disposal of Unserviceable ammunition
2.2.9.2 Discuss the provision of Ranges, range siting Boards and safety Boards
2.2.9.3 Discuss the issuing of a "Certificate of Disposal" of unserviceable Ammunition
2.2.9.4 Examine Ammunition Destruction - Burning Tanks, Open Burning & Open Detonation
2.2.9.5 Examine the safe use, construction and closure of Ranges

## Slide 4
UN Range Management – Guidance Documents
Notes: Phase 1. Introduction (Time allocation - 15 min)

## Slide 5: Guidance Documents
In UN and IATG documents Range Management is covered in the
UN WAM Policy
Manual on Ammunition Management Chapter 4: Expiration, Replenishment and Disposal of Ammunition
IATG 10.10 Demilitarisation, destruction and logistic disposal of conventional ammunition
UN COE Manual
Notes: Main idea/objective for slide:
Highlight the 4 key reference documents that relate to the effective and safe range management on operational missions.

## Slide 6: 1. UN WAM Policy
The WAAB shall be responsible for providing advice on all WAM related aspects, with the exception of use of force.
The disposal of ammunition shall be in accordance with IATG 10.10.
Detailed procedures are included in the UNMAM, IATG, IMAS and UN COE manual.
Notes: Main idea/objective for slide:
Highlight the content in the UN WAM Policy that relates to the effective and safe range management on operational missions.

## Slide 7: 2. Manual on Ammunition Management
Early warning of expired ammunition during inspections
Shelf life of ammunition determined by SATO
T/PCC’s will be notified about state of expiring ammunition through contingent commanders/ATOs
T/PCC has 6 months to take action
  Replenishment
  Extension of shelf life
If no action taken mission HQ will escalate the issue to UNHQ where it will be raised with the Permanent Mission.
Notes: Main idea/objective for slide:
Highlight the content in the Manual on Ammunition Management that relates to the effective and safe range management on operational missions.

## Slide 8: 2. Manual on Ammunition Management
Processing replenishment / shelf life extension certificate of expiring ammunition
Shelf life extension certificate may be requested from the T/PCC national technical authority (IATG 07.20)
T/PCC’s may be requested to replenish said ammunition
Either option must be completed before expiration of ammunition and its subsequent disposal
Notes: Main idea/objective for slide:
Highlight the content in the Manual on Ammunition Management that relates to the effective and safe range management on operational missions.

## Slide 9: 2. Manual on Ammunition Management
Replenishment of unserviceable ammunition
T/PCC’s to obtain clearance from SATO/COE Unit for processing replenishment
SATO/COE will check records of initial deployment to confirm that it had considerable shelf life remaining when deployed
Force/Police HQ will then recommend ammunition replenishment
Notes: Main idea/objective for slide:
Highlight the content in the Manual on Ammunition Management that relates to the effective and safe range management on operational missions.

## Slide 10: 2. Manual on Ammunition Management
Disposal of Unserviceable Ammunition
Unserviceable ammunition must be disposed of due to the risk that it poses to the safety of UN personnel, local population and environment.
Contingent commander will obtain permission for disposal from the national authorities.
Force EOD units are responsible for the disposal of unserviceable ammunition. If there are no EOD units in the mission then UNMAS may be requested to carry out the disposal.
Explosives used in the disposal will be reimbursed as per the COE manual.
Notes: Main idea/objective for slide:
Highlight the content in the Manual on Ammunition Management that relates to the effective and safe range management on operational missions.
What the instructor should cover (in addition to slide content)
Discuss necessity, responsibility and planning for the disposal of Unserviceable ammunition

## Slide 11: 2. Manual on Ammunition Management
Certificate of Disposal of Unserviceable Ammunition
A certificate of destruction will be rendered by the Force EOD unit / UNMAS and this will be sent to the military and police unit with a copy sent to SATO and COE unit.
The creation of the Operational Ammunition Expenditure Certificate (OAEC) will be in line with the COE Manual and the COE Field Verification and Control Guidelines. This should be verified by the SATO.
Notes: Main idea/objective for slide:
Highlight the content in the Manual on Ammunition Management that relates to the effective and safe range management on operational missions.
Discuss the issuing of a "Certificate of Disposal" of unserviceable Ammunition
What the instructor should cover (in addition to slide content)
Discuss necessity, responsibility and planning for the disposal of Unserviceable ammunition

## Slide 12: 3. IATG 10.10 Demilitarisation, destruction and logistic disposal of conventional ammunition
What is covered by IATG 10.10?
International legislation
Demilitarisation cycle
Technical factors which need to be addressed by the disposal unit including the emission levels and the technology that must be used to reach these levels
Demilitarisation and destruction technology and techniques (see details in later slides (19))
Management of stockpile demilitarisation or destruction
Quality management
Environmental management
Notes: Main idea/objective for slide:
Highlight the content in IATG 10.10 that relates to the effective and safe range management on operational missions.

## Slide 13
Range Safety Boards and their roles
Notes: Phase 2. Development (Time allocation - 65 min)
Stage 1 (Time allocation 20 mins) – Range Safety Boards and their roles

## Slide 14: Range Safety Board (Annex L to UNMAM)
UN missions will establish a Range Safety Board when using firing ranges provided by the host government or mission constructed
Mission constructed ranges will be built under permission of the host government and an environmental impact assessment should be carried out prior to construction (SOP 2019.09 - Environmental Impact Assessment for UN Field Missions)
A Range Siting Board shall convene to approve the location and design of the firing range
The Range Safety Board will provide certified assessments to the Range Siting Board on safety issues when mission-constructed ranges are required
The Range Safety Board will ensure that safety issues regarding the range are included in the Range Safety Orders
Notes: Main idea/objective for slide:
Discuss in depth the need for effective range management practices on a UN mission paying particular attention to the safety of troops and non-military personnel.
participant Activity
Ask participants to list who they think make up the Range Siting Board.
What the instructor should cover (in addition to slide content)
Introduce and list the members of the Range Siting Board:
  Senior military officer of rank Lieutenant Colonel (Lt Col) or above to act as chairman • Senior civilian officer P5 or above • Senior police official • Military engineer • Civilian engineer • Ammunition technical officer • Mission environmental officer
Introduce and list the members of the Range Safety Board:
  Senior military officer of rank Lt. Col. or above to act as chairman. • Senior civilian officer P-5, or above. • Senior police official. • Ammunition technical officer. • Contingent representative (x 2 if appropriate).
Range Siting Board considerations:
  The proposed range site, range orientation, topography, drainage and vegetation. • Weapon firing templates and range danger zones for the weapons and ammunition approved for use. • Local human and animal populations. • Possible human and animal site encroachment. • Environmental issues. • Noise and noise attenuation if required. • Other issues.

## Slide 15: Frequency of Practice / Firing Training
Force firing standards may be set by DPO/ITS/OMA/PD in consultation with member states. This includes;
  Pre-deployment
  Induction
  In-mission training
  Ongoing training to maintain firing standards and to provide remedial training
  Scenario based training to address mission-specific operational firing
Firing training shall be conducted at least once every 6 months during the tour of duty
T/PCCs shall adhere to national SOPs regarding level/standard of firing and to confirm serviceability of weapons
Military aviation units shall have their own regular training requirements, approved by national SOPs
Notes: Main idea/objective for slide:
Discuss importance of firing training
What the instructor should cover (in addition to slide content)
DPO/ITS/OMA/PD: Department of Peace Operations, Integrated Training Service / Office of Military Affairs / Procurement Department

## Slide 16: Frequency of Practice / Firing Training
Training ammunition shall be part of the operational ammuntion deployed to the mission (COE Manual, Chapter 3, Annex A)
Military and police units can use up to 10% of their overall authorised ammunition quantity for training purposes annually
This does not apply to military aviation, tank or artillery ammunition
Notes: Main idea/objective for slide:
Discuss importance of firing training

## Slide 17
Conduct of Firing Ranges
Notes: Phase 2. Development (Time allocation - 65 min)
Stage 2 (Time allocation 25 mins) – Conduct of firing ranges

## Slide 18: Conduct of Firing
Range SOPs shall be referred to ensuring all safety measures are in place prior to firing
Local police shall be informed and may be present if possible
A certificate of safe range after firing confirming that the range is safe and free from unexploded ordnance and hazardous materials shall be obtained from the responsible authority by the concerned contingent
Fired Cartridge Cases (FCC) are to be deposited with the Property Disposal Unit (PDU) in line with the Environmental Policy for UN Field Missions (2009.06).
Removal of lead shot from the range
The SATO, UNMAS, EOD unit shall render a certificate to the PDU stating that the FCCs are free from explosives and safe for disposal as metal waste
Notes: Main idea/objective for slide:
Discuss the safe practices required to conduct safe use, construction and closure of ranges.
Introduce and explain the completion of the range clear safety certificate and outline how and when this certificate is completed.

## Slide 19: Range Closure - Removal of Lead Shots
Removal of lead shot is a key action to ensure mitigation of environmental and public health hazards.
Engineering section will carry out a careful excavation of materials and soil from the range impact zone and extraction of spent lead bullets.
Once the soil is deemed remediated it can be handed back to national/local authority
Notes: Main idea/objective for slide:
Emphasise the requirement to remove all lead shots from ranges which are decommissioned prior to handing over.

## Slide 20
Conduct of Disposal Ranges
Notes: Phase 2. Development (Time allocation - 65 min)
Stage 2 (Time allocation 25 mins) – Conduct of firing ranges

## Slide 21: Demilitarisation and destruction technology and techniques
Open Burning (OB) and Open Detonation (OD) (Level 1)
Cost effective, easiest and often safest for ammunition destruction <1000 tonnes and for unsafe ammunition
Completion of an environmental impact assessment required before selecting OB or OD due to the potential for pollution
OB is usually used for destruction of propellants and pyrotechnic compositions. Small quantities of unconfined high explosive may also be subjected to OB.
If OB high explosives the danger area is calculated as per destruction by detonation.
OB is done on concrete ground or burning trays to improve efficiency
Notes: Main idea/objective for slide:
Discuss the various mechanisms used for the destruction of time expired ammunition and explosives (Burning Tanks, Open Burning & Open Detonation) and describe how these range practices are conducted safely.

## Slide 22: Demilitarisation and destruction technology and techniques
Open Burning (OB) and Open Detonation (OD) (Level 1)
OD uses serviceable explosives that act as donor charges that destroy ammunition by sympathetic detonation. The disadvantages are (participants to list the possible disadvantages on a flip chart):
  large danger areas
  weather and time dependent (daylight hours)
  labor intensive
  ammunition being ejected from the pit is possible
  environmental impact (noise, air, geology and ground pollution)
  requires intensive training for personnel to carry out the task
Larger stockpiles and challenges with logistics and the demolition area may require industrial demilitarisation
Notes: Main idea/objective for slide:
Discuss the various mechanisms used for the destruction of time expired ammunition and explosives (Burning Tanks, Open Burning & Open Detonation) and describe how these range practices are conducted safely.
participant Activity
Before revealing the list of possible disadvantages, participants to list the possible disadvantages on a flip chart

## Slide 23: Layout of Disposal Site (pg 33)
Notes: Main idea/objective for slide:
Discuss layout of disposal site
References/further reading
Appendix 1 to Annex D of IATG 10.10.2021

## Slide 24: Control of Disposal Activity - participant activity
Notes: Main idea/objective for slide:
participant exercise on control of disposal activity
participant Activity
participants are split into 3 groups:
Group 1 is tasked with briefing the class on “Arrival tasks” (before disposal commences)
Group 2 is tasked with briefing the class on ‘During disposal” drills including supervision and control, paying particular attention to safety
Group 3 is tasked with briefing the class on ”Misfire procedures”.
References/further reading
(reference document Annex D to IATG 10.10.2021)

## Slide 25: Demilitarisation and destruction technology and techniques
2. Industrial demilitarisation (Levels 2 and 3)
Advantages
  Mechanical disassembly using machines
  Environmentally friendly incineration / destruction
  24/7 operation possible 365 days a year
Disadvantages
  High cost
  Not a practical option in UN field missions
  Stockpile levels, cost, location and safety means that OBOD is the only pragmatic and feasible option for field missions.
Notes: Main idea/objective for slide:
Discuss the various mechanisms used for the destruction of time expired ammunition and explosives (Burning Tanks, Open Burning & Open Detonation) and describe how these range practices are conducted safely.
Industrial demil
Equipment being developed
Costs are coming down
More environmentally friendly

## Slide 26
Participant Exercise
Notes: Phase 2. Development (Time allocation - 65 min)
Stage 3 (Time allocation 20 mins) – participant Exercise

## Slide 27: Participant Exercise
1. Group discussion: Risks associated with ranges.
  Split into three groups
  Each group to list all of the risks that you think ranges pose in UN Missions
  Each group to brief the others on the risks and mitigation measures
  Discuss
2. CARANA scenario
  A new range is to be build by the mission in Sector 3, adjacent to the township of Corma to facilitate the in-mission training of the contingent using small arms up to 7.62mm calibre. This will include a pistol range.
  You are tasked by the Range Siting Board to develop a range safety report (UNMAM Annex L) including an assessment of the environmental impact of the range. The area for the range has been selected by the host government.
Notes: Main idea/objective for slide:
Introduce participant exercise to identify risks and mitigations associated with ranges, and practice completing a range safety certificate
The next slides contain a map and some participant tips for these exercises.

## Slide 28: Participant Exercise
Location of firing range
Notes: Main idea/objective for slide:
Introduce UN CARANA scenario for exercise

## Slide 29: Participant Exercise (Tips)
The Range Safety Board is responsible for:
• Providing certified assessments to the Range Siting Board on safety issues associated with any range siting and construction design and provide other technical advice in support of the Range Siting Board’s activities;
• For each operational firing range, determine safety requirements including, for example:
  ➢ Communication requirements.
  ➢ Sentry locations and encroachment control.
  ➢ Danger flag locations.
  ➢ Range movement management and restrictions.
  ➢ Other issues relevant to a specific range.
Notes: Main idea/objective for slide:
Provide tips to support participant exercise
participant Activity
In groups, list all of the risks ranges pose in UN field operations
Review another group’s list and develop mitigation measures for the risks, based on the UN Manual on Ammunition Management and associated documents
Develop a range safety report (pg 57 UN WAM) including an assessment of the environmental impact of the range.
What the instructor should cover (in addition to slide content)
When the groups have completed their groupwork, work through the answers with the class and ask questions.
The solution needs to consider the point listed here:
Permission to conduct range practice (SOP).
  ➢Communication requirements.
  ➢ Sentry locations and encroachment control.
  ➢ Danger flag locations.
  ➢ Range movement management and restrictions.
  ➢ Range clearance certificate on completion of range practice.
  ➢ Range security on completion of range practice.
  ➢ Other issues relevant to a specific range.

## Slide 30: Lesson overview
Discuss necessity, responsibility and planning for the disposal of unserviceable ammunition
Discuss the provision of Ranges, Range Siting Boards and Safety Boards
Discuss issuing a "Certificate of Disposal" for unserviceable ammunition
Examine Ammunition Destruction - Burning Tanks, Open Burning & Open Detonation
Examine the safe use, construction and closure of Ranges
Notes: Phase 3. Consolidation (Time allocation - 10 min)
Main idea/objective for slide:
Recap Key Learning Points
participant activity
Give participants opportunity to ask any questions
Key Learning Points
2.2.9.1 Discuss necessity, responsibility and planning for the disposal of Unserviceable ammunition
2.2.9.2 Discuss the provision of Ranges, range siting Boards and safety Boards
2.2.9.3 Discuss the issuing of a "Certificate of Disposal" of unserviceable Ammunition
2.2.9.4 Examine Ammunition Destruction - Burning Tanks, Open Burning & Open Detonation
2.2.9.5 Examine the safe use, construction and closure of Ranges

## Slide 31
Ammunition Management
UN policy into practice
Look Ahead: Safeguarding
Notes: Main idea/objective for slide:
Look ahead to the next lesson of the course:
  Safeguarding